## Slide 1: DIGITAL SIGNAL PROCESSING Chapter 6
EEE DSP Teaching Team
Notes: In chapter 6 we are going to learn about z transform. You may have learn about the laplace transform, s transform in analog signal.

## Slide 2: Understand the use of z-transform in signals and systems analysis.
At the end of this chapter, students should:
Define the z-transform and explain its properties.
Explain how z-transform and inverse z-transform of common signals can be obtained using the standard z-transform table.
Explain how the system function of a digital system is obtained.
Explain how the frequency response of a digital system is obtained.
Describe the stability of a digital system.
Notes: In this Chapter, it covers the following :
Definition of the z-transform and explain its properties.
how z-transform and inverse z-transform of common signals can be obtained using the standard z-transform table.
how the system function of a digital system is obtained. Through the use of z transform, a discrete-time system can be characterized by a discrete-time system function similar to continuous system function in an analog system
how the frequency response of a digital system is obtained.
How to determine the stability of a digital system.

## Slide 3: Z-transform
It is a mathematical tool to analyse discrete-time signals and systems.
Z-transform is defined as:
Notes: The z transform is a very important mathematical tool in describing and analysing digital systems.
It can be thought as an operator Z to transform a sequence to a function.
The Z transform converts a discrete-time signal, x(n) which is a sequence of real or complex numbers, into complex discrete frequency domain signal representation, capital X(n).
It can be considered as a discrete-time equivalent of the Laplace transform which is analog in nature. It is mainly used to analyze and process digital data.
Depending on what you want to do with the signal, processing in one of the two domains will have advantages. A good example is when a sinewave is corrupt by large noise signal. In time-domain, it looks a mess. In frequency-domain, the energy is spread over the entire spectrum and therefore the sinewave is not “masked” by the noise and we can use techniques in z domain to remove away the noise and signal intact.
Hence it supports the techniques for digital filter design and frequency analysis of digital systems.
The bilateral (two sided) z-transform of a discrete time signal x(n) is given by the above expression where z is the complex variable, the summation taken from n from minus infinity to plus infinity
The set of z values for which this summation converges is called region of convergence (ROC in short) for the transform. Apparently, as z-transform is a power series with infinite terms, it may not converge for all the values of z.

## Slide 4: Computing z-transform
Unit impulse function
x(n) = (n)
Notes: Given an unit impulse function and using the definition of z transform and expanding out the series, the Z transform of x(n) is 1 which is X(z)
If you think carefully, you will realize that in the previous chapter when we do Fourier transform for an impulse function, it will a horizontal straight line in the frequency domain.
Here we can see that the z transform of an unit impulse function is 1, a straight line in the z domain similar to the laplace transformation,

## Slide 5: Computing z-transform
z-transform of a finite sequence.
Example:
Calculate z transform of x(n) = {1,-3,4,2}
Notes: Here we have a discrete time signal, x(n) with values x(0)=1 for n =0, x(1) =-3 for n=1, x(2) = 4 for n=2 and x(3) = 2 for n=3
Substituting the values into the formulate, we obtain capital X(n) the z transform of the discrete time signal, x(n)

## Slide 6: Computing z-transform
Unit step function: x(n) = u(n)
Using Binomial theorem
u(0)=1
Notes: Now we turn our attention to unit step function u(n)
We expand the summation series from minus infinity to plus infinity, we can the z transformation of u(n) as 1 over 1 minus z to the power of -1 through binomial theorem.

## Slide 7: Computing z-transform
Exponential function
x(n) = anu(n)
Notes: Another example of exponential function, a to the n multiply by u(n)
In this example a is less than 1 and you can see the exponential curve declining
Similarly using the binomial theorem, we obtain the z transformation of the discrete time signal x(n)

## Slide 8: Computing z-transform
z-transform of a function is mathematically tedious
Usually, z-transform tables are used for the common functions
Notes: Using the definition of z transformation , we can work out the z transform of the discrete signals.
However, it is very tedious. Hence we use the z transform tables to help us for the common functions such as unit impulse and unit step z transformation

## Slide 9: Z-transform table
Sequence | Transform
d[n] | 1
u[n] | 
d[n - m] | z-m
anu[n] | 
nanu[n] | 
Notes: On your left is the common discrete time signal function and the right side of the table is their z transformation
Pay particular attention for delta n minus m. The z transformation z to the power of minus m

## Slide 10: Z-transform table
Sequence | Transform
Notes: If the discrete time domain involve sine and cosine terms, we can also used the z transform table where their transformation is shown on the right hand side.
Notice that the left side of the sequence involves u(n) where u(n) will only have the value of 1 when n is equal to 0 or greater than 0. These sequence are also called positive time sequence.
Hence we can see that the summation starts from 0 to infinity instead from negative infinity.

## Slide 11: Region of Convergence
The set of z values for which summation converges
If z=5
If z=0.2
Example ( causal sequence):
Notes: The region of convergence (ROC) is the set of points in the complex plane for which the Z-transform summation converges.
ROC allows us to determine the inverse z transform uniquely.
Apparently, as z-transform is a power series with infinite terms, it may not converge for all the values of z.
Now we consider the ROC of two basic types of signals : Causal and anticausal.
For the causal signal where n starts from zero, there are two cases, z =5 and z =0.2
For z =5, the series converges to a fixed value, 1.11
While z =0.2, it does not converge.

## Slide 12: Region of Convergence
Z transform
ROC
Notes: Hence we can see from the previous slide, there seems to be some region of convergent.
You will see the circle with radius 0.5, hence any regions outside the region of 0.5, the summation is a fixed value and within the circle it is non convergent, or divergent.

## Slide 13: Region of Convergence
If z=5
If z=0.2
Example ( noncausal sequence):
Notes: Now we turn to our a noncausual signal which n takes the negative value. For detail, you can refer to the textbook.
For this course, we will not cover the noncausual signal.

## Slide 14: Properties of z-transform
Two important properties of z-transform:
  Linearity property
  Z{ax(n) + by(n)} = aZ{x(n)} + bZ{y(n)}
  = aX(z) + bY(z)
  Time or Sample shift property
  If Z{x(n)} = X(z), then Z{x(n – k)} = z-kX(z)
Notes: There are two very important properties of z transform. Linearity property and time shift property
We will apply these two properties in the following examples
if you take a unit impulse delta n and delay it by k samples, then the delayed version can be represented (in the z-domain) as z minus k.

## Slide 15: Example of z-transform
Find the z-transform of:
x1(n) = {1.0, 0.5, 0.0, –1.8, –3.0}
x2(n) = 2(0.5)(n – 3)u(n – 3) + 3(n – 2)
Notes: WE are going to look at two examples for x1 and x2 and using the two properties to find out the z transform

## Slide 16: Example of z-transform
Solution:
x1(n) = {1.0, 0.5, 0.0, –1.8, –3.0}
n = 0
n = 1
n = 2
n = 3
n = 4
Notes: For x1, we expand the summation of the casual discrete time signal starting from n=0
n = 1 means delayed by one unit time sample, in z domain , z to the power of minus one
n=3 means delayed by 3 unit time samples

## Slide 17: Example of z-transform
2(0.5)nu(n)
shift of 3 samples
z-transform
To account for the shift
3z-2
x2(n) = 2(0.5)(n – 3)u(n – 3) + 3(n – 2)
Notes: Here we to be careful that the power n minus 3 is the same as the unit function n minus 3 so that we can use the property of time shift of 3

## Slide 18: Inverse z-transform
To convert a z-domain signal back to the discrete-time form
  Using z-transform table
  Partial fractions
  Long division
Notes: A discrete-time signal, x(n), is transformed to its z-domain, X(z), by z-transform. The reverse process where a z-domain signal is converted back to its discrete-time form is called the inverse z-transform.
There are 3 methods to do this
First method using the z transform table
Second method using partial fractions
Third method using long division

## Slide 19: Find the inverse Z-transform Using the Z Transform Table
Referring to the z transform table, we obtain
Notes: Here we try to convert the power of z to suit the z transform table.
In the next 2 examples, we will use partial fractions and also the z transform table

## Slide 20: Example of inverse z-transform
Find the inverse z-transform of the following expressions:
a)
b)
Notes: Think about how are you going to solve find the inverse z transform of H z
Let look at H1 for the next slide

## Slide 21: Example of inverse z-transform
Solution:
From the given expression, we do not find any entry in the z-transform table that resembles to it.
To simplify algebra, we convert the expression to contain only positive powers of z.
Notes: You will find that there is no expression in the z transform table that could have a match
The next step is convert to the power powers of z as shown in the next slide

## Slide 22: Example of inverse z-transform
To simplify the inverse z-transform later, we multiply both sides of the equation by
Notes: After we convert the numerator and denominator in the positive power of z, we need to divide both side by z to form the expression given

## Slide 23: Example of inverse z-transform
Using partial fraction decomposition:
Notes: Our next step is find the A B and C according the steps.
To find A, remove z leaving only the factor z minus 2 and z minus 4 and substituting z = 0 to get 1 over 8
To find B, remove the factor z minus 2 and leave the other two factors z and z minus 4 and substituting z=2 to get minus 7 over 4
To find C, remove the factor z minus 4 and leave the other two factors z and z minus 2 and substituting z=4 to get 13 over 8

## Slide 24: Example of inverse z-transform
Hence,
Notes: The final step is to use the z transform table to get the individual discrete time sequence.

## Slide 25: Example of inverse z-transform
Taking the inverse z-transform:
Notes: Using the z transform table, we work backward to obtain the discrete time sequence h(n)
Small cap h
You will have to be familiar with the steps explained

## Slide 26: Example of inverse z-transform
In this case, partial fraction will not work!
Notes: To find H2, if we use the above method, we will find that we can quite a complex denominator.

## Slide 27: Example of inverse z-transform
On closer examination of the z-transform table, we have
If we choose cos 0 = 0.8, then the RightHandSide of the equation would be the same as the H(z) in question.
Since cos 0 = 0.8  0 = 0.6435 rad, we have
Notes: In this case, we will have to look cosine portion of the sequence and realize that the equivalent of the z transform has z to the power of minus 1 and minus 2. Furthermore we also notice that the coefficient of the denominator 1.6 is double of the numerator 0.8
Hence we try to see if the cosine omega zero = 0.8 can fit into the right side of the z transform.
And we fortunately obtain the equivalent of the discrete time sequence , cosine 0.6435 n u n
Note that omega zero is 0.6435 radian and not degree

## Slide 28: Example of inverse z-transform
Find the inverse z transform of:
Notes: Most of the z transform involved only the quadratic equation or the z square
Here we see a more complicated equation involving z to the power of 3
This can be solved by the third method using long division

## Slide 29: Inverse z-transform
Use long division
X
Notes: It is good to start this method for both the number and denominator to have positive power. In the textbook, the author uses the negative power which is also acceptable.
By performing the normal long division and taking care of the power of z, we can work out a series of values for the number.
The series can be finite or infinite depending on the polynomial of the numerators and denominators
After getting the z transform of y z and we use the inverse z transform to get y n
This complete the 3 method of doing inverse z transform

## Slide 30: System function
System function is defined as the ratio of the output of the system to the input.
In other words, system function,
SYSTEM, h(n) or H(z)
x(n)
X(z)
y(n)
Y(z)
y(n) = h(n)*x(n)
Notes: A system or transfer function may be defined as the ratio of the output of the system to the input.
In chapter 5, the system function is defined as h n and to get the output y n, h n will convolute with x n
X n is the input or excitation
Y n is the output or response
H n is the impulse response
H z is the z transform of the impulse response of the system

## Slide 31: System function
System function describes the relationship between the output and the input of the system in the z-domain.
The system function can also be seen as the z-transform of the impulse response of the system.
Notes: System function H z describes the relationship between the output and the input of the system in the z-domain and follows similar to the analog form

## Slide 32: Z-transform of impulse response
SYSTEM
x(n)
y(n)
X(z)
Y(z)
(n)
1
h(n)
Z{ h(n) }
H(z) = Z{ h(n) }
Notes: If the input is unit impulse, the system function, Hz will become Y z as X z is 1 for z transform for unit impulse

## Slide 33: Z-transform of impulse response
If the input x(n) = d(n), then the output is the impulse response of the system. Or y(n) = h(n).
But Z{d(n)} = X(z) = 1 (see previous slide for d(n))
Hence, Impusle response of the system,
H(z)= Y(z)/X(z)= Y(z) = Z{y(n)} = Z{h(n)}
Notes: If the input is unit impulse, then H z or h n will be called as impulse response of the system
From the z domain, it is not hard to see that the z transform of delta n is one hence the H z is equal to Y z

## Slide 34: Relationship with convolution
For a system with known impulse response, we can determine its output with discrete linear convolution:
y(n) = h(n) * x(n)
From the system function equation, we have:
Y(z) = H(z)  X(z)
Hence, convolution in time domain is transformed to multiplication in z-domain.
SYSTEM
x(n)
y(n) = h(n) * x(n)
X(z)
Y(z) = H(z)  X(z)
h(n)
H(z)
Notes: For an unit impulse input, delta n, y n will become h n
Similar in z or digital domain capital y z will become capital h z

## Slide 35: Example 1: difference equation  system function
Find the system function of the digital network below.
z-1
z-1
z-1
z-1
3
4
5
8
9
x(n)
y(n)
x(n–1)
x(n–2)
y(n–1)
y(n–2)
Notes: You can see that there are two networks cascaded in series
One feedforward with terms such as x n minus 1 and x n minus 2 and the other feedback with terms such as y n minus 1 and y n minus 2

## Slide 36: Example 1: difference equation  system function
y(n)=3x(n)+4x(n-1)+5x(n-2)+8y(n-1)+9y(n-2)
Y(z) = 3X(z) + 4z-1X(z) + 5z-2X(z) + 8z-1Y(z) + 9z-2Y(z)
Y(z)[1 – 8z-1 – 9z-2] = X(z)[3 + 4z-1 + 5z-2]
This example illustrates how system function may be obtained from the difference equation.
x(n)  X(z)
x(n-1) X(z).z-1
….
y(n)  Y(z)
y(n-1) Y(z).z-1
….
Notes: To find out the z-transformed system function, we will write out the output y n and do the z transform for each of the elements
We can also use the time-shifting and linearity theorems for the z transformed X z and Y z
After that, we will group all the Y z and X z terms together to obtain H z

## Slide 37: Example 2: Evaluation of difference equation
For the digital network shown:
Find the system function.
Find the value of the 15th sample of the output, y(n), when the input
(i) x(n) = (n)
(ii)x(n) = u(n)
z-1
y(n)
x(n)
0.5
Notes: Given a digital network, we see that there is a feedback loop from y n through the one sample delay z minus 1
We want to find out the system function for case 1 when the input is a delta n or unit impulse and the second case when the input is unit step function
We will have to work out the value of the 15th sample of the output for n = 14

## Slide 38: Example 2: evaluation of difference equation
The difference equation can be easily found:
y(n) = x(n) + 0.5y(n – 1)
We can find y(n) iteratively from the difference equation but it would be tedious.
A more efficient way to compute y(n) is to use z-transform.
Notes: It is not difficult to find out the different equation using the feedback loop
And use the iterative method to work out the value of y values from n= 0 to n = 14
A more productive method is to use the z transform method

## Slide 39: Example 2: evaluation of difference equation
a)Taking z-transform
Y(z) = X(z) + 0.5z-1Y(z)
Y(z) [1 – 0.5z-1] = X(z)
b)
(i) For x(n) = (n), X(z) = 1
Therefore,
Step 2
Step 1
Step 3
Notes: Here we take the z transform of difference equation y n = x n + 0.5 y minus 1
The second step is to find the z transform system function H z
The third step substitute X z as one to obtain Y z

## Slide 40: Example 2: evaluation of difference equation
Taking inverse z-transform
h(n)=y(n) = (0.5)nu(n)
To find the 15th sample, substitute n = 14
y(n) = (0.5)14u(14) = 6.1035  10–5
Notes: Using the z transform table, we can obtain y n as 0.5 to the power of n multiply by u n
Substituting n =14, we get the fifteen sample as 6.1035 multiple by ten to the power of -5

## Slide 41: Example 2: evaluation of difference equation
(ii) For x(n) = u(n), X(z) =
Therefore,
Notes: Similarly we can out the same step except that now the input is unit step function
Using the partial fraction method we work out the coefficients of A and B

## Slide 42: Example 2: evaluation of difference equation
We have
Taking inverse z transform
Notes: After getting Y z and using the z transform table, we can obtain the sequence y n
And then work out the fifteen coefficient y 14 as almost 2

## Slide 43: Example 3 system function  impulse response
Find the impulse response of a system given as:
We know that the system function is equal to the z-transform of the impulse response.
Hence, h(n) = Z-1{H(z)}
Notes: More practice for the above H z

## Slide 44: Example 3 system function  impulse response
Inverse z of given H(z) easily found in z-transform table,
Impulse response, h(n) = cos(0.6435n)u(n)
Notes: Here H z can be inverse transformed to h n using the z transform table to obtain h n
We can see that h n as a discrete cosine function
Note that omega not is 0.6435 radian

## Slide 45: Example 3 system function  impulse response
Find the difference equation of a system given as:
We have
Y(z)[1 –1.6z-1 + z-2] = X(z)[1 – 0.8z-1]
Rearranging the terms
Y(z) = X(z) – 0.8z-1X(z) + 1.6z-1Y(z) – z-2Y(z)
Taking inverse z-transform
y(n) = x(n) – 0.8x(n – 1) + 1.6y(n – 1) – y(n – 2)
Notes: To obtain the difference equation, y n we need to cross multiple to get Y z and X z and arrange y n as the object
Here Y n is equal to x n minus 0.8 x n minus 1 plus 1.6 y n minus 1 and – y n minus 2
Through observation of the difference equation, you will notice that there are both feedforward portion involving x n minus 1 and feedback loop y n minus 1 and y n minus 2

## Slide 46: Example 4:Simplification of difference equation
Find the difference equation of the following digital network.
z-1
y(n)
x(n)
–1
–2
2
t(n)
t(n – 1)
Input node
Output node
Notes: The above digital network looks complex.
We can simplify by adding another term t n in between the input and output nodes.

## Slide 47
At the output node
y(n) = 2t(n) – 2t(n – 1) ….(1)
At the input node
t(n) = x(n) – t(n – 1) …(2)
Taking z-transform of (1) , we have
…(3)
Taking z-transform of (2), we have
…(4)
Notes: At both the input and output nodes, we can write out their difference equation quite readily
By taking the z transform of both equations, we obtained the z transformed equation for both nodes’ equations

## Slide 48: Example 4:Simplification of difference equation
Combining (3) and (4),
Taking inverse z-transform,
y(n) = 2x(n) – 2x(n – 1) – y(n – 1)
Notes: Since H z is Y z over X z, we obtain the system equation.
By taking the inverse z transform, we get 2 x n – 2 x n minus 1 – y n minus 1
This is to be expected for y n minus 1 as there is a feedback to the input nodes by t n minus 1
This completes the single system transform function. What happen when two systems are cascaded or connected in series and parallel like resistors circuit?

## Slide 49: Combination of System Functions
Cascaded systems: (a) Series System
(b) Parallel System
Notes: In the above, we see two cascaded systems, connected in series in part a and connected in parallel in part b
For series connection,
To find the overall or total system function, you will just need to multiply all the individual H z
In time domain, it is done through convolution
To find the overall or total system function for parallel cascaded system, you will need to add them up. We will show an example how this is being done.

## Slide 50: Example of cascading systems
Given two systems, H1(z) = 1 + z-1
and H2(z) = 1 +2 z-1
Find the series and parallel system functions for the two systems.
Series: Hs(z) =H1(z) x H2(z) = (1+ z-1)(1+ 2z-1)
= 1 +3z-1+2z-1
Parallel: Hp(z)= H1(z) + H2(z)= 1+ z-1+1+ 2z-1
= 2+ 3z-1
Notes: Above are two systems functions, H1 and H2
For series connection, we need to multiply both
For parallel connection, H1 and H2 are just added

## Slide 51: Example 5: Cascaded systems
Find the overall system function of the following digital network.
Notes: Here we can see two subsystems, h1(n) and h2(n) connected in series or cascaded in series.
Two of them are feedback systems with y n minus 2 and 0.5
It has a single delay unit delay

## Slide 52
Solution:
H1(z)
H2(z)
X(z)
Y(z)
Notes: There are two way that we can go about doing it.
The first method is a little more complex where there is a intermediate t n
T n is the output of h1 system and input of h2 system
First write out the difference equation for h1 and h2 then multiply to get cancel T z to H s the cascaded series system.
Another way we you can get work out the z transform of each system separately H 1 and H 2 z and multiply them.

## Slide 53: What is frequency response?
When a pure sinusoid of frequency, f0, is applied to a LTI system, its output will also be a sinusoid at the same frequency.
Notes: The input is a sinusoidal input with V1 peak to peak with frequency f0
The output will have no frequency change except amplitude or magnitude change

## Slide 54: What is frequency response?
HOWEVER, the magnitude
or phase
or both magnitude and phase
of the output signal may be different from the input.
Notes: Now we turn out attention to Frequency response of a system.
Rather it should be term as frequency response analysis
Frequency response analysis is the technique whereby a sinusoidal test signal is used to measure points on the frequency response of a system function
The magnitude and phase of the output y are in fact related to the system or transfer function h at the frequency) of the input sinusoid.
By examining the magnitude and phase changes at the output with respect to the input, we can deduce the characteristic of the system.
In our earlier studies, we have come across system that behave like a low pass filter, high pass filter or even bandstop filter

## Slide 55: What is frequency response analysis?
For different frequencies, the variation at the magnitude and phase of the output signal will also be different.
System
Notes: Hence the input is varied for different frequencies and observing the output changes for both the magnitude and phase
Therefore, it is important to know the magnitude and phase behaviour of the system at each frequency.
This phenomenon is commonly referred as frequency response of systems.

## Slide 56: What is frequency response?
Frequency response of a digital system can be observed experimentally in a lab setup.
Simply, apply sine waves of different frequency but same amplitude and measure the amplitude and phase deviation at the output signal.
Notes: In a typical lab setup for hardware measurement of the frequency response of a system.
The input is generally carried out using a signal generator where a fixed magnitude of a signal with a set of different frequencies are injected in the digital system.
The output of the digital system is them measured using an oscilloscope which will be able to measure both the magnitude and phase change.

## Slide 57: What is frequency response?
We can plot the magnitude and phase characteristic of the system empirically.
For instance, by observing the above charts, we can conclude that the system under test behaves like a low pass filter.
Notes: Here is an example of the output response of the system.
For the magnitude, you can see that frequency ZERO, the amplitude is 2 as frequency is increased, the magnitude drops
For the phase, as frequency increases, the phase change is not linear.

## Slide 58: What is frequency response?
Apparently, experimental method is
tedious and requires a hardware setup.
However, if we know the system function,
or difference equation of a digital system
we can do the same observation
ANALYTICALLY.
Notes: We can carry out the frequency response analysis using the experimental or the analytical method.
For the experimental method, we will employ some hardware equipment such as signal generator, oscilloscopes and some cables to connect up the system
For analytical method, we can use paper and pen to calculate or using some software simulation tools such as Matlab to assist us in finding out the frequency response of the system

## Slide 59: What is frequency response?
In order to do this analysis, we will first discuss how we can transform discrete time signals and systems into frequency domain.
Time
Frequency
Notes: We have learned the discrete time representation of the signal, x n in the time domain
We have also learned the z transformation of the discrete time signal into the frequency representation
Now we will discuss how these two are connected.

## Slide 60: Discrete-time signals and systems in frequency domain
We know that the frequency spectrum of analog signals can easily be found by Fourier transform:
F(w) =F { x(t) } =
If x(t) is casual (that is it exist t=0 onwards) and sampled at a sampling frequency of fs, than its spectrum can be derived as:
F { x(n) } =
t=nTs
t=n/fs
Sampling interval, Ts = 1/ fs
Notes: Fourier transform is used to transform the analog time signal x t into the F omega
We call that continuous time Fourier transform CTFT because the input signal is continuous signal x t
We are concerned for casual signal where t is greater than 0
If the signal x t is sampled at a frequency f s to yield a number sequence x n
The continuous time t is replaced by discrete value of t called n T s where T s is the sampling interval and f s is the sampling frequency
T s is 1 over f s
The input signal is now discrete and we perform the Fourier transform we call that discrete time Fourier transform DTFT
There is a close relationship between Z transform and Fourier transform. If we replace the complex variable z by e –jω, then z transform is reduced to Fourier transform.

## Slide 61: Discrete-time signals and systems in frequency domain
This relationship is
Hence, if you have a signal in z-domain, its spectrum can simply be found by substituting z with ej.
Similarly, if you have a system function in z-domain, its frequency response can be found by substituting z with ej.
Notes: There is a close relationship between Z transform and Fourier transform. If we replace the complex variable z by e to the power of j omega, then z transform is reduced to Fourier transform.

## Slide 62: Discrete-time signals and systems in frequency domain
Let
Hence, we have X(w) = F { x(n) } =
Again from the definition of z transform, we know :
From the above, we can deduce that there is a direct relationship between z transform and Fourier transform.
Remember from the earlier chapter that this is also the definition of normalized angular frequency!
Notes: Normalized Frequency
In the analog world, a signal frequency f is measured in hertz or cycles per second. But the digital system often uses a digital frequency, which is the ratio between the analog frequency and the sampling frequency and we termed it as normalized angular frequency omega.
The digital frequency is known as the normalized frequency and is measured in cycles per sample.
The normalized frequency ranges from 0.0 to 1.0, which corresponds to a real frequency range of 0 to the sampling frequency fs.
So a normalised frequency of 1 represents your sampling frequency or angular frequency of 2 pi and 0.5 represents the Nyquist frequency.
Hence we have the X omega the fourier transform of sequence x(n) and X z Z transform of sequence x n

## Slide 63: Different frequency terms
Term | Symbol | Unit | Relationship to f | Remarks
Absolute frequency | f | Hz | – | Used mostly in analog system
Normalised angular frequency |  | rad |  | Used in discrete-time systems only
Here is a list of frequency terms used in engineering:
Notes: Note that tthe normalized angular frequency with sampling frequency, fs, normalized to unity. The unit for normalized angular frequency is radians. We always use normalized angular frequency, omega in our frequency analysis of discrete-time systems or signals.

## Slide 64: Example 6 – frequency response
Find the frequency response of a system whose system function is given by:
Solution:
To find frequency response, we substitute z  ej:
Notes: The z transform system function H z is given 1 over 1 minus 0.5 z to the power of -1
Substitute z by e to the power of j omega
We obtain fourier transform of h n

## Slide 65: Example 6 – frequency response
Using Euler’s formula (that is e±jw = cos w ± j sin w),
we have
The magnitude (or gain) and phase plot can be found by evaluating |H(ej)| and H(ej) respectively.
Notes: Use Euler’s formula, we are able to obtain the real term and the imaginary term j
The real term for the denominator is a, 1 minus 0.5 cosine omega and the imaginary term b = 0.5 sine omega

## Slide 66: Example 6 – frequency response
We can reorganise this equation by multiplying numerator and denominator with the complex conjugate.
Real
Imaginary
Now, we can derive equations for the system’ gain and phase characteristics as follows:
Notes: We can reorganise this equation by multiplying numerator and denominator with the complex conjugate
And we are able to obtain both the magnitude, system’s gain and the system’ phase expression.

## Slide 67
Final step would be the plotting of gain and phase characteristics.
To do that we need to give a range of values to w from 0 to 2 p and calculate the corresponding gain and phase (in radian or degrees):
w 0, 0.25p, 0.5p, 0.75p, p , . . . . . . .
|H(ejw)| 2.0000 1.3572 0.8944 0.7148, 0.6667, . . . . . .
<H(ejw) 0.0000 -28.6751 -26.5651 -14.6388 0.0000, . . . . . .
Notes: Substituting omega from 0 0.25 omega 0.5 omega etc we obtain the values of the system’s magnitude and phase for the different omegas

## Slide 68: Example 6 – frequency response
Result in graphical form:
Notes: We observe that it has a low pass filter characteristic from omega from 0 to pi radian

## Slide 69: Example 7 – Frequency Response
For the digital network shown below answer the followings:
What is the impulse response of the system? (h(n)=?)
What kind of filtering function does the system show?
What is the gain of the system at 2 kHz if the sampling frequency used is 8 kHz?
z-1
x(n)
y(n)
0.5
-0.5
Notes: The digital network describes a digital filter.
Let us use those technique that we have learnt to analyse this digital network

## Slide 70: Example 7 – Frequency Response
Solution:
a)
From the network the difference equation is derived as:
y(n) = 0.5x(n) – 0.5x(n – 1)
By taking the z-transform, we have
Y(z) = 0.5X(z) – 0.5z–1X(z)
Notes: First step, write out the difference equation
Second step, take the z transform
Third step, find the z transform of the system, H z as Y z over X z
Four step, find the inverse z transform to obtain h n

## Slide 71: Example 7 – Frequency Response
b) To find frequency response :
Magnitude response:
Phase response:
Notes: Replace z by e exponent j omega to obtain the Fourier transform and arrange the real and imaginary terms
To find the magnitude H we need to find the square root of the square of the real and imaginary terms
And phase arc tangent of y over x

## Slide 72: Example 7 – Frequency Response
From the plot, it is obvious that the system is a high pass filter.
w = 0, 0.25p, 0.5p, 0.75p, p , . . . . . . .
|H(ejw)|=0.000, 0.3827, 0.7071, 0.9239, 1.000, . . . . . . .
<H(ejw) = 0.000, 67.500, 45.000, 22.500 , 0.000, . . . . . .
Notes: By working out the values for the individual magnitude, we can see that the graph shows a high pass filter characteristic
You will have noticed that the previous example with the reciprocal shows a low pass filter

## Slide 73: Example 7 – Frequency Response
c) 2 kHz in normalized angular frequency:
and gain at w=0.5p
Hence, the gain of the filter at 2 kHz is 0.7071 (–3dB).
Notes: To calculate the gain at a specific frequency, you will have to calculate the value of the normalized angular frequency and substitute into H omega
For half the sampling frequency, it is 0.7071

## Slide 74: Important points to note
we can deduce that w=2p indicates f=fs and at w=p indicates f=fs/2
Frequency axis is normalised.
Remember the definition of normalized angular frequency :
For example, if the sampling frequency of the system is 10 kHz then
w=2p indicates 10Khz and w=p indicates 5 kHz in absolute frequency terms
Notes: Important points to note is that is the sampling frequency is 10 kHz, a 5kHz will be half the sampling frequency and it will be indicated as normalized angular frequency pi

## Slide 75: Important points to note
Magnitude plot is an even function (that is symmetric) while the phase plot is an odd function.
Notes: Notice that the magnitude spectrum is symmetrical along the axis pi which means it is an even function similar to cosine function

## Slide 76: Important points to note
Basic spectrum replicates itself every 2 radians.
Notes: The spectrum also duplicates every 2 pi radians

## Slide 77: Important points to note
4) What kind of filter does the spectrum show? Low-pass? High-pass? Band-pass? Band-stop?
To answer this, we look at 0 to p range of the magnitude plot
Why 0 to p ?
Remember p indicates half the sampling frequency! That is 0-p range is the proper working range of any digital system without aliasing distortion!
Notes: To find the characteristic of the filter, we observe the shape from 0 to pi radian range.

## Slide 78: Stability of digital systems
A stable system has a bounded output response when subjected to a bounded input.
One way to determine the stability of a system is by observing its impulse response.
For a system to be stable,
Notes: Next we turn our attention to when the system h n is stable or not.
One way is to observe when the magnitude of the sequence h n decreases when n increase. If it does, the system is stable

## Slide 79: Stability of digital systems
System
0
2
4
0
1
2
Impulse input
0
2
4
0
1
2
Case A-stable
0
2
4
-1
0
1
Case B-marginally stable
0
2
4
0
5
Case C-unstable
Notes: A simple diagram to illustrate the concept of system stability
For case A, h n values decrease as n increase hence it is stable
For case B, h n oscillates between 2 values hence the system is marginally stable as it neither increases or decreases
For case C, h n values increase hence the digital system is unstable

## Slide 80: Example 8- determining stability
Consider the digital network below. Is it stable?
z-1
2
x(n)
y(n)
y(n–1)
Notes: Let look at the digital system given
It is a feedback system
Is it stable?

## Slide 81
Solution:
Difference equation of the system:
y(n) = x(n) + 2y(n – 1)
Taking z-transform and finding the system function:
Y(z) = X(z) + 2z–1Y(z)
Impulse response:
h(n) = (2)nu(n)
Notes: First step, write out the difference equation
Second step, find the z transform
Third step find the z transform of the digital system H z
Fourth step use the inverse z transform table to work out h n

## Slide 82: Example 8- determining stability
Output of the system grows exponentially, hence unstable system.
1
2
4
Notes: Substituting the value n = 0 we obtain h 0 = 2 to the power of zero multiple by u 0 which gives us 1
N =1 we obtain h 1= 2 to the power of 1 multiple by u 1 which gives us 2
N =2 we obtain h 1= 2 to the power of 2 multiple by u 2 which gives us 4
Hence you can see that the magnitude continue by a factor of 2 and the system is termed unstable

## Slide 83: Example 9 – system stability
Is the following system stable?
z-1
–1
x(n)
y(n)
y(n–1)
Notes: How about this system?
Is it stable?

## Slide 84
Solution:
Difference equation: y(n) = x(n) – y(n – 1)
System function:
Taking the inverse z-transform of H(z)
yields: h(n) = (–1)nu(n)
Notes: First step write out the difference equation
Second step find the z transform
Third step find the inverse z transform of H z which is h n using the z transform table
Notice that the value of h n oscillates between 1 and -1 or rather have values of 1 and -1 alternatively
It is neither increasing or decreasing hence the digital system is marginally stable

## Slide 85: Stability of digital systems
We can also observe system stability in Z domain by referring to pole-zero diagram.
For a stable system poles and zeros must be within unit circle
1
1
real
img
Stable zone
Notes: The second method to check whether the system is stable marginally stable or unstable is to use the pole zero diagram in the z domain

## Slide 86: Example 10 – system stability
Plot the pole-zero diagram of is the following system, is it stable?
Notes: Given the above H z we multiply both the numerator and denominator by z square to convert to all positive power of z
Then we find the roots for the numerator and denominator

## Slide 87
Solution
Zeros of the system(numerator):
Poles of the system(denominator):
Stable!
Notes: We obtain z to the power of 2 over z to the power of 2 minus 1 point 6 z plus 0 point 8
If we plot the points we have two zeroes at z = 1 and -1
We are particularly concerned about the two poles ie z1 0.8 plus j 0.4 and z2 0.8 minus j 0.4
Both poles fall with the unity circle of radius 1 hence the digital system is stable
If the pole is on the unity circle, the digital system is marginal stable
We avoided computing the inverse z transform H into h n

## Slide 88: Summary
This session you have learned tools for analysing digital systems.
Z-transform and frequency response analysis are primary tools for this purpose.
Frequency response analysis shows the behaviour of system for different frequencies.
Learn how to check whether the digital system through h(n) and the pole zero diagram
Notes: We can conclude this chapter to use some of the tools to analyse the digital systems
Z transform is a useful technique especially in frequency response analysis
Frequency response analysis is able to tell us the characteristics of the system for different frequencies.
By observing the magnitude of h n increasing and decreasing and also whether the values of the poles from the denominator of the H z, we can deduce whether the system is stable, unstable or marginal stable.