## Slide 1: DIGITAL SIGNAL PROCESSING Chapter 7
EEE DSP Teaching Team
Notes: Digital Signal Processing Chapter 7
In chapter 7, we are going to learn a very important topic Discrete Fourier Transform
As the name implied it has to do with discretizing the analog Fourier Transform

## Slide 2: Understand how the discrete Fourier transform (DFT) of a signal may be obtained.
At the end of this chapter, students should:
Define the DFT of a finite sequence.
Compare and contrast DFT and Fast Fourier transform.
Notes: In previous chapter, chapter 6 we learn about the fourier transform of an x n sequence and obtained Discrete time fourier transform, DTFT
The input is x n and the output is X omega
In short, discrete time fourier transform (DTFT) I simply Fourier transform of any arbitrary discrete time sequence x n is presented by the complex exponential sequence e to the power of minus j omega n where omega is the real frequency variable
From that we obtain the continuous frequency domain to deduce whether the digital system is a low pass, high pass or bandpass filter in the continuous frequency domain
Here we will look into the discrete frequency instead of continuous frequency
We will learn how to define the discrete fourier transform, DFT of a finite sequence x n
In short, Discrete Fourier Transform is simply the Fourier Transform when it is applied to discrete signal x n rather than a continuous signal x t
Discrete Fourier Transform (DFT) is a practical version of the DTFT, the discrete version of the Fourier Transform (FT) that transforms a signal (or discrete sequence) from the time domain representation to its representation in the frequency domain. The DFT becomes equal to the DTFT as the length of the sample becomes infinite and the DTFT converges to the continuous Fourier transform in the limit of the sampling frequency going to infinity.
Discrete Fourier transform DFT find applications in linear filtering, correlation analysis and spectrum analysis
Whereas, Fast Fourier Transform (FFT) is any efficient algorithm or faster version for calculating the DFT.

## Slide 3: Discrete Fourier Transform
Discrete Fourier Transform (DFT) is a mathematical tool to obtain a discrete spectrum from a discrete-time signal.
The input is x(n) sequence and the output is a discrete value of frequencies.
Notes: Discrete Fourier transform (DFT) converts a finite sequence of equally-spaced samples of x n into a same-length sequence of equally-spaced samples of the discrete-time Fourier transform (DTFT), which is mentioned in chapter 6
Note that the input is x n sequence and the output is X k discrete value of frequencies which is related to the sampling frequency f s
This will be cover in greater detail

## Slide 4: Effect of “sampling” the spectrum
Consider the following example:
x(n) = {1, 1, 1}
Its spectrum can simply be calculated using z transform:
From previous chapter, we know that
Notes: Given a discrete time sequence x n 1 1 1
We do a z transform and obtain X z
By substituting z by e to the power of j omega, we obtain the continuous fourier transform of the discrete time sequence X

## Slide 5: Effect of “sampling” the spectrum
For , we can plot the magnitude and phase spectrum as usual.
Fourier
transform
Discrete Time Signal
Spectrum in frequency domain
Notes: You will notice on the right hand side of the slide the magnitude is continuous from 0 to 2 pi where 2 pi is the sampling frequency equivalent

## Slide 6: Effect of “sampling” the spectrum
In DFT, we simply “sample” the spectrum.
We take N frequency samples between 0    2.
Hence, the spectrum X(ej) is sampled to produce:
For example, if we have 8 samples between 0 £ w £ 2p, the frequency interval will be:
This interval is called the frequency resolution.
Notes: If we take N frequency samples similar to the sampling process where we take the sampling interval, T
We basically divide the equivalent sampling frequency fs or normalized angular frequency 2 omega in discrete values
Frequency resolution Delta omega = 2 pi over N where N is the discrete frequency samples
The higher the value of N the frequency resolution will be smaller

## Slide 7: Effect of “sampling” the spectrum
Samples at frequency domain for N = 8
Frequency resolution
Frequency axis is normalized, therefore only the frequency index will be used.
Notes: For example if N = 8 then each value is fs over 8 resolution
In that sense we are sampling the frequency domain

## Slide 8: Effect of “sampling” the spectrum
Assume that N = 8 and sampling frequency is 8kHz.
Notes: If the sampling frequency is 8 kHz and N = 8 then we have 8 samples from 0 kilo hertz to 8 kilo hertz
The discrete frequency values are 0 kilo hertz 1 kilo hertz 2 kilo hertz to 7 kilo hertz and the cycle repeats

## Slide 9: Effect of “sampling” the spectrum
Fourier
transform
Discrete Frequency Values in terms of k
Frequency Domain
Discrete Time Values in term of n
Time Domain
Notes: Hence we can form the discrete frequency spectrum for the frequency domain
A big tell a thousand words and both discrete representation in time and frequency domain are shown
The frequency spectrum is now discretized and represented by the dot on the right side of the slide

## Slide 10: Effect of “sampling” the spectrum
Example: Fourier transform of a continuous time signal
Notes: The diagram shows the Fourier transform of x t in the time domain to frequency domain

## Slide 11: Effect of the time sampling
Fourier transform of the discrete time signal
Notes: When we do the sampling of the signal in the earlier chapter, the sampled frequency representation will be duplicated for different frequency sampling frequency 1 f s 2 fs 3 fs
Here it will be represented by 2 pi 4 pi and so for

## Slide 12: Effect of “frequency sampling” the spectrum
Continuous spectrum converted to discrete
Notes: We can perform the “discrete frequency” spectrum as shown for X k

## Slide 13: Effect of “frequency sampling” on the spectrum
Discrete Fourier transform
Notes: By taking a finite sequence of x n this is shown in the previous slides we obtain the discrete fourier transform from n = 0 to N where each interval is the frequency resolution
If the frequency resolution is very small than the discrete fourier values approach continuous values

## Slide 14: Effect of “sampling” the spectrum
The inverse Fourier transform of will not get back the time sequence x(n); but instead a periodic version of it.
In another words, is the sequence x(n) repeating itself every N samples.
In practice, we are only interested in one period of or
Notes: This is quite similar to what we have learned from sampling theory where the sampling of a signal in the time domain creates spectral images in the frequency domain.
Here, we see that the sampling of a signal in the frequency domain creates waveform images in the time domain.

## Slide 15: Fourier Transform
Fourier transform
time (t)-> continuous frequency (w)->continuous
Fourier transform of discrete time signal
time (n)-> discrete frequency (w)->continuous
Discrete Fourier transform for discrete time & frequency
time (n)-> discrete frequency (k)->discrete
Discrete Fourier Transform
Notes: We have the 3 forms of Fourier transform
The first one, the fourier transform of a continuous time signal to a continuous frequency signal
The second one, Discrete time fourier transform of a discrete time signal to a continuous frequency signal
The third one, Discrete Fourier transform of a discrete time signal of a finite sequence to a discrete frequency signal

## Slide 16: Definition of Discrete Fourier transform
Discrete Fourier transform (DFT):
Inverse Discrete Fourier transform (IDFT):
Notes: These are the mathematical representation of both the Discrete Fourier Transform and Inverse Discrete Fourier Transform which we will use later
You need to do some practice to be familiar with the equations

## Slide 17: Conventions used
Note the conventions used here:
x : small letters
 denotes time domain signals
X : Capital letters
 denotes frequency domain signals
n  time index
k  frequency index
Notes: Some important conventions to take note of
Small x denotes time domain signals
Capital x denotes frequency domain signals
t is the time index and k is the frequency index
In tutorials or exams, the students will have to follow this common conventions

## Slide 18: Example 2
Determine the 4-point DFT of the sequence
Solution:
Hence,
ej
1
j
-j
-1
Notes: We will look into a discrete time signal x n = 1 1 1 1
Small x 0 = 1
Small x 1 = 1
Small x 2 = 1
Small x 3 = 1
Small x 4 = 0 and so for
Taking 4-point discrete fourier transform of the sequence
Capital X k equations can be easily written for k = 1 2 3 and 4

## Slide 19
Therefore, X(k)={4,0,0,0}
k=0
k=1
k=2
k=3
Example 2
Notes: By substituting k = 0 1 2 and 3
The spectral components Capital X k values can be calculated that correspond to the spectrum of a period sequence of period 4
The result is not surprising
X 0 represents the dc component and the rest of the ac components ZEROs
It is easily calculated by adding all the values of the individual values of x n
If you look at all the discrete time signal, there is no variation that is they have the same value a constant

## Slide 20
Graphical Representation
Discrete time signal
Discrete frequency magnitude
spectrum of the signal
Discrete frequency phase
spectrum of the signal
Notes: Since there is no imaginary number in the X components there is no phase angle hence the phase values are all zeros

## Slide 21: Example-2
Determine the 8-point DFT of the sequence:
Solution:
Example 3
Notes: The second example, we use N =8
And we follow the same procedure as the first example to get the discrete time fourier transform representation of capital x k representation

## Slide 22: Example-2
Notes: Substituting the k index from 0 to 7 we obtain the values for the individual magnitude spectrum capital X k
X 0 = 1 + 1 +1 +1 + 0 + 0 + 0+ 0 = 4
Note that there is imaginary components for some of the values and they can express as magnitude plus its phase values
You will also observe that the capital X 0 is equal to capital X 4 and correspondingly capital X 1 with X 5 but in conjugate form where the magnitude is the same but the phase angle has changed 180 degrees

## Slide 23: Example-2
In graphical form
Signal
Phase plot
Magnitude plot
Notes: As shown graphically we can have a clear picture, where the folding or mirror corresponding values is at k = 4 for the magnitude plot where k = 1 equals to k =5, k = 2 with k =6 etc
And for the phase plot there is a change of 180 degrees for their corresponding value, ie k=1 with k=5

## Slide 24
Some important points to note (for N = 8):
  X(0) represents the DC component.
  X(1) represents the lowest AC component.
  X(4) or X(N/2) represents the highest frequency component.
  X(5)  X(7) are the mirror images of X(1)  X(3)
Notes: Some important points to take note of
K=0 means the frequency is zero so capital X 0 is the dc component
For the individual space out frequency components, X 1 will represent the lowest AC component and the actual value of frequency can be known if we have the sampling frequency
X 5 and X 7 are mirror images and X 2 and X 6 correspondingly

## Slide 25: Example 3
i) Determine the 4-point DFT of the sequence
(that is X(k)=?)
ii) Prove that 4 point inverse DFT of X(k) is equal to signal x(n)
Example 4
Notes: Can you guess the value of X 0?
What are the values of x n
1 1 0 0
Yes the value of X 0 is 1 plus 1 plus 0 plus 0 equals 2
For this example, besides doing fourier transform we are going to do the inverse fourier transform (discrete time to discrete frequency) to get back the discrete time signal (discrete frequency to discrete time)

## Slide 26
Solution:
i)
Notes: X 0 is easy to calculate just by adding all the amplitudes of the discrete time signal
To find the remaining X k values, we will have to use the definition of Discrete Fourier Transform and obtain the general expression for X k
By substituting the values of k from 0 1 2 and 3 we will obtain the individual values of the amplitude of the discrete frequency components.
Remember to relate what you learn about fourier transform to discrete fourier transform

## Slide 27: Example 3
ii) Now, take the solution of X(k) as input and apply inverse DFT to find x(n):
Notes: To find the inverse Discrete Fourier Transform, we use the inverse Discrete Fourier Transform to find x n expression
To find the individual x n value we need to replace n with 0, 1, 2 and 3

## Slide 28: Example 3
Notes: X 0 is 1 x 1 is 1 and x 2 is 0 x 3 is 0
e to the power of j pi 0 is 1
e to the power of j pi over 2 which is 90 degrees is j
e to the power of j pi which is 180 degrees is -1
e to the power of j p 3 pi over 2 is –j
Using the above result we can find the value of x 0 x 1 x 2 and x 3
It also means that the students have to revisit how to handle complex numbers

## Slide 29: Fast Fourier transform
From the definition of DFT
we can see that to compute each value of X(k) many complex multiplications and complex additions are required.
Notes: Discrete Fourier Transform is a complex computation involves the calculation of x k which involve complex numbers
And additions form n = 0 to capital N minus 1
Because of this huge number of operations as N get larger the computation time is more.
FFT Fast Fourier Transform is an algorithm that efficiently computes the discrete Fourier Fourier Transform

## Slide 30: Fast Fourier transform
To compute all the values of X(k),
number of complex multiplications = N2
number of complex additions = N(N – 1)
In total ~=2 N2
This requires long processing time if N is a big number.
Notes: To compute number of complex multiplications is N x N
And the number of complex additions = N x (N – 1)
Given N = 8, the total number of steps in computing will be 8 x 8 plus 8 x 7 = 64 plus 56 = 120
So as the N increase, it will have longer processing time to do the computation

## Slide 31: Fast Fourier transform
James W. Cooley and John W. Tukey discovered a fast algorithm to compute DFT in 1965 and it is still used today.
This algorithm is known as Fast Fourier transform (FFT).
The main idea behind FFT is to reduce the number of complex operations.
Total number of operations when using FFT becomes:
Notes: James W. Cooley and John W. Tukey uses a fast algorithm to compute DFT in 1965
This helps to reduce the number of complex operations and the total number of operations reduces significantly as N becomes extremely large
The DFT and FFT are excellent for convolution, and useful for frequency-domain analysis of sampled analog signals.
In the last chapter we will learn another transformation called DCT, discrete cosine transform.
For image compression, we would like energy compaction; we would like a transform that reduces the signals of interest to a small number of nonzero coefficients and take advantage of such property

## Slide 32: Example 5
If each machine cycle in a CPU takes 125msec, 1024 point DFT will take:
2x(1024)2 x125msec=252.144 sec
on the other hand using FFT algorithm:
(3x1024/2)xlog2(1024)x125msec=1.92 sec!!!!!
Notes: To see how much time reduction to compare using DFT and FFT, we use N = 1024
Using DFT it takes about 252 seconds and about 2 seconds if one will to use FFT.
This is a huge saving of computation time

## Slide 33: Summary
This lecture covered DFT.
DFT produce spectrum of the signal in discrete manner.
In practice, we use FFT algorithm to compute DFT.
Notes: In this chapter, we have represent a sequence in terms of a linear combination of complex exponentials using the discrete-time Fourier transform (DTFT) /
For finite-length sequences, Discrete Fourier transform, DFT representation is used.
DTFT is a continuous refunction of a continuous variable omega while DFT is a sequence that corresponds to samples of the DTFT.
Such representation is useful for digital computations and perform tasks such as digital filtering and evaluating the frequency response of a linear shift-invariant system.
We have also briefly mentioned Fast Fourier Transform, FFT a faster way in computation than Discrete Fourier Transform, in practise.