## Slide 1: DIGITAL SIGNAL PROCESSING Chapter 8
EEE DSP Teaching Team
Information Theory and Coding
Official (Open), Non-sensitive
Notes: Welcome to chapter 8, information theory and coding. There are two parts. The first part is information theory and the second part is source coding, in particular a very useful technique call Huffman coding. For Information Theory, we will define what is information and how to calculate source entropy.
The ultimate goal of any communication system is to transmit over a channel, the information originating from a source in one location, to the destination in another location as speedily and reliable as possible. A communication system will comprise of the transmitter, channel and receiver. At the transmitter side, we will have the source generator that will send information to the source encoder, channel encoder and modulator. We will concentrate on the source encoder. The purpose of the source encoder is to remove or reduce the redundancy in the source output so as to give an efficient representation of the message information given by the source by using less bits. In other words, we can treat source encoding as data compression.
Huffman coding a useful technique of source coding will be taught in this chapter.

## Slide 2: Understand the Information Theory and Coding
At the end of this chapter, students should:
Understand basic concepts of information theory.
Understand the need for source coding for efficient and reliable digital communication.
Official (Open), Non-sensitive
Notes: In Chapter 8, we will go through the basic concepts of information theory and the need for source coding for efficient and reliable digital communication.
We will try to understand what is information? Can we measure it? And to what extend we measure it? The information can be discrete symbols, one dimensional array of digital audio signals, two dimensional image signals and three dimensional video signals.

## Slide 3: 8.1 Introduction to Information Theory
Information content of a message depends on the probability of the event associated with the message.
The lower the probability of occurrence of the event, the higher is the information content of the message.
    The sun will rise from the east tomorrow: → 100% probability → Zero information content
    Singapore will have an earthquake next week: → Very low probability → Very high information content
In digital communications, information content is measured on a per symbol basis.
Official (Open), Non-sensitive

## Slide 4: 8.1 Introduction to Information Theory
Average Information content of symbols
Suppose a source emits one of M symbols, S1, S2, S3, ... SM. Let P1, P2, P3, ... PM be the probabilities of occurrence of the M symbols, respectively.
Information content, I of the symbol Si is defined as:
I(Si) = log2 ( 1/Pi ) bits where Pi is the probability of occurrence of the symbol, Si
E.g I(S3) = log2 ( 1/P3 ) bits
From the formula, symbol less likely to occur provide more information.
Official (Open), Non-sensitive

## Slide 5: Quiz
A fair die has six faces marked 1, 2,3,4,5 and 6 with the same probability 1/6 for all the faces. Find the information content associated with the single throw of the die
a) 2.59 bits
b) 1.59 bits
c) 0.59 bits
d) 0 bit
Official (Open), Non-sensitive
Notes: Answer a

## Slide 6: Quiz
A coin has 2 faces marked head, H and tail, T with the same probability 1/2 for each faces. Find the information content associated with the single throw of the coin.
a) 2 bits
b) 1 bit
c) 0.5 bit
d) 0 bit
Official (Open), Non-sensitive
Notes: Answer b

## Slide 7: 8.1 Introduction to Information Theory
The average information content of a N-symbol message is given by:
I (total)/ N = Pi log2 (1/Pi)
= ‑ Pi log2 Pi bits/symbol (6.4)
= Source entropy, H
The average rate of information going through a channel is:
Average rate of information or Information Rate = H x rs
where rs is the symbol rate.
I(total) =Total information content in the message

## Slide 8: Quiz
A source emits two symbols, a and b with probabilities Pa = 0.25 and Pb = 0.75. What is the source entropy?
a) 1 bit/symbol
b) 0.5 bit/symbol
c) 0.25 bit/symbol
d) 0.8112 bit/symbol
Official (Open), Non-sensitive
Notes: Answer d

## Slide 9: 8.1 Introduction to Information Theory
Note:loga b =
Example 8.2
A discrete source emits one of five symbols once every millisecond. The symbol probabilities are P1 = 1/2; P2 = 1/4; P3 = 1/8; P4 = 1/16; P5 = 1/16. Find the source entropy and information rate.
Solution
Symbol rate rs = 1000 symbols/sec
Entropy H = Pi log2 1/Pi where M = 5
H = 1/2 log2 2 + 1/4 log2 4 + 1/8 log2 8 + 1/16 log2 16 + 1/16 log2 16
H = 1.875 bits/symbol
Information rate = H x rs = 1 875 bits/sec

## Slide 10: Image Entropy
Gray Image
Entropy value ?

## Slide 11: 8.2 SOURCE CODING

Discrete
Information
Source
  Noise
Source
Encoder
Channel
Encoder
Electrical
Communication
Channel
Demodulator
Channel
Decoder
Source
Decoder
Destination
c
b
a
d
f
g
h
i
Modulator
Binary
Stream
Sequence
of
Symbols
Digitally
encoded
carrier
(Analog)
+
+
0, 01,11

## Slide 12: 8.2 SOURCE CODING
Source coding converts symbols into binary bits reducing any redundant information.
Purpose of source coding : reduce the bandwidth/transmission time and storage capacity.
A common source coding method: variable-length coding (instead of fixed-length coding).
  Symbols with higher probability are coded with shorter codewords thus using less bits on average.

## Slide 13: 8.2 SOURCE CODING
Properties of codes
For a code to be useful it must have the following properties:
  uniquely decodable property
  prefix-free property
A code is a mapping of symbols into codewords (binary bits)
Symbol | Code A | Code B
a | 00 | 00
b | 11 | 10
c | 111 | 110

## Slide 14: 8.2 SOURCE CODING
Symbol | Code 1 | Code 2 | Code 3 | Code 4 | Code 5 | Code 6
a | 00 | 00 | 0 | 1 | 1 | 1
b | 00 | 01 | 1 | 10 | 00 | 01
c | 11 | 10 | 11 | 100 | 01 | 11
Table 8.2 Six possible binary codes for the 3-symbol source
Various binary codes can be designed to represent the 3-symbol source:
codewords
uniquely decodable
prefix-free
Properties
Table 8.1 Three-symbol alphabet

## Slide 15: 8.2 SOURCE CODING
Uniquely Decodeable Property
Allow remap to the original symbol alphabet without ambiguity.
Code 1 is not uniquely decodable as the symbol a and b are assigned the same binary codeword.
First requirement of a useful code is that each symbol be assigned a unique binary codeword.
Codes 3 and 6 have unique binary codewords. Problem occurs when these codewords are transmitted serially.

## Slide 16: 8.2 SOURCE CODING
E.g, In code 3, try to decode the received binary pattern: 1 0 1 1 1
Answers:
1 / 0 / 1 / 1 / 1 ------ b, a, b, b, b
1 / 0 / 1 / 1 1 ------ b, a, b, c
1 / 0 / 1 1 / 1 ------ b, a, c, b
Hence code 3 is not uniquely decodable even though each symbol has a unique codeword.
Code 6 has the same problem and is also not uniquely decodable

## Slide 17: 8.2 SOURCE CODING
A solution – Codes with Prefix-Free Property
Condition for uniquely decodable code is that no codeword be the prefix of any other codeword - prefix-free codes.
Prefix-free codes have another feature – they are also instantaneously decodable or prefix code.
An instantaneously decodable code is one for which the boundary of the present codeword can be identified by the end of the present codeword rather than by the beginning of the next codeword.
Code 4 is not instantaneously decodable.
1 0
1 0
0
 c
 b ?
1 0
1
 b a
1
 a ?

## Slide 18: 8.2 SOURCE CODING
Symbol | Code 1 | Code 2 | Code 3 | Code 4 | Code 5 | Code 6
a | 00 | 00 | 0 | 1 | 1 | 1
b | 00 | 01 | 1 | 10 | 00 | 01
c | 11 | 10 | 11 | 100 | 01 | 11
Table 6.2 Six possible binary codes for the 3-symbol source
Code 5 is prefix-free : both uniquely decodeable and instantaneously decodable – best code.

## Slide 19: 6.2 SOURCE CODING
Code Length and Source Entropy
The average code length of a code is denoted by . It is computed as:
(7.5)
Source entropy, H has been defined as the average information per symbol.
Source entropy, H also represents the minimum possible average bit length achievable by a variable-length code – ideal for a source.
ni = number of bits in the codeword
P(Xi) = probability of occurrence

## Slide 20: Various codes to represent the 3-symbol source:
Symbol | Code 1 | Code 2 | Code 3 | Code 4 | Code 5 | Code 6
a | 00 | 00 | 0 | 1 | 1 | 1
b | 00 | 01 | 1 | 10 | 00 | 01
c | 11 | 10 | 11 | 100 | 01 | 11
E.g. Average bit length for code 5
Table 8.1 Three-symbol alphabet
8.2 SOURCE CODING

## Slide 21: 8.2 SOURCE CODING
Huffman Coding
Prefix-free variable-length code.
Can achieve the shortest average code length.
Source Entropy, H is the ideal average code length.
The Huffman code is generated as part of a tree forming process: - Fig. 8.3
  List the input symbols and their probabilities in decreasing order of occurrence
  Each entry corresponds to the branch of a tree.
  The 2 entries with the lowest probabilities are merged to form a new branch with their composite probability.

## Slide 22: 8.2 SOURCE CODING
a
b
c
d
e
f
0.4 0.4 0.4 0.4 0.6
0.6
0.4
0.1
0.1 0.1
0.1 0.1 0.2
0.1 0.2 0.2 0.2
0.2 0.2 0.2 0.4
0.4
0.2
1.0
0.2
Figure 8.3 Huffman coding tree for a six-symbol set
Symbols

## Slide 23: 8.2 SOURCE CODING
  After every merging, the new branch and the remaining branches are reordered to preserve the descending probability of occurrence.
  After forming the tree, each branch is labelled with a binary 1 or 0. If 1 is to be sent as often as possible, we label the branch going up with a 1 and the branch going down with a 0.
  The path from the base of the tree to the symbol contains the codeword for that symbol.

## Slide 24: 8.2 SOURCE CODING
a
b
c
d
e
f
0.4 0.4 0.4 0.4 0.6
1
0
0.6
0.4
0.1
0.1 0.1
0.1 0.1 0.2
0.1 0.2 0.2 0.2
0.2 0.2 0.2 0.4
0.4
0.2
1.0
0.2
Figure 6.3 Huffman coding tree for a six-symbol set
LSB
MSB
1
0
1
0
1
0
1
0

## Slide 25: Quiz
What is codeword for a?
a) 11
b) 00
c) 101
d) 100
Notes: Answer a

## Slide 26: Quiz
What is codeword for b?
a) 11
b) 00
c) 101
d) 100
Notes: Answer b

## Slide 27: Quiz
What is codeword for c?
a) 11
b) 00
c) 100
d) 101
Notes: Answer d

## Slide 28: Quiz
What is codeword for d?
a) 11
b) 00
c) 101
d) 100
Notes: Answer c

## Slide 29: 8.2 SOURCE CODING
Xi | P(Xi) | Code-word | ni | niP(Xi)
a | 0.4 | 11 | 2 | 0.8
b | 0.2 | 00 | 2 | 0.4
c | 0.1 | 101 | 3 | 0.3
d | 0.1 | 100 | 3 | 0.3
e | 0.1 | 011 | 3 | 0.3
f | 0.1 | 010 | 3 | 0.3
 |  |  |  | =2.4
where i = 1, 2, ..., 6
Table 8.3 below lists the resulting codewords.

## Slide 30: 8.2 SOURCE CODING
The average code length, for this alphabet is 2.4 i.e. on the average 240 bits are when transmitting 100 symbols.
Note: A fixed-length code would require a code length of 3 bits per symbol.
Compression ratio = average number of bits per symbol before compression average number of bits per symbol after compression.
For this code, compression ratio = 3.0/2.4 = 1.25
Code efficiency = (entropy  average code length) x 100%
Entropy for this code is 2.32. Hence this code achieve 2.32/2.4 or 96.4% of the possible compression ratio.

## Slide 31
END OF CHAPTER 8