## Slide 1: Mechanical Components

## Slide 2: Fasteners & Locking Devices
Secure 2 or more parts together
Screws for different materials
  Wood
  Plastic
  Machine
Difference in head & different tools are required

## Slide 3: Bearings & Sliders
Reduce friction on moving components
Rotation
  Axial
  Radial
Sliding
  Shafts
  Other components

## Slide 4: Springs
Stores energy from moving components
  Rotation
  Tension
  Compression
Comes in different shapes
  Leaf spring
  Flat coil spring

## Slide 5: Gears
Transmit motion
Change speed or torque
Types
  Spur
  Bevel
  Helical
  Worm & worm wheel
  Rack & pinion
  Sun & planet

## Slide 6: Gears – Calculating Speed/Gear Teeth
↑ rotational speed  ↓ torque
Equate gear ratio to speed and torque
Gear Ratio
Speed
(rad/s) or RPM
Torque (Nm)

## Slide 7: Gears – Calculate Speed
Gear 1 has 15 teeth & rotates at 100RPM
Gear 2 has 50 teeth
What is gear 2 speed(RPM)?
2
1

## Slide 8: Gears – Calculate Torque
Gear 1 has rotates at 100RPM & has 10Nm
Gear 2 has rotates at 250RPM
What is gear 2 torque (Nm)
Which gear is which?
?
?
1
2

## Slide 9: Gears - Characteristics
Changes direction
  2 meshing gears rotate in opposing directions
Addition of the centre gear changes the direction of output gear
  Direction of output is the same as the input gear

## Slide 10: Belts & Pulleys
Transmits motion
Used to move objects
Types
  Round belt
  Flat belt
  V-belt
  Timing belt
  Conveyer belt

## Slide 11: Belts & Pulleys – Installation
Open
Crossed
Turned
Serpentine

## Slide 12: Cams
Transmits a specific desired linear motion from rotation or linear motion
Types
  Radial cam
    Pear
    Snail
    Eccentric
  Wedge cam

## Slide 13: Cams – Followers
Types
  Slider
  Lever
Follower end types
  Knife
  Roller
  Flat

## Slide 14: Cams – Types of Motion
Snail
  Gradual increment, then a drop
Pear
  Gentle increment and decrement between constant displacements
Eccentric
  Smooth wave motion (sine/cosine)

## Slide 15: Mechanisms – Bell Cranks
Transmits motion & force
Ability to change the output motion & force
Increases mechanical advantage

## Slide 16: Mechanisms – Cranks
Ability to rotate a shaft easier

## Slide 17: Mechanisms – Linkages (1)
Toggle mechanism
  A small effort is applied but a large force is generated

## Slide 18: Mechanisms – Linkages (2)
Reverse motion
  Reverts output motions

## Slide 19: Mechanisms – Linkages (3)
Push-pull linkage
  Output link moves and has the same force as the input link

## Slide 20: Mechanisms – Linkages (4)
Rotary motion
  A linear motion is converted to rotary and vice-versa

## Slide 21: Mechanisms – Linkages (5)
Parallel motion
  A parallel motion is transmitted to maintain a level motion

## Slide 22: Mechanisms – Applications

## Slide 23: Mechanisms – Screw Threads
Bench vice
Glue stick
Conveyer
Lead screw

## Slide 24: Mechanisms – Ratchet & Pawl
Allows rotation in one direction