## Slide 1: Unit 13 Inductors
Part A: Structure & Types of Inductors

## Slide 2
What will you learn?
  Describe the basic structure and characteristics of an inductor.
  Identify various types of inductors.
  Calculate self-inductance.

## Slide 3: Introduction
Basic form: a length of wire is formed into a coil.
Store energy in its magnetic field.
  Inductance is the property of a wire coil that opposes any change in current going through the coil.
  A coil used in this way is called
    an inductor or
    a choke.

## Slide 4
A basic inductor
The Basic Inductor
Inductor is basically a coil of wire. It is also called a coil or a choke in certain applications.
L
Symbol for inductor

## Slide 5
S
N
Any induced voltage in coil?
Why?
Magnet is stationary
Constant current
Any induced voltage in coil?
Why?
THE BASIC INDUCTOR
THE BASIC INDUCTOR
The Basic Inductor

## Slide 6
S
N
Expanding magnetic field
Increasing
current
Any induced voltage in coil?
Why?
Any induced voltage in coil?
Why?
Magnet in motion
THE BASIC INDUCTOR
THE BASIC INDUCTOR
The Basic Inductor

## Slide 7
Voltage is induced in coil.
What is the polarity of the induced voltage?
Can you recall Lenz’s Law?
Induced voltage opposes increase in current.
Expanding magnetic field
Increasing
current
THE BASIC INDUCTOR
The Basic Inductor

## Slide 8
Voltage is induced in coil.
Induced voltage opposes decrease in current.
Collapsing magnetic field
Decreasing
current
This property of the coil to oppose any change in current through it is called Inductance.
THE BASIC INDUCTOR
The Basic Inductor

## Slide 9: Self-Inductance
When a current passes through a coil, a magnetic field is established.
If the current changes continuously, the magnetic field around the coil will also change continuously.
A constantly changing magnetic field can cause an induced voltage across the coil (Faraday’s law).
The induced voltage is in a direction that opposes the change in current (Lenz’s law).

## Slide 10: Self-Inductance
The property described is called self-inductance or simply as inductance L.
Self-inductance is a measure of a coil's ability to establish an induced voltage as a result of a change in its current.
The unit of inductance is henry (H).

## Slide 11: Self-Inductance
Inductance is 1 H when current changing at a rate of 1 A/s, flows into a coil and induces 1 V across the coil.

## Slide 12: Self-Inductance
Example
Determine the induced voltage across a 1 H inductor when the current is changing at the rate of 2 A per second.
Solution:

## Slide 13: Energy Stored in Inductor
An inductor stores energy in the magnetic field created by the current.
This energy can be calculated as follows:
where
energy W is in joules;
current I is in amperes; and
inductance L is in henries.

## Slide 14: Physical Characteristics of Inductors
The Amount of Inductance is physically determined by
  number of coil turns N,
  length of the core l,
  cross sectional area of the coil A, and
  permeability of core material.
Inductance in henries (H)

## Slide 15
Permeability of a material determines how easily a magnetic field can be established within the material.
The permeability of vacuum or “free space” μo is used as a reference with a value of
      4π x 10−7 Wb/At.m (weber/ampere-turn.meter).
Air is assumed to have the same permeability as “vacuum”.
All ferromagnetic core materials have higher permeability.
Permeability µ

## Slide 16
The ratio of absolute permeability to the permeability of a vacuum is called relative permeability μr .
Relative Permeability μr
For air-core inductors, μr = 1.
or

## Slide 17: Physical Characteristics of Inductors
Example
Determine the inductance of a 350-turn inductor. The radius of the cylindrical core is 0.25 cm. The length of the core is 1.5 cm. The permeability of the core material is H/m.
Solution
= 1.5 cm = 0.015 m

## Slide 18: Winding Resistance
Because a coil is made of wire, an inherent resistance called the winding resistance Rw is present.
Although this resistance occurs along the whole length of wire, it can be represented as an Rw in series with L.
Often, Rw is small and can be ignored.
Coil is then considered as an ideal inductor.
Winding Resistance of a Coil
(b) Equivalent circuit

## Slide 19: Winding Capacitance
Stray capacitance, called winding capacitance Cw, is also present in a coil.
Often, this is very small and has no significant effect.
In other cases, particularly at high frequencies, it may become quite important.
The equivalent circuit for a practical (real) inductor is given below:

## Slide 20: Types of Inductors
Inductors come in a variety of shapes and sizes.
Basically, they fall into 2 general categories:
  fixed
  variable
Both fixed and variable inductors can also be classified according to the type of core material.
3 common types are
  air core
  iron core
  ferrite core
Air core
Iron core
Ferrite core

## Slide 21: Types of Inductors
Fixed Inductor
Variable inductor

## Slide 22
Enc apsulated Torroid coil
Applications:
—Power supplies, transformers, electric motors, radios, TVs, and radars.
Variable
Types of Inductors
Toroid coil
Encapsulated

## Slide 23
Impedance Analyser for Measuring Inductance

## Slide 24
You have learned
  An inductor is made of wire coil. Its core is usually air, iron or ferromagnetic material.
  Inductance or self-inductance is the property of a coil of wire opposes any change in current going through the coil.
  The polarity of the induced voltage is in a direction that opposes the change in current.
  Winding resistance and winding capacitance, fixed and variable inductors and some applications of inductors.

## Slide 25
Coming Up Next
  Charging and Discharging Processes of Inductors