## Slide 1
Solution to Tutorial 1, Question 3
3. Using source conversion method, simplify the given circuit in Figure 4 to its equivalent current source between the terminals AB.
Ans: I = 4A (A +ve), R =2.5 W

## Slide 2
Given Circuit:
1 W
3 W
15 V
7 A
1 W
2 A
Figure 3
A
B
5 W
Solution to Tutorial 1, Question 3

## Slide 3
1 W
3 W
15 V
7 A
1 W
2 A
A
B
5 W
Solution: Convert the two current sources to voltage sources
Solution to Tutorial 1, Question 3

## Slide 4
Solution: Convert the two current sources to voltage sources
1 W
1 W
A
B
5 W
V1=7 V
3 W
15 V
V2=2 V
Solution to Tutorial 1, Question 3

## Slide 5
Solution: Combine all the voltage sources and resistances
20 V
5 W
A
B
5 W
Solution to Tutorial 1, Question 3

## Slide 6
Solution: Convert the voltage source to current source and combine the resistance
4 A
A
B
5 W
5 W
Solution to Tutorial 1, Question 3

## Slide 7
Solution: Convert the voltage source to current source and combine the resistance
4 A
A
B
2.5 W
Solution to Tutorial 1, Question 3