## Slide 1: Solution to Tutorial 5, Question 5
5. A balanced star load, having a power factor of 0.8 lagging, is connected to a 400 V, 3-phase, 3-wire balanced star supply. The total power consumption of the load is 3 kW. Find the impedances of the load in polar form.
Ans: Z = 42.67 Ð36.87o W

## Slide 2: Solution to Tutorial 5, Question 5
Given: VL= 400V, PT = 3kW, cos F = 0.8 (lag)

## Slide 3: Solution to Tutorial 5, Question 5
F = cos-1 0.8 = 36.870
cos F = 0.8 lag

## Slide 4: Solution to Tutorial 5, Question 5
Lagging power factor implies inductive load
If power factor is leading, load will be capacitive
Positive impedance angle for inductive load
Negative impedance angle for capacitive load