## Slide 1
Instructions for using the PowerPoint slides:
To view the animated steps - click anywhere on the slide.
To skip the animated steps to go to previous or next page - click the arrowheads at the bottom right.

## Slide 2
Introductory Concepts
Numbering Systems
Boolean Algebra
Combinational Logic
Flip-Flops
Arithmetic Circuits
Counters & Shift Registers
IC Logic Families
MSI Devices

## Slide 3
Introduction
Basic Logic Gates (NOT, OR, AND)
Truth Table
Logic Circuit << >> Boolean Expression
Boolean Theorems
Universality of NOR / NAND gates
3. Boolean Algebra

## Slide 4: Introduction
e.g. 1
Fridge Light Logic
L
D
L = F(D)
Door
3.1
Light

## Slide 5: Introduction
Simplified Aircraft
take off signal
logic
T
V
T = F(V, C)
Visibility
3.1
Take off signal
C
Aircraft Condition
e.g. 2

## Slide 6: Boolean Algebra
In general, it’s a mean to express the relationship between a logic circuit’s outputs and inputs
Logic Circuit
X
Y
A
B
C
D
X = F1(A,B,C,D)
Y = F2(A,B,C,D)
Boolean variables
3.1
Boolean variables

## Slide 7: Boolean Algebra
Boolean variables can have
only 2 possible values, 0 or 1
Close
Open
Yes
No
High
Low
On
Off
True
False
Logic 1
Logic 0
3.1

## Slide 8: Boolean Operation
Logic addition: OR operation
Logic multiplication: AND operation
Logic complementation: NOT operation
Circuits that carry out elementary operations is known as GATES
3.2

## Slide 9: NOT Gate (Inverter)
A | X
0 | 1
1 | 0
3.5
Truth Table
A
X
Symbol
Boolean Equation
Note:
output = inverted input
It has 1 input and 1 output

## Slide 10
3.2
Complete the boolean equation:

## Slide 11
3.2
Complete the boolean equation:
A
A

## Slide 12: OR Gate
X = A + B
3.3
Only all inputs = 0 then output = 0
Any input = 1, output = 1
Has 1 output and minimum of 2 inputs
A | B | X
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Truth Table
A
B
X
Symbol
Boolean Equation
Note:

## Slide 13
You can say this glass is half full or half empty, both describe the situation fully. This is because there can only be 2 possibilities, full or empty.
Likewise, in the case of logic circuits, the output can only be 1 or 0. It is therefore sufficient to describe just when the output will be 1.

## Slide 14
3.2
Complete the Boolean equation:

## Slide 15
3.2
Complete the Boolean equation:
Boolean Theorem 1 - 4

## Slide 16
3.2
Complete the X waveform:
A
B
X
A
B
X
t1
t2
t3

## Slide 17
3.2
Complete the X waveform:
A
B
X
A
B
X
disabled
disabled
Enable A to pass through
A can be data signal, B can be the control signal
t1
t2
t3

## Slide 18: AND Gate
A | B | X
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
3.3
Only all inputs = 1 then output = 1
Any input = 0, output = 0
Has 1 output and minimum of 2 inputs
Truth Table
Symbol
Boolean Equation
Note:
A
B
X

## Slide 19
3.2
Complete the boolean equation:

## Slide 20
3.2
Complete the boolean equation:
Boolean Theorem 5 - 8

## Slide 21
3.2
Complete the X waveform:
A
B
X
A
B
X
t1
t2
t3

## Slide 22
3.2
Complete the X waveform:
A
B
X
disabled
Enable A to pass through
A
B
X
Enable A to pass through
A can be data signal, B can be the control signal
t1
t2
t3

## Slide 23: Truth Tables
Relate output to inputs (in details)
For N inputs there will be 2N possible combinations
3.2
Logic
Circuit
Y
A1
0 . . . 0 ?
0 . . . 1 ?
1 . . . 0 ?
1 . . . 1 ?
A1 … AN
Y
A2
AN
.
.
2N

## Slide 24
3.2
Write the truth table for a 3-input OR gate
A | B | C | X
A
B
C
X
23=8

## Slide 25
3.2
Write the truth table for a 3-input OR gate
A | B | C | X
0 |  |  | 
0 |  |  | 
0 |  |  | 
0 |  |  | 
1 |  |  | 
1 |  |  | 
1 |  |  | 
1 |  |  | 
A
B
C
X

## Slide 26
3.2
Write the truth table for a 3-input OR gate
A | B | C | X
0 | 0 |  | 
0 | 0 |  | 
0 | 1 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 0 |  | 
1 | 1 |  | 
1 | 1 |  | 
A
B
C
X

## Slide 27
3.2
Write the truth table for a 3-input OR gate
A | B | C | X
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
A
B
C
X

## Slide 28
3.2
Write the truth table for a 3-input OR gate
A | B | C | X
0 | 0 | 0 | 0
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
A
B
C
X
only all inputs = 0 then output = 0

## Slide 29
3.2
Write the truth table for a 3-input OR gate
A | B | C | X
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
A
B
C
X
any input = 1, output = 1

## Slide 30
3.2
Write the truth table for a 4-input AND gate
A
B
C
D
X
A | B | C | D | X
24=16

## Slide 31
3.2
Write the truth table for a 4-input AND gate
A
B
C
D
X
A | B | C | D | X
0 |  |  |  | 
0 |  |  |  | 
0 |  |  |  | 
0 |  |  |  | 
0 |  |  |  | 
0 |  |  |  | 
0 |  |  |  | 
0 |  |  |  | 
1 |  |  |  | 
1 |  |  |  | 
1 |  |  |  | 
1 |  |  |  | 
1 |  |  |  | 
1 |  |  |  | 
1 |  |  |  | 
1 |  |  |  | 

## Slide 32
3.2
Write the truth table for a 4-input AND gate
A
B
C
D
X
A | B | C | D | X
0 | 0 |  |  | 
0 | 0 |  |  | 
0 | 0 |  |  | 
0 | 0 |  |  | 
0 | 1 |  |  | 
0 | 1 |  |  | 
0 | 1 |  |  | 
0 | 1 |  |  | 
1 | 0 |  |  | 
1 | 0 |  |  | 
1 | 0 |  |  | 
1 | 0 |  |  | 
1 | 1 |  |  | 
1 | 1 |  |  | 
1 | 1 |  |  | 
1 | 1 |  |  | 

## Slide 33
3.2
Write the truth table for a 4-input AND gate
A
B
C
D
X
A | B | C | D | X
0 | 0 | 0 |  | 
0 | 0 | 0 |  | 
0 | 0 | 1 |  | 
0 | 0 | 1 |  | 
0 | 1 | 0 |  | 
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 
1 | 1 | 1 |  | 

## Slide 34
3.2
Write the truth table for a 4-input AND gate
A
B
C
D
X
A | B | C | D | X
0 | 0 | 0 | 0 | 
0 | 0 | 0 | 1 | 
0 | 0 | 1 | 0 | 
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 0 | 
0 | 1 | 0 | 1 | 
0 | 1 | 1 | 0 | 
0 | 1 | 1 | 1 | 
1 | 0 | 0 | 0 | 
1 | 0 | 0 | 1 | 
1 | 0 | 1 | 0 | 
1 | 0 | 1 | 1 | 
1 | 1 | 0 | 0 | 
1 | 1 | 0 | 1 | 
1 | 1 | 1 | 0 | 
1 | 1 | 1 | 1 | 

## Slide 35
3.2
Write the truth table for a 4-input AND gate
A
B
C
D
X
A | B | C | D | X
0 | 0 | 0 | 0 | 
0 | 0 | 0 | 1 | 
0 | 0 | 1 | 0 | 
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 0 | 
0 | 1 | 0 | 1 | 
0 | 1 | 1 | 0 | 
0 | 1 | 1 | 1 | 
1 | 0 | 0 | 0 | 
1 | 0 | 0 | 1 | 
1 | 0 | 1 | 0 | 
1 | 0 | 1 | 1 | 
1 | 1 | 0 | 0 | 
1 | 1 | 0 | 1 | 
1 | 1 | 1 | 0 | 
1 | 1 | 1 | 1 | 1
only all inputs = 1 then output = 1

## Slide 36
3.2
Write the truth table for a 4-input AND gate
A
B
C
D
X
A | B | C | D | X
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1
any input = 0, output = 0

## Slide 37: Logic Circuits << >> Boolean Expression
A
C
X
3.6
Write the Boolean expression for X
B

## Slide 38
A
C
X = AB + C
3.6
Write the Boolean expression for X
AB
B
Logic Circuits << >> Boolean Expression

## Slide 39
X =
C
A
B
3.6
Write the Boolean expression for X
Logic Circuits << >> Boolean Expression

## Slide 40: Logic Circuits
A + B
X = (A + B) C
C
A
3.6
Write the Boolean expression for X
B

## Slide 41
3.6
Write the Boolean expression for X
A
B
X =
Logic Circuits << >> Boolean Expression

## Slide 42
3.6
Write the Boolean expression for X
A
B
Logic Circuits << >> Boolean Expression

## Slide 43
3.6
Write the Boolean expression for X
A
B
X =
Logic Circuits << >> Boolean Expression

## Slide 44
3.6
Write the Boolean expression for X
A + B
A
B
Logic Circuits << >> Boolean Expression

## Slide 45
A
B
A
C
Y=?
3.6
Write the Boolean expression for Y.

## Slide 46
A
B
A
C
Y
3.6
Write the Boolean expression for Y.

## Slide 47: Evaluate the output of the logic circuit.
A=0
B=1
C=1
A=0
C=1
3.7

## Slide 48: Evaluate the output of the logic circuit.
A=0
B=1
0
C=1
1
0
A=0
C=1
1
0
3.7

## Slide 49
For the circuit shown, evaluate the output for
A=0, B=1, C=0, D=0 and E=1
A
B
C
D
E
3.7
0
1
0
0
1

## Slide 50
For the circuit shown, evaluate the output for
A=0, B=1, C=0, D=0 and E=1
A
B
C
D
E
3.7
1
0
1
0
0
1
1
1
1
0

## Slide 51: Implement circuit from Boolean Expression
3.8
Logic Circuits << >> Boolean Expression

## Slide 52: Implement circuits from Boolean Expression
3.8
B
A
C
Y
Work from output

## Slide 53: Implement circuits from Boolean Expression
3.8
B
A
C
Y
Can also work from input

## Slide 54
Implement the following functions with logic gates
(a)
(b)
3.8

## Slide 55
Y
W
Z
X
(a)
X
A
C
B
(b)

## Slide 56
A circuit output expression is
Draw the truth table for the circuit.
Evaluate Y when A=0, B=1, C=1and D=1
3.8

## Slide 57
3.8
A | B | C | D | ABC | (ABC) + D | Y
A, B, C, D : 4 inputs
Break down the expression into manageable terms
Truth Table

## Slide 58
3.8
A | B | C | D | ABC | (ABC) + D | Y
0 | 0 | 0 | 0 |  |  | 
0 | 0 | 0 | 1 |  |  | 
0 | 0 | 1 | 0 |  |  | 
0 | 0 | 1 | 1 |  |  | 
0 | 1 | 0 | 0 |  |  | 
0 | 1 | 0 | 1 |  |  | 
0 | 1 | 1 | 0 |  |  | 
0 | 1 | 1 | 1 |  |  | 
1 | 0 | 0 | 0 |  |  | 
1 | 0 | 0 | 1 |  |  | 
1 | 0 | 1 | 0 |  |  | 
1 | 0 | 1 | 1 |  |  | 
1 | 1 | 0 | 0 |  |  | 
1 | 1 | 0 | 1 |  |  | 
1 | 1 | 1 | 0 |  |  | 
1 | 1 | 1 | 1 |  |  | 
Fill up the different input combinations

## Slide 59
3.8
A | B | C | D | ABC | (ABC) + D | Y
0 | 0 | 0 | 0 | 0 |  | 
0 | 0 | 0 | 1 | 0 |  | 
0 | 0 | 1 | 0 | 0 |  | 
0 | 0 | 1 | 1 | 0 |  | 
0 | 1 | 0 | 0 | 0 |  | 
0 | 1 | 0 | 1 | 0 |  | 
0 | 1 | 1 | 0 | 0 |  | 
0 | 1 | 1 | 1 | 0 |  | 
1 | 0 | 0 | 0 | 0 |  | 
1 | 0 | 0 | 1 | 0 |  | 
1 | 0 | 1 | 0 | 0 |  | 
1 | 0 | 1 | 1 | 0 |  | 
1 | 1 | 0 | 0 | 0 |  | 
1 | 1 | 0 | 1 | 0 |  | 
1 | 1 | 1 | 0 | 1 |  | 
1 | 1 | 1 | 1 | 1 |  | 
Only all input = 1, output = 1

## Slide 60
3.8
A | B | C | D | ABC | (ABC) + D | Y
0 | 0 | 0 | 0 | 0 | 0 | 
0 | 0 | 0 | 1 | 0 | 1 | 
0 | 0 | 1 | 0 | 0 | 0 | 
0 | 0 | 1 | 1 | 0 | 1 | 
0 | 1 | 0 | 0 | 0 | 0 | 
0 | 1 | 0 | 1 | 0 | 1 | 
0 | 1 | 1 | 0 | 0 | 0 | 
0 | 1 | 1 | 1 | 0 | 1 | 
1 | 0 | 0 | 0 | 0 | 0 | 
1 | 0 | 0 | 1 | 0 | 1 | 
1 | 0 | 1 | 0 | 0 | 0 | 
1 | 0 | 1 | 1 | 0 | 1 | 
1 | 1 | 0 | 0 | 0 | 0 | 
1 | 1 | 0 | 1 | 0 | 1 | 
1 | 1 | 1 | 0 | 1 | 1 | 
1 | 1 | 1 | 1 | 1 | 1 | 
any input = 1, output = 1

## Slide 61
3.8
A | B | C | D | ABC | (ABC) + D | Y
0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0 | 1 | 0
1 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 0 | 1
1 | 1 | 0 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 1 | 1 | 0
1 | 1 | 1 | 1 | 1 | 1 | 0
output
= inverted input

## Slide 62
3.8
A | B | C | D | ABC | (ABC) + D | Y
0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0 | 1 | 0
1 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 0 | 1
1 | 1 | 0 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 1 | 1 | 0
1 | 1 | 1 | 1 | 1 | 1 | 0
when A=0, B=1, C=1, D=1, Y = 0

## Slide 63
when A=0, B=1, C=1and D=1
3.8
Another way of working out the output value:
(substitute the input values into the expression)

## Slide 64: NOR Gate
A | B | X
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
3.3
Only all inputs = 0 then output = 1
Any input = 1, output = 0
Has 1 output and minimum of 2 inputs
Truth Table
Symbol
Boolean Equation
Note:
A
B
X

## Slide 65
3.2
Complete the X waveform:
A
B
X
A
B
X
t1
t2
t3

## Slide 66
3.2
Complete the X waveform:
A
B
X
disabled
disabled
Enable A to pass through, though inverted
A can be data signal, B can be the control signal
A
B
X
t1
t2
t3

## Slide 67: NAND Gate
A | B | X
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
3.3
Only all inputs = 1 then output = 0
Any input = 0, output = 1
Has 1 output and minimum of 2 inputs
Truth Table
Symbol
Boolean Equation
Note:
A
B
X

## Slide 68
3.2
Complete the X waveform:
A
B
X
A
B
X
t1
t2
t3

## Slide 69
3.2
Complete the X waveform:
A
B
X
disable
Enable A to pass through, though inverted
Enable A to pass through, though inverted
A can be data signal, B can be the control signal
A
B
X
t1
t2
t3

## Slide 70
Summary on Gates
Inverter |  |  | output = inverted input
OR |  |  | Any input = 1, output = 1. Only all inputs = 0 then output = 0.
AND |  |  | Any input = 0, output = 0. Only all inputs = 1, then output = 1.
NOR |  |  | Any input = 1, output = 0. Only all inputs = 0, then output = 1.
NAND |  |  | Any input = 0, output = 1. Only all inputs = 1, then output = 0.
A
X
A
X
B
A
X
B
A
X
B
A
B
X

## Slide 71: Boolean Theorems 9 - 14
Commutative laws
Associative laws
Distributive laws
3.10

## Slide 72: Boolean Theorems 15 - 16
3.10
Proof:
Apply Theorem (15), rewrite A back into A + AB
Variation of (16a)

## Slide 73
A | B | 
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
Same behaviour
Proof of DeMorgan’s Theorem

## Slide 74
A | B | 
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Same behaviour
Proof of DeMorgan’s Theorem

## Slide 75: Boolean Theorems 17 - 18
3.11
With 3 variables
DeMorgan’s Theorem
A way to remember:
change the operation,
split / join the bar

## Slide 76: Common Mistake
3.11

## Slide 77
Simplify the Boolean expression using Boolean Theorem
(1)
(2)
3.11

## Slide 78
(3)
Use brackets to make expression clear

## Slide 79
(4)
3.11

## Slide 80
(5)

## Slide 81
(6)
3.11

## Slide 82
(7)
3.11

## Slide 83
3.11
(8)
Apply
Theorem 16a

## Slide 84
(9)
3.11

## Slide 85
(3)
Use brackets to make expression clear

## Slide 86
Why simplify Boolean Expression ?
simpler circuit, save cost !
3.11
Because it lead to

## Slide 87: Universality of NAND gates
A
3.12
NOT Function can be implemented by NAND gate
Inputs are shorted together, i.e. both inputs to the NAND gate are A

## Slide 88: Universality of NAND gates
3.12
B
A
AND Function can be implemented by NAND gates alone

## Slide 89: Universality of NAND gates
3.12
Alternative Representationof OR gate
A
B
OR Function can be implemented by NAND gates alone

## Slide 90: Universality of NAND gates
3.12
Alternative Representation of NOR gate
B
A
NOR Function can be implemented by NAND gates alone

## Slide 91
A
X
B
A
X
A
B
X
B
A
X
Summary | Equivalent | X =
 |  | AB
 |  | A+B
A
X
B
A
X
X
A
B
X
B
A

## Slide 92: Universality of NOR gates
3.12
NOT Function can be implemented by NOR gate
A
Inputs are shorted together, i.e. both inputs to the NOR gate are A

## Slide 93: Universality of NOR gates
3.12
OR Function can be implemented by NOR gates alone
B
A

## Slide 94: Universality of NOR gates
3.12
Alternative Representationof AND gate
A
B
AND Function can be implemented by NOR gates alone

## Slide 95: Universality of NOR gates
3.12
Alternative Representation of NAND gate
NAND Function can be implemented by NOR gates alone
A
B

## Slide 96
A
X
B
A
X
A
B
X
A
B
X
Summary | Equivalent | X =
 |  | A+B
 |  | AB
A
X
X
B
A
B
A
X
X
B
A

## Slide 97: IC (Integrated Circuit)
74LS00 NAND (Quad)
74LS08 AND (Quad)
74LS32 OR (Quad)
etc.
3.12

## Slide 98
How do we minimize number of ICs to implement a circuit?
By converting the circuit to using universal gates ONLY

## Slide 99
3.12
Implement the expression. How many IC do you need?

## Slide 100
3.12
A
B
C
D
X
2 IC (1 AND gate IC and 1 OR gate IC)
are required if no conversion is done
Implement the expression. How many IC do you need?

## Slide 101
3.12
A
B
C
D
X
Implement the expression using NAND gates only
Method 1
Replace each gate by NAND equivalent

## Slide 102
AND
OR
3.12
Implement the expression using NAND gates only
A
B
C
D
X
Method 1
Replace each gate by NAND equivalent

## Slide 103
AND
OR
3.12
Implement the expression using NAND gates only
A
B
C
D
X
Method 1 con’t
Cancel 2 inversion in a row (if any)

## Slide 104
Method 1 con’t
(redraw after cancelling 2 inversion in a row)
3.12
Implement the expression using NAND gates only
X
A
C
B
D
Now, only 1 NAND gate IC is required

## Slide 105
Method 2
(Place double bar over OR operation,
then apply DeMorgan Theorem)
3.12
Implement the expression using NAND gates only
X
A
C
B
D

## Slide 106
3.12
Implement the expression. How many IC do you need?

## Slide 107
3.12
A
B
X
C
D
2 IC (1 OR gate IC and 1 AND gate IC)
are required if no conversion is done
Implement the expression. How many IC do you need?

## Slide 108
3.12
Implement the expression using NOR gates only
Method 1
Replace each gate by NOR equivalent
A
B
X
C
D

## Slide 109
Method 1
Replace each gate by NOR equivalent)
OR
AND
3.12
Implement the expression using NOR gates only
A
B
C
D
X

## Slide 110
Method 1 con’t
Cancel double inversion in a row (if any)
OR
AND
3.12
Implement the expression using NOR gates only
A
B
C
D
X

## Slide 111
Method 1 con’t
(redraw after cancelling 2 inversion in a row)
3.12
Implement the expression using NOR gates only
Now, only 1 NOR gate IC is required
X
A
C
B
D

## Slide 112
Method 2
(Place double bar over AND operation,
then apply DeMorgan Theorem)
3.12
Implement the expression using NOR gates only
A
B
C
D
X

## Slide 113
3.12
Implement the expression using one 7400 package
A
B
X

## Slide 114: Examples
Example 3-20
Example 3-21
Example 3-23
3.14
Self Study

## Slide 115: The End