## Slide 1
Instructions for using the PowerPoint slides:
To view the animated steps - click anywhere on the slide.
To skip the animated steps to go to previous or next page - click the arrowheads at the bottom right.

## Slide 2
  Introductory Concepts
  Numbering Systems
  Boolean Algebra
  Combinational Logic
  Flip-Flops
  Digital Arithmetic
  Counters & Registers
  IC Logic Families
  MSI Logic Circuits

## Slide 3
  IC Logic Families – Part 1
  Digital IC Terminology
  TTL Logic Family
  TTL Series Characteristics
  Other TTL Characteristics
  CMOS Series Characteristics
  Low-Voltage Technology
  Tristate Logic Outputs

## Slide 4: IC family – based on complexity
Complexity Number of Gates
SSI (Small Scale Integration) < 12
MSI (Medium …) 12 to 99
LSI (Large …) 100 to 9999
VLSI (Very Large …) 10,000 to 99,999
ULSI (Ultra Large …) 100,000 to 99,9999
GSI (Giga …) > 1 million
(Table 4-5)
8.1 – Digital IC Terminology

## Slide 5: Examples of some IC Manufacturers
Motorola
Texas Instrument e.g. SN7400
National Semiconductors e.g. DM7400
Signetics e.g. S7400
Advanced Micro Devices (AMD)
Hitachi
Intel
etc http://www.advanced-tech.com/ic_logos/ic_logos.htm
8.1 – Digital IC Terminology

## Slide 6: Examples of some IC Packages
DIP – Dual-In-line Package
lead-pitch
8.1 – Digital IC Terminology
Dual-in-line: 2 rows of leads
The distance between the adjacent leads is called lead-pitch.

## Slide 7: Examples of some IC Packages
PLCC – Plastic leaded chip
carrier (J-lead)
More IC packages on page 422
8.1 – Digital IC Terminology
PLCC has leads on 4 sides.

## Slide 8: Some Comparisons on Different IC packages
Acronym | Package name | Height (mm) | Lead pitch
DIP | Dual-In-line Package | 5.1 | 2.54
SOIC | Small Outline Integrated Circuit | 2.65 | 1.27
SSOP | Shrink Small Outline Package | 2.0 | 0.65
TSSOP | Thin Shrink Small Outline Package | 1.1 | 0.65
TVSOP | Thin Very Small Outline Package | 1.2 | 0.4
PLCC | Plastic Leaded Chip Carrier | 4.5 | 1.27
QFP | Quad Flat Pack | 4.5 | 0.635
TQFP | Thin Quad Flat Pack | 1.6 | 0.5
1mils = 0.0255mm = 1/1000 of an inch
8.1 – Digital IC Terminology
This is only for information

## Slide 9: Simple Comparisons on Different IC packages
Acronym | Package name | Height (mm) | Lead pitch
DIP | Dual-In-line Package | 5.1 | 2.54
SOIC | Small Outline Integrated Circuit | 2.65 | 1.27
SSOP | Shrink Small Outline Package | 2.0 | 0.65
TSSOP | Thin Shrink Small Outline Package | 1.1 | 0.65
TVSOP | Thin Very Small Outline Package | 1.2 | 0.4
PLCC | Plastic Leaded Chip Carrier | 4.5 | 1.27
QFP | Quad Flat Pack | 4.5 | 0.635
TQFP | Thin Quad Flat Pack | 1.6 | 0.5
1mils = 0.0255mm = 1/1000 of an inch
Surface-Mount packages
8.1 – Digital IC Terminology

## Slide 10: Digital IC Terminology
IC manufacturers have to provide data sheet for the IC.
Data sheet details the IC’s functional characteristics, electrical characteristics and timing characteristics.
8.1 – Digital IC Terminology
Functional characteristics tell us about the purpose of the IC and how it works. e.g. through a truth table.

## Slide 11: Digital IC Terminology
Electrical characteristics tell us things like the range of supply voltage, input and output voltages, input and output currents, etc.
8.1 – Digital IC Terminology
Timing characteristics tell us things like propagation delay, hold time, setup time, etc.

## Slide 12: Digital IC Terminology
In the following slides, we are going to learn the terms used for the electrical and timing characteristics.
8.1 – Digital IC Terminology

## Slide 13: Input Voltages - VIH / VIL
VIH(min) - High-level Input voltage
The voltage required for a logic ‘1’ at an input
Typically VIH(min) = 2.0 Volt
VIL(max) - Low-level Input voltage
The voltage required for a logic ‘0’ at an input
Typically VIL(max) = 0.8 Volt
8.1 – Digital IC Terminology

## Slide 14: Output Voltages – VOH / VOL
VOH(min) - High-level Output voltage
The voltage at the output in the logic ‘1’ state
Typically VOH(min) = 2.4 Volt
VOL(max) - Low-level Output voltage
The voltage at the output in the logic ‘0’ state
Typically VOL(max) = 0.4 Volt
8.1 – Digital IC Terminology

## Slide 15: VIH / VIL and VOH / VOL (Pictorially)
Logic 1
Logic 0
Indeterminate
range
VOH(min)
VOL(max)
VIH(min)
VIL(max)
8.1 – Digital IC Terminology
Logic 1
Logic 0
Disallowed
range
OUTPUT
INPUT
0.8V
2.0V
2.4V
0.4V

## Slide 16: Digital IC Terminology – IIH / IIL and IOH / IOL
IIH(max) - High-level Input current
The current that flow into an Input when a specified logic High voltage is applied to that input
IIL(max) - Low-level Input current
The current that flow into an Input when a specified logic Low voltage is applied to that input
IOH(min) - High-level Output current
The current that flow from an Output in the logic High state under specified load condition
IOL(min) - Low-level Output current
The current that flow from an Output in the logic Low state under specified load condition
8.1 – Digital IC Terminology

## Slide 17
Current and Voltage in Logic HIGH state
- A circuit illustration
8.1 – Digital IC Terminology
IOH
IIH
+
VOH
-
+
VIH
-

## Slide 18
8.1 – Digital IC Terminology
Current and Voltage in Logic LOW state
- A circuit illustration
IOL
IIL
+
VOL
-
+
VIL
-
+5V

## Slide 19: Noise Immunity (i)
It is a circuit’s ability to tolerate noise voltages on its inputs.
Noise Immunity is measured by Noise Margin.
It is the amount of noise that can be added without the circuit malfunctioning.
8.1 – Digital IC Terminology

## Slide 20: Noise Immunity (ii)
High State noise margin VNH
VNH = VOH(min) – VIH(min)
8.1 – Digital IC Terminology
VOH(min)
VIH(min)
Logic 1
Logic 1
Logic 0
Logic 0
voltage
Disallowed
range
Indeterminate
range
output
input
-ve noise
VNH

## Slide 21: Noise Immunity (iii)
When a HIGH logic output is driving another input, any NEGATIVE noise spikes greater than VNH will cause the voltage to fall into the indeterminate range, causing the circuit to malfunction.
8.1 – Digital IC Terminology
High State noise margin VNH = VOH(min) – VIH(min)

## Slide 22: Noise Immunity (iv)
Low State noise margin VNL
VNL = VIL(max) – VOL(max)
8.1 – Digital IC Terminology
VIL(max)
Logic 1
Logic 1
Logic 0
Logic 0
voltage
Disallowed
range
Indeterminate
range
output
input
VOL(max)
+ve noise
VNL

## Slide 23: Noise Immunity (v)
When a LOW logic output is driving another input, any POSITIVE noise spikes greater than VNL will cause the voltage to rise into the indeterminate range, causing the circuit to malfunction.
8.1 – Digital IC Terminology
Low State noise margin VNL = VIL(max) – VOL(max)

## Slide 24
Parameter | Min(V) | Typical(V) | Max(V)
VOH | 2.4 | 3.4 | 
VOL |  | 0.2 | 0.4
VIH | 2.0* |  | 
VIL |  |  | 0.8*
Determine the maximum-amplitude noise spike that can be tolerated when a HIGH output is driving an input
(b) Determine the maximum-amplitude noise spike that can be tolerated when a LOW output is driving an input
8.1 – Digital IC Terminology

## Slide 25
Parameter | Min(V) | Typical(V) | Max(V)
VOH | 2.4 | 3.4 | 
VOL |  | 0.2 | 0.4
VIH | 2.0* |  | 
VIL |  |  | 0.8*
Determine the maximum-amplitude noise spike that can be tolerated when a HIGH output is driving an input
VNH = VOH (min) - VIH (min)
= 2.4 – 2 = 0.4V
(b) Determine the maximum-amplitude noise spike that can be tolerated when a LOW output is driving an input
VNL = VIL (max) - VOL (max)
= 0.8 – 0.4 = 0.4V
8.1 – Digital IC Terminology

## Slide 26
8.1 – Digital IC Terminology
End of Chp8-ICGatesFamily Part 1