## Slide 1
Instructions for using the PowerPoint slides:
To view the animated steps - click anywhere on the slide.
To skip the animated steps to go to previous or next page - click the arrowheads at the bottom right.

## Slide 2
  Introductory Concepts
  Numbering Systems
  Boolean Algebra
  Combinational Logic
  Flip-Flops
  Digital Arithmetic
  Counters & Registers
  IC Logic Families
  MSI Logic Circuits

## Slide 3
  IC Logic Families – Part 3
  Digital IC Terminology (Con’t)
  TTL Logic Family
  TTL Series Characteristics
  Other TTL Characteristics
  CMOS Series Characteristics
  Low-Voltage Technology
  Tristate Logic Outputs

## Slide 4: CMOS Logic Family
CMOS – Complementary Metal Oxide Semiconductor
CMOS use unipolar MOSFET transistors as their major circuit elements.
8.10 – CMOS Series Characteristics

## Slide 5: CMOS Series Characteristics
Used in products where very low power is a priority
eg. Calculators, watches
Used in products where a very high level of integration is necessary.
eg. computers
Used in products where there is a lot of noise and high ambient temperatures.
eg. electronic fuel injection
Used in products where heat dissipation is a priority.
eg. satellites
8.10 – CMOS Series Characteristics

## Slide 6: CMOS Series Characteristics (i)
8.10 – CMOS Series Characteristics
Series | Comments | PD(mW) | tpd(nS)
4000/1000 | Very slow compared to TTL & other CMOS Not pin compatible Not electrically compatible Rarely used | 1 | 50
74C | Same as 4000 series Pin compatible Functionally equivalent to TTL (74C74 and 7474) Not electrically compatible | 1 | 50
74HC/HCT (High Speed CMOS) | Improved version of 74C series Increase speed & higher output current capability Pin compatible & Functionally equivalent to TTL (HC) Electrically compatible with TTL (74HCT) | 2.5 | 8

## Slide 7: CMOS Series Characteristics
8.10 – CMOS Series Characteristics
2 ICs are pin compatible when their pin configurations are the same. (i.e. pin-to-pin matching)
2 ICs are functionally equivalent when the logic functions they perform are exactly the same. (e.g both ICs each have 4 2-input NAND gates)
2 ICs are electrically compatible when they can be connected to each other directly.

## Slide 8: CMOS Series Characteristics (iii)
8.10 – CMOS Series Characteristics
Series | Comments | PD(mW) | tpd(nS)
74BCT (BiCMOS) | Low power characteristics of CMOS and high speed characteristics of bipolar Some are pin compatible with TTL |  | 
74ABT (Advanced BiCMOS) | Second generation of BiCMOS devices Designed for low-voltage systems |  | 
This is only for information

## Slide 9: CMOS Series Characteristics (ii)
8.10 – CMOS Series Characteristics
Series | Comments | PD(mW) | tpd(nS)
74AC/ACT (Advanced CMOS) | Advantage over HC series in noise immunity Max Clock speed Functionally equivalent to TTL Not Pin compatible with TTL Not electrically compatible with TTL (74AC) electrically compatible with TTL (74ACT) | 5 | 4.7
74AHC (Advanced High-speed CMOS) | Direct replacement for HC series devices with improved characteristics | 9 x 10-2 | 3.7
This is only for information

## Slide 10: CMOS Series Characteristics (iv)
8.10 – CMOS Series Characteristics
Parameters | Comments
Power supply voltage | 4000 and 74C series will operate with VDD values from 3 to 15 V. 74HC and 74HCT series will operate with VDD values from 2 to 6V
Voltage level | i/p and o/p voltage level is different for different CMOS VOL for CMOS is very close to 0V VOH for CMOS is very close to VDD
Noise margin | CMOS devices has greater noise margin than TTL. Noise margin increases when CMOS operates at higher supply voltage
Power dissipation | Power dissipation is very small – typically 2.5 nW per gate when VDD is 5v As the frequency increases, the power consumption PD increase proportionally.

## Slide 11: CMOS Series Characteristics (v)
8.10 – CMOS Series Characteristics
Parameters | Comments
Fan out | CMOS fan-out is dependant upon the maximum propagation delay and frequency of operation. Typically at frequency less than 1 MHz the fan-out would be limited to 50.
Unused inputs | All CMOS inputs must be tied to VDD or 0V or to another input.
Static charge susceptibility | CMOS devices are very susceptible to static charge. Good handling procedures must be observed.
Latch up | High voltage spike can turn on the unwanted transistor embedded in the substrate of CMOS IC, causing large current to flow and destroy the IC.

## Slide 12: Comparison of TTL and CMOS
Table 8-9
8.10 – CMOS Series Characteristics
Self Study

## Slide 13: Low Voltage Technology
8.10 – CMOS Series Characteristics
Increasing chip density will reduce propagation delay,(tpd) BUT increase power Dissipation, PD.
Solution: Low Voltage Technology
Self Study

## Slide 14: Tristate (Three-State) Logic Outputs (i)
There are situations in which several digital devices must share the use of a single wire in order to transmit a signal to some destination device. e.g. sharing of data bus
This means that several devices must have their outputs tied to the same wire. But …
8.13 – Tristate (Three-State) Logic Outputs

## Slide 15: Tristate (Three-State) Logic Outputs (ii)
Conventional CMOS outputs should never be tied together.
TTL totem pole outputs should never be tied together.
Outputs tied together will cause high current to flow through the output transistors, especially when an output is at logic “0”.
The resultant voltage level at the output may fall into the indeterminate range.
8.13 – Tristate (Three-State) Logic Outputs

## Slide 16: Tristate (Three-State) Logic Outputs (iii)
1
0
Look at this situation, what will be the Logic Level at the output ?
8.13 – Tristate (Three-State) Logic Outputs

## Slide 17: Tristate (Three-State) Logic Outputs (iv)
GND
+V
0
1
E=1
GND
+V
1
0
E=1
GND
+V
0 or 1
Hi-Z
E=0
8.13 – Tristate (Three-State) Logic Outputs
- Using Tristate is the Solution, e.g. shows a Tristate Inverter
- Enabled
- Enabled
Disabled,
output in a high-impendance (Z) state

## Slide 18: Tristate (Three-State) Logic Outputs (v)
1
0
8.13 – Tristate (Three-State) Logic Outputs
E
Now, what is the Logic level at the output?
It is important to note that when tristate outputs are connected together, ONLY ONE of them should be enabled at one time.
- An application:

## Slide 19
End of Chp8-ICGatesFamily Part 3
8.13 – Tristate (Three-State) Logic Outputs