## Slide 1
Instructions for using the PowerPoint slides:
To view the animated steps - click anywhere on the slide.
To skip the animated steps to go to previous or next page - click the arrowheads at the bottom right.

## Slide 2
  Introductory Concepts
  Numbering Systems
  Boolean Algebra
  Combinational Logic
  Flip-Flops
  Digital Arithmetic
  Counters & Registers
  IC Logic Families
  MSI Logic Circuits

## Slide 3
9-1 Decoders
MSI stands for Medium-Scale-Integration
Digital ICs (Integrated Circuits) are often categorized according to their circuit complexity as shown in this table:
Complexity Number of Gates in the IC
SSI (Small) < 12 (e.g. 74LS00 – nand gate ICs)
MSI (Medium) 12 to 99
LSI (Large) 100 to 9999
VLSI (Very Large) 10,000 to 99,999
ULSI (Ultra Large) 100,000 to 99,9999
GSI (Giga) > 1 million (e.g. microprocessor)
What is MSI Logic Circuits?

## Slide 4
9-1 Decoders
In this chapter, we will study 4 MSI devices.
They are:
Decoder
Encoder
Multiplexer
Demultiplexer

## Slide 5
9-1 Decoders
A decoder is a logic circuit that accepts a binary number and activates only the output that corresponds to that input number.
Decoder

## Slide 6: Decoders – e.g.
9-1 Decoders
1-of-8
Decoder
A0
A1
A2
.
.
.
O0
O1
O7
Inputs can accept a
3-bit binary
8 outputs
Each output detects a different input code. e.g. O6 detects binary 110, i.e. O6 will become active only when input is 110.

## Slide 7: Decoders – in general
9-1 Decoders
Decoder
.
.
.
A0
A1
AN-1
.
.
.
O0
O1
OM-1
Inputs can accept an N-bit binary
M outputs,
M can be less than or equal to 2N

## Slide 8
9-1 Decoders
Next slide introduces 74LS138 decoder IC

## Slide 9: 74LS138
/E1/E2E3
/O7 /O6 /O5 /O4 /O3 /O2 /O1 /O0
74LS138
1-of-8 decoder
A2 A1 A0
9-1 Decoders
Inputs can accept a
3-bit binary
8 outputs

## Slide 10: 74LS138
9-1 Decoders
1-of-8 decoder is also called:
3-line to 8-line decoder
Binary-to-octal decoder
Binary-to-octal converter
74LS138 is a 1-of-8 decoder
What is 1-of-8?
1-of-8 means only 1 of the 8 outputs can be active at one time.

## Slide 11: 74LS138
/E1/E2E3
/O7 /O6 /O5 /O4 /O3 /O2 /O1 /O0
74LS138
1-of-8 decoder
A2 A1 A0
9-1 Decoders
74LS138 has ACTIVE LOW outputs.
e.g. /O6 becomes LOW only when inputs A2A1A0 = 110

## Slide 12: 74LS138
/E1/E2E3
/O7 /O6 /O5 /O4 /O3 /O2 /O1 /O0
74LS138
1-of-8 decoder
A2 A1 A0
/E1 /E2 E3 outputs
9-1 Decoders
1 X X
74LS138 has 3 enable inputs
When any of the enable inputs is inactive, all outputs will be HIGH
all HIGH
X 1 X
X X 0
all HIGH
all HIGH

## Slide 13: 74LS138
/E1/E2E3
/O7 /O6 /O5 /O4 /O3 /O2 /O1 /O0
74LS138
1-of-8 decoder
A2 A1 A0
/E1 /E2 E3 outputs
9-1 Decoders
0 0 1
ALL enable inputs must be active, then will the outputs respond to the input codes
Respond to input code. e.g. /O5 becomes LOW when A2A1A0 = 101

## Slide 14: 74LS138
9-1 Decoders
What are the outputs for the following inputs:
1. /E1=0, /E2=1, E3=1, A2=1, A1=1, A0=0
2. /E1=0, /E2=0, E3=1, A2=0, A1=1, A0=0
Why are there multiple enable inputs?

## Slide 15: 74LS138
9-1 Decoders
What are the outputs for the following inputs:
1. /E1=0, /E2=1, E3=1, A2=1, A1=1, A0=0
all high (/E2 is disabled)
2. /E1=0, /E2=0, E3=1, A2=0, A1=1, A0=0
all high except O2
Why are there multiple enable inputs?
to allow easy expansion

## Slide 16
Using two 74LS138 ICs, design a 1-of-16 decoder
1-of-16 decoder is also known as binary-to-hex decoder/converter
1-of-16
decoder
A0
A1
A2
A3
.
.
/O0
/O13
/O14
/O15
9-1 Decoders
Must take care of additional input A3
16 outputs

## Slide 17
A3 A2 A1 A0
/O0 /O1 /O2 ….. /O6 /O7 /O8 /O9 /O10 .…. /O14 /O15
9-1 Decoders
First, try writing the truth table for the 1-to-16 decoder

## Slide 18
A3 A2 A1 A0
/O0 /O1 /O2 ….. /O6 /O7 /O8 /O9 /O10 .…. /O14 /O15
0 0 0 0 0 1 1 ….. 1 1 1 1 1 ….. 1 1
0 0 0 1 1 0 1 ….. 1 1 1 1 1 ….. 1 1
0 0 1 0 1 1 0 ….. 1 1 1 1 1 ….. 1 1
0 0 1 1 1 1 1 0 .. 1 1 1 1 1 ….. 1 1
0 1 0 0 1 1 1 ..0.. 1 1 1 1 1 ….. 1 1
0 1 0 1 1 1 1 ...0 1 1 1 1 1 ….. 1 1
0 1 1 0 1 1 1 ….. 0 1 1 1 1 ….. 1 1
0 1 1 1 1 1 1 ….. 1 0 1 1 1 ….. 1 1
1 0 0 0 1 1 1 ….. 1 1 0 1 1 ….. 1 1
1 0 0 1 1 1 1 ….. 1 1 1 0 1 ….. 1 1
1 0 1 0 1 1 1 ….. 1 1 1 1 0 ….. 1 1
1 0 1 1 1 1 1 ….. 1 1 1 1 1 0 .. 1 1
1 1 0 0 1 1 1 ….. 1 1 1 1 1 ..0.. 1 1
1 1 0 1 1 1 1 ….. 1 1 1 1 1 …0 1 1
1 1 1 0 1 1 1 ….. 1 1 1 1 1 ….. 0 1
1 1 1 1 1 1 1 ….. 1 1 1 1 1 ….. 1 0
9-1 Decoders
The truth table for the 1-to-16 decoder
Enable 1st 74LS138
Enable 2nd 74LS138

## Slide 19
A3 A2 A1 A0
/O0 /O1 /O2 ….. /O6 /O7 /O8 /O9 /O10 .…. /O14 /O15
0 0 0 0 0 1 1 ….. 1 1 1 1 1 ….. 1 1
0 0 0 1 1 0 1 ….. 1 1 1 1 1 ….. 1 1
0 0 1 0 1 1 0 ….. 1 1 1 1 1 ….. 1 1
0 0 1 1 1 1 1 ….. 1 1 1 1 1 ….. 1 1
0 1 0 0 1 1 1 ….. 1 1 1 1 1 ….. 1 1
0 1 0 1 1 1 1 ….. 1 1 1 1 1 ….. 1 1
0 1 1 0 1 1 1 ….. 0 1 1 1 1 ….. 1 1
0 1 1 1 1 1 1 ….. 1 0 1 1 1 ….. 1 1
1 0 0 0 1 1 1 ….. 1 1 0 1 1 ….. 1 1
1 0 0 1 1 1 1 ….. 1 1 1 0 1 ….. 1 1
1 0 1 0 1 1 1 ….. 1 1 1 1 0 ….. 1 1
1 0 1 1 1 1 1 ….. 1 1 1 1 1 ….. 1 1
1 1 0 0 1 1 1 ….. 1 1 1 1 1 ….. 1 1
1 1 0 1 1 1 1 ….. 1 1 1 1 1 ….. 1 1
1 1 1 0 1 1 1 ….. 1 1 1 1 1 ….. 0 1
1 1 1 1 1 1 1 ….. 1 1 1 1 1 ….. 1 0
9-1 Decoders
Write the truth table for the 1-to-16 decoder
A3 can be used to control which 74LS138 is enabled

## Slide 20
/O0 /O1 /O2 /O3 /O4 /O5 /O6 /O7
74LS138
1-of-8 decoder
A0A1 A2
74LS138
1-of-8 decoder
A0A1 A2
/E1/E2 E3
/E1/E2 E3
+5V
A3
A0
A1
A2
/O8 /O9 /O10 /O11 /O12 /O13 /O14 /O 15
0 1 2 3 4 5 6 7
0 1 2 3 4 5 6 7
9-1 Decoders
Draw the circuit for 1-of-16 decoder
A3 = 0 enables the 1st 74LS138
A3 = 1 enables the 2nd 74LS138

## Slide 21: Using four 74LS138 ICs, design a 1-of-32 Decoder
Decoder
.
.
.
A0
O0
O1
O31
5 inputs
32 outputs
A1
A2
A3
A4
9-1 Decoders
(See the data sheet example)

## Slide 22: Truth Table of 1-of-32 decoder
A4 A3 A2 A1 A0
Active output
0 0 0 0 0 /O0
.
.
0 0 1 1 1 /O7
0 1 0 0 0 /O8
.
.
0 1 1 1 1 /O15
1 0 0 0 0 /O16
.
.
1 0 1 1 1 /O23
1 1 0 0 0 /O24
.
.
1 1 1 1 1 /O31
IC1
IC2
IC3
IC4
9-1 Decoders

## Slide 23: Truth Table of 1-of-32 decoder
A4 A3 A2 A1 A0
Active output
0 0 0 0 0 /O0
.
.
0 0 1 1 1 /O7
0 1 0 0 0 /O8
.
.
0 1 1 1 1 /O15
1 0 0 0 0 /O16
.
.
1 0 1 1 1 /O23
1 1 0 0 0 /O24
.
.
1 1 1 1 1 /O31
IC1
IC2
IC3
IC4
9-1 Decoders
A3 and A4 can be used to control which 74LS138 is enabled

## Slide 24: 1-of-32 decoder implementation
74LS138
74LS138
74LS138
74LS138
A0
A1
A2
A3
A4
5V
A0 A1 A2 E
A0 A1A2 E
A0 A1A2 E
A0 A1 A2 E
0 1 2 3 4 5 6 7
0 1 2 3 4 5 6 7
0 1 2 3 4 5 6 7
0 1 2 3 4 5 6 7
Q0 . . . Q7 Q8 . . . Q15 Q16 . . . Q23 Q24 . . . Q31
9-1 Decoders

## Slide 25: Next slide introduces 7442 BCD-to-Decimal Decoder
9-1 Decoders

## Slide 26: 7442 BCD-to-Decimal Decoder
/O9 /O8 /O7 /O6 /O5 /O4 /O3 /O2 /O1 /O0
7442
1-of-10 decoder
A B C D
BCD-to-Decimal decoder is also called:
1-of-10 decoder
4-line to 10-line decoder
9-1 Decoders
Inputs accept BCD code
10 outputs

## Slide 27: Truth Table of BCD-to-Decimal decoder
D C B A
0 0 0 0 /O0 (i.e. all HIGH except /O0)
0 0 0 1 /O1
0 0 1 0 /O2
0 0 1 1 /O3
0 1 0 0 /O4
0 1 0 1 /O5
0 1 1 0 /O6
0 1 1 1 /O7
1 0 0 0 /O8
1 0 0 1 /O9
1 0 1 0 None
1 0 1 1 None
1 1 0 0 None
1 1 0 1 None
1 1 1 0 None
1 1 1 1 None
Active output
9-1 Decoders
Invalid BCD codes, all outputs are HIGH

## Slide 28: Decoder Applications
Used when an output or a group of outputs is to be activated only on the occurrence of a specific combination of input levels.
9-4 Encoders
These inputs often come from the outputs of a counter or a register.
When the decoder inputs come from a counter that is being continually pulsed, the decoder outputs will be activated sequentially, and they can be used as timing signals to turn devices on or off at specific times.

## Slide 29
9-1 Decoders
End of Decoder

## Slide 30
9-4 Encoders
Encode means to give something a code.
To process the real world data in a digital system, the real world data first has to be represented in a way that the digital system can ‘understand’. This step is called ‘encoding’.
An example you definitely can relate to is the keyboard encoder. When we type a letter on the keyboard, the keyboard encoder gives that letter a code that the computer can ‘understand’.
Encoder

## Slide 31
9-1 Decoders
An encoder is a logic circuit that has many inputs. When one input is activated, the outputs will present the code that corresponds to that input.
It’s function is the exact opposite to the decoder.
Encoder

## Slide 32: Encoder – e.g.
Octal-to-Binary
Encoder
O0
O1
O2
8 inputs
only one
ACTIVE
at a time
3-bit
output
code
9-4 Encoders
e.g. when A3 is activated, outputs will be 011
A0
A1
A7
A2
.
.

## Slide 33: Encoder – in general
Encoder
.
.
.
O0
O1
ON-1
M inputs
only one
ACTIVE
at a time
N-bit
output
code
A0
A1
AM-1
.
.
9-4 Encoders

## Slide 34
9-1 Decoders
Let’s examine one encoder example in detail.

## Slide 35: e.g. Octal-to-Binary Encoder (i)
Octal-to-
Binary Encoder
/A0
O0
O1
O2
/A1
/A7
.
.
9-4 Encoders
Octal-to-Binary encoder is also called:
8-line to 3-line encoder

## Slide 36: e.g. Octal-to-Binary Encoder (ii)
The Truth Table
9-4 Encoders
When /A0 is active, or when none is active, the output code is 000
Looking at the logic
x 1 1 1 1 1 1 1 0 0 0
x 0 1 1 1 1 1 1 0 0 1
x 1 0 1 1 1 1 1 0 1 0
x 1 1 0 1 1 1 1 0 1 1
x 1 1 1 0 1 1 1 1 0 0
x 1 1 1 1 0 1 1 1 0 1
x 1 1 1 1 1 0 1 1 1 0
x 1 1 1 1 1 1 0 1 1 1
A0 A1 A2 A3 A4 A5 A6 A7
O2 O1 O0

## Slide 37: e.g. Octal-to-Binary Encoder (iii)
x 1 1 1 1 1 1 1 0 0 0
x 0 1 1 1 1 1 1 0 0 1
x 1 0 1 1 1 1 1 0 1 0
x 1 1 0 1 1 1 1 0 1 1
x 1 1 1 0 1 1 1 1 0 0
x 1 1 1 1 0 1 1 1 0 1
x 1 1 1 1 1 0 1 1 1 0
x 1 1 1 1 1 1 0 1 1 1
The Truth Table
9-4 Encoders
When /A1 is active, the output code is 001
A0 A1 A2 A3 A4 A5 A6 A7
O2 O1 O0

## Slide 38: e.g. Octal-to-Binary Encoder (iv)
The Truth Table
9-4 Encoders
When /A2 is active, the output code is 010
x 1 1 1 1 1 1 1 0 0 0
x 0 1 1 1 1 1 1 0 0 1
x 1 0 1 1 1 1 1 0 1 0
x 1 1 0 1 1 1 1 0 1 1
x 1 1 1 0 1 1 1 1 0 0
x 1 1 1 1 0 1 1 1 0 1
x 1 1 1 1 1 0 1 1 1 0
x 1 1 1 1 1 1 0 1 1 1
A0 A1 A2 A3 A4 A5 A6 A7
O2 O1 O0

## Slide 39: e.g. Octal-to-Binary Encoder (v)
The Truth Table
9-4 Encoders
When /A3 is active, the output code is 011
x 1 1 1 1 1 1 1 0 0 0
x 0 1 1 1 1 1 1 0 0 1
x 1 0 1 1 1 1 1 0 1 0
x 1 1 0 1 1 1 1 0 1 1
x 1 1 1 0 1 1 1 1 0 0
x 1 1 1 1 0 1 1 1 0 1
x 1 1 1 1 1 0 1 1 1 0
x 1 1 1 1 1 1 0 1 1 1
A0 A1 A2 A3 A4 A5 A6 A7
O2 O1 O0

## Slide 40: e.g. Octal-to-Binary Encoder (vi)
The Truth Table
9-4 Encoders
When /A4 is active, the output code is 100.
And so on …
x 1 1 1 1 1 1 1 0 0 0
x 0 1 1 1 1 1 1 0 0 1
x 1 0 1 1 1 1 1 0 1 0
x 1 1 0 1 1 1 1 0 1 1
x 1 1 1 0 1 1 1 1 0 0
x 1 1 1 1 0 1 1 1 0 1
x 1 1 1 1 1 0 1 1 1 0
x 1 1 1 1 1 1 0 1 1 1
A0 A1 A2 A3 A4 A5 A6 A7
O2 O1 O0

## Slide 41: e.g. Octal-to-Binary Encoder (vii)
The Truth Table
9-4 Encoders
Now, try to draw the
encoding circuit.
x 1 1 1 1 1 1 1 0 0 0
x 0 1 1 1 1 1 1 0 0 1
x 1 0 1 1 1 1 1 0 1 0
x 1 1 0 1 1 1 1 0 1 1
x 1 1 1 0 1 1 1 1 0 0
x 1 1 1 1 0 1 1 1 0 1
x 1 1 1 1 1 0 1 1 1 0
x 1 1 1 1 1 1 0 1 1 1
A0 A1 A2 A3 A4 A5 A6 A7
O2 O1 O0

## Slide 42: e.g. Octal-to-Binary Encoder (viii)
A0 A1 A2 A3 A4 A5 A6 A7
x 1 1 1 1 1 1 1 0 0 0
x 0 1 1 1 1 1 1 0 0 1
x 1 0 1 1 1 1 1 0 1 0
x 1 1 0 1 1 1 1 0 1 1
x 1 1 1 0 1 1 1 1 0 0
x 1 1 1 1 0 1 1 1 0 1
x 1 1 1 1 1 0 1 1 1 0
x 1 1 1 1 1 1 0 1 1 1
The Truth Table
9-4 Encoders
From the truth table,
we observe that:
O2=1 when /A4=0 or /A5=0 or /A6=0 or /A7=0
O1=1 when /A2=0 or /A3=0 or /A6=0 or /A7=0
O0=1 when /A1=0 or /A3=0 or /A5=0 or /A7=0
O2 O1 O0

## Slide 43: e.g. Octal-to-Binary Encoder (viii)
9-4 Encoders
From the truth table,
we observe that:
O2=1 when /A4=0 or /A5=0 or /A6=0 or /A7=0
O1=1 when /A2=0 or /A3=0 or /A6=0 or /A7=0
O0=1 when /A1=0 or /A3=0 or /A5=0 or /A7=0
A0 A1 A2 A3 A4 A5 A6 A7
O0
LSB
O1
O2
MSB
The encoding circuit :

## Slide 44: e.g. Octal-to-Binary Encoder (x)
A0 A1 A2 A3 A4 A5 A6 A7
O0
LSB
O1
O2
MSB
9-4 Encoders
What happens when /A3 and /A5 are both LOW?
When /A3 is low, O0 and O1 will be ‘1’. When /A5 is low, O0 and O2 will be ‘1’.
i.e. the outputs will be 111.
The outputs correspond to neither 3 nor 5 !!!

## Slide 45
9-1 Decoders
Problem with simple encoder
Notice that when more than one input is active, the output code will be wrong.
This leads to the design of
priority encoder.

## Slide 46: Priority Encoder
It ensures that when 2 or more inputs are activated, the output code will correspond to the highest-numbered input.
e.g. if /A3 and /A5 are low, the output is 101
9-4 Encoders
74LS148
is an Octal-to-binary priority encoder IC
74LS147
is a Decimal-to-BCD priority encoder IC

## Slide 47: 74LS147 Decimal-to-BCD Priority Encoder
74LS147
Decimal-to-BCD
Priority
Encoder
.
.
.
/A1
/A2
/A8
/A9
/O3
/O2
/O1
/O0
Take note that the outputs are also active LOW.
i.e. Outputs give an inverted BCD.
9-4 Encoders
There are 10 inputs.
All active LOW.

## Slide 48: 74LS147 Decimal-to-BCD Priority Encoder
/A1 /A2 /A3 /A4 /A5 /A6 /A7 /A8 /A9 /O3 /O2 /O1 /O0
1 1 1 1 1 1 1 1 1 1 1 1 1
x x x x x x x x 0 0 1 1 0
x x x x x x x 0 1 0 1 1 1
x x x x x x 0 1 1 1 0 0 0
x x x x x 0 1 1 1 1 0 0 1
x x x x 0 1 1 1 1 1 0 1 0
x x x 0 1 1 1 1 1 1 0 1 1
x x 0 1 1 1 1 1 1 1 1 0 0
x 0 1 1 1 1 1 1 1 1 1 0 1
0 1 1 1 1 1 1 1 1 1 1 1 0
When none of the inputs is active, output is the inverted “0000”
9-4 Encoders
The Truth Table

## Slide 49: 74LS147 Decimal-to-BCD Priority Encoder
/A1 /A2 /A3 /A4 /A5 /A6 /A7 /A8 /A9 /O3 /O2 /O1 /O0
1 1 1 1 1 1 1 1 1 1 1 1 1
x x x x x x x x 0 0 1 1 0
x x x x x x x 0 1 0 1 1 1
x x x x x x 0 1 1 1 0 0 0
x x x x x 0 1 1 1 1 0 0 1
x x x x 0 1 1 1 1 1 0 1 0
x x x 0 1 1 1 1 1 1 0 1 1
x x 0 1 1 1 1 1 1 1 1 0 0
x 0 1 1 1 1 1 1 1 1 1 0 1
0 1 1 1 1 1 1 1 1 1 1 1 0
When /A9 is active, output is the inverted “1001”, regardless of whether the smaller numbered inputs are active.
9-4 Encoders
The Truth Table

## Slide 50: 74LS147 Decimal-to-BCD Priority Encoder
/A1 /A2 /A3 /A4 /A5 /A6 /A7 /A8 /A9 /O3 /O2 /O1 /O0
1 1 1 1 1 1 1 1 1 1 1 1 1
x x x x x x x x 0 0 1 1 0
x x x x x x x 0 1 0 1 1 1
x x x x x x 0 1 1 1 0 0 0
x x x x x 0 1 1 1 1 0 0 1
x x x x 0 1 1 1 1 1 0 1 0
x x x 0 1 1 1 1 1 1 0 1 1
x x 0 1 1 1 1 1 1 1 1 0 0
x 0 1 1 1 1 1 1 1 1 1 0 1
0 1 1 1 1 1 1 1 1 1 1 1 0
When /A8 is active, output is the inverted “1000”, regardless of whether the smaller numbered inputs are active.
9-4 Encoders
The Truth Table

## Slide 51: 74LS147 Decimal-to-BCD Priority Encoder
/A1 /A2 /A3 /A4 /A5 /A6 /A7 /A8 /A9 /O3 /O2 /O1 /O0
1 1 1 1 1 1 1 1 1 1 1 1 1
x x x x x x x x 0 0 1 1 0
x x x x x x x 0 1 0 1 1 1
x x x x x x 0 1 1 1 0 0 0
x x x x x 0 1 1 1 1 0 0 1
x x x x 0 1 1 1 1 1 0 1 0
x x x 0 1 1 1 1 1 1 0 1 1
x x 0 1 1 1 1 1 1 1 1 0 0
x 0 1 1 1 1 1 1 1 1 1 0 1
0 1 1 1 1 1 1 1 1 1 1 1 0
When /A7 is active, output is the inverted “0111”, regardless of whether the smaller numbered inputs are active.
And …
9-4 Encoders
The Truth Table

## Slide 52: 74LS147 Decimal-to-BCD Priority Encoder
/A1 /A2 /A3 /A4 /A5 /A6 /A7 /A8 /A9 /O3 /O2 /O1 /O0
1 1 1 1 1 1 1 1 1 1 1 1 1
x x x x x x x x 0 0 1 1 0
x x x x x x x 0 1 0 1 1 1
x x x x x x 0 1 1 1 0 0 0
x x x x x 0 1 1 1 1 0 0 1
x x x x 0 1 1 1 1 1 0 1 0
x x x 0 1 1 1 1 1 1 0 1 1
x x 0 1 1 1 1 1 1 1 1 0 0
x 0 1 1 1 1 1 1 1 1 1 0 1
0 1 1 1 1 1 1 1 1 1 1 1 0
So, if /A7 and /A8 are LOW, what is the output?
9-4 Encoders
The output will correspond to the highest-numbered input. i.e. the output will be “0111”.

## Slide 53
Design a circuit using 74LS147 to detect the depressing of the number pad (like the one on a calculator). Generate a normal BCD code to show on 4 LEDs.
9-4 Encoders

## Slide 54
74147
Decimal-to-BCD
Priority
Encoder
.
.
.
.
.
/A1
/A8
/A9
/O3
/O2
/O1
/O0
To obtain
Normal
BCD
5V
sw0
sw1
sw8
sw9
9-4 Encoders
Design a circuit using 74LS147 to detect the depressing of the number pad (like the one on a calculator). Generate a normal BCD code to show on 4 LEDs.
Every input is connected to a pull-up resistor. For space constraint, only one is shown.

## Slide 55
74147
Decimal-to-BCD
Priority
Encoder
.
.
.
.
.
/A1
/A8
/A9
/O3
/O2
/O1
/O0
Normal
BCD
5V
sw0
sw1
sw8
sw9
9-4 Encoders
Design a circuit using 74LS147 to detect the depressing of the number pad (like the one on a calculator). Generate a normal BCD code to show on 4 LEDs.
e.g. when sw1 is depressed, /A1 is shorted to ground, thus generating a ‘0’ at the /A1 input.
The outputs after the inverters will be ‘0001’.

## Slide 56
74147
Decimal-to-BCD
Priority
Encoder
.
.
.
.
.
/A1
/A8
/A9
/O3
/O2
/O1
/O0
Normal
BCD
5V
sw0
sw1
sw8
sw9
9-4 Encoders
Design a circuit using 74LS147 to detect the depressing of the number pad (like the one on a calculator). Generate a normal BCD code to show on 4 LEDs.
e.g. when none of the switches is depressed, or when sw0 is depressed, ALL inputs are ‘1’.
The outputs after the inverters will be ‘0000’.

## Slide 57
74147
Decimal-to-BCD
Priority
Encoder
.
.
.
.
.
/A1
/A8
/A9
/O3
/O2
/O1
/O0
Normal
BCD
sw0
sw1
sw8
sw9
5V
9-4 Encoders
Design a circuit using 74LS147 to detect the depressing of the number pad (like the one on a calculator). Generate a normal BCD code to show on 4 LEDs.
When you depress buttons 3 and 6 at the same time on your calculator, what number gets displayed?

## Slide 58
9-4 Encoders
End of Encoder

## Slide 59: Multiplexer (Data Selectors)
A Multiplexer (in short, MUX) has many inputs but only one output.
The MUX selects out of the many inputs, one to be transmitted to the output.
Which input the MUX selects depends on a set of select inputs.
9-6 Multiplexers

## Slide 60: Multiplexer – e.g. 2-input MUX
9-6 Multiplexers
0 I0
1 I1
S
Z
I1
I0
Z
S
2 inputs
1-bit select input
1 output
When S = 0, data at I0 gets transmitted to Z, when S=1, data at I1 gets transmitted to Z

## Slide 61: Multiplexer – in general
SELECT inputs
Output Z
I0
I1
IN-1
A MUX select one
out of N inputs and
transmit it to
the output
9-6 Multiplexers

## Slide 62: Two-input Multiplexer – in detail
9-6 Multiplexers
0 I0
1 I1
S
Z
I1
I0
Z
S
What goes inside this box???

## Slide 63: Two-input Multiplexer
9-6 Multiplexers
0 I0
1 I1
S
Z
I1
I0
Z
S
I0 | I1 | S | Z
2 data inputs and 1 select input

## Slide 64: Two-input Multiplexer
9-6 Multiplexers
0 I0
1 I1
S
Z
I1
I0
Z
S
I0 | I1 | S | Z
 |  | 0 | 
 |  | 0 | 
When S=0, I0 will get transmitted to Z. It is like Z will follow I0.

## Slide 65: Two-input Multiplexer
9-6 Multiplexers
0 I0
1 I1
S
Z
I1
I0
Z
S
I0 | I1 | S | Z
0 | X | 0 | 0
 |  | 0 | 
When S=0, I0 will get transmitted to Z. It is like Z will follow I0.

## Slide 66: Two-input Multiplexer
9-6 Multiplexers
0 I0
1 I1
S
Z
I1
I0
Z
S
I0 | I1 | S | Z
0 | X | 0 | 0
1 | X | 0 | 1
When S=0, I0 will get transmitted to Z. It is like Z will follow I0.

## Slide 67: Two-input Multiplexer
9-6 Multiplexers
0 I0
1 I1
S
Z
I1
I0
Z
S
I0 | I1 | S | Z
0 | X | 0 | 0
1 | X | 0 | 1
 |  | 1 | 
 |  | 1 | 
When S=1, I1 will get transmitted to Z. It is like Z will follow I1.

## Slide 68: Two-input Multiplexer
9-6 Multiplexers
0 I0
1 I1
S
Z
I1
I0
Z
S
I0 | I1 | S | Z
0 | X | 0 | 0
1 | X | 0 | 1
X | 0 | 1 | 0
 |  | 1 | 
When S=1, I1 will get transmitted to Z. It is like Z will follow I1.

## Slide 69: Two-input Multiplexer
9-6 Multiplexers
0 I0
1 I1
S
Z
I1
I0
Z
S
I0 | I1 | S | Z
0 | X | 0 | 0
1 | X | 0 | 1
X | 0 | 1 | 0
X | 1 | 1 | 1
When S=1, I1 will get transmitted to Z. It is like Z will follow I1.

## Slide 70: Two-input Multiplexer
9-6 Multiplexers
0 I0
1 I1
S
Z
I1
I0
Z
S
I0 | I1 | S | Z
0 | X | 0 | 0
1 | X | 0 | 1
X | 0 | 1 | 0
X | 1 | 1 | 1
Z = I0 /S + I1 S
Writing the output expression:

## Slide 71: Two-input Multiplexer
I1
I0
S
Z
0
0
1
0
I0
I0
0 I0
S
Z
9-6 Multiplexers
Z = I0 /S + I1 S
See the data flow in action …

## Slide 72: Two-input Multiplexer
I1
I0
S
Z
0
1
1
0
I1
I1
0 I0
S
Z
9-6 Multiplexers
1 I1
Z = I0 /S + I1 S

## Slide 73
In the next slide, we will see a 4-input multiplexer.
In order to be able to select 1 out of 4 inputs, we need a 2-bit select code.
9-6 Multiplexers

## Slide 74: Four-input Multiplexer
I1
I0
Z
0 0 I0
0 1 I1
1 0 I2
1 1 I3
S1 S0
Z
I2
I3
S0
S1
Z = I0 /S0/S1 + I1 S0/S1 + I2 /S0S1 + I3 S0S1
9-6 Multiplexers
Try to digest this yourself.

## Slide 75: Next slide introduces 8-Input 74LS151 Multiplexer
9-1 Decoders

## Slide 76: 74LS151 Eight-input Multiplexer
Figure 9-22 show internal circuit
8 Data In
I7
I6
I5
I4
I3
I2
I1
I0
Z
74ALS151
MUX
/E
S2
S1
S0
/E S2 S1 S0 Z /Z
X X X 0 1
0 0 0 0 I0 /I0
0 0 0 1 I1 /I1
0 0 1 0 I2 /I2
0 0 1 1 I3 /I3
0 1 0 0 I4 /I4
0 1 0 1 I5 /I5
0 1 1 0 I6 /I6
0 1 1 1 I7 /I7
/Z
9-6 Multiplexers
1 Enable
3 Select Inputs

## Slide 77
Using 74151S, design a 16-input MUX
9-6 Multiplexers

## Slide 78
Using 74151S, design a 16-input MUX
9-6 Multiplexers
Since each 74151 has only 8 inputs, we will need 2 74151.
To be able to select one out of 16 inputs, we need a 4-bit selection code.
We can make use of the ‘/E’ input (as the MSB of the selection code.) In fact ‘/E’ is used to select which 74151 to be enabled.
How many 74151 do we need?
But every 74151 only allow a 3-bit selection code?
How do we select one out of 16 inputs?
Hmm… how do I combine the output from the 2 74151?
Since at any one time, only one 74151 is enabled, we can OR the ‘Z’ from the 2 74151.

## Slide 79
S3
S2
S1
S0
9-6 Multiplexers
Using 74151 ICs, design a 16-input MUX
74151 Mux
I0 I1 I2 I3 I4 I5 I6 I7
Z
74151 Mux
/E
S2
S1
S0
I0 I1 I2 I3 I4 I5 I6 I7 I8I9I10I11I12I13I14I15
X
74151 Mux
I0 I1 I2 I3 I4 I5 I6 I7
Z
74151 Mux
/E
S2
S1
S0
See the solution unfold …

## Slide 80: Next slide introduces 74LS157 Quad 2-Input MUX
9-1 Decoders

## Slide 81: 74LS157 Quad Two-input Multiplexer
Figure 9-24
74LS157 MUX
/E
S
Za Zb Zc Zd
I1a I1b I1c I1d
I0a I0b I0c I0d
/E S Za Zb Zc Zd
1 X 0 0 0 0
0 0 I0a I0b I0c I0d
0 1 I1a I1b I1c I1d
9-6 Multiplexers
Quad means there are 4 MUX (a,b,c,d) in this IC. Each is a 2-input MUX (I0, I1)
The 4 MUX share the same Enable and Select inputs.

## Slide 82: MUX Applications: Data Routing
9-7 Multiplexer Applications
Next, we are going to look at a few MUX applications.
First, Data Routing.
This application example is fully explained in the Text Book.
Imagine we have only 1 display panel, but we want to be able to display data from 2 sources. Let’s see how this can done.

## Slide 83: MUX application: Data Routing
Show how you use 74157 to select which set of BCD counters to display.
BCD counter
BCD counter
CLK#1
BCD counter
BCD counter
CLK#2
BCD to 7-segment decoder
BCD to 7-segment decoder
9-7 Multiplexer Applications

## Slide 84: MUX application: Data Routing
Show how you use 74157 to select which set of BCD counters to display.
BCD counter
BCD counter
CLK#1
BCD counter
BCD counter
CLK#2
BCD to 7-segment decoder
BCD to 7-segment decoder
74ALS157 MUX
74ALS157 MUX
Counter Select
E
S
S
E
I0
9-7 Multiplexer Applications
I1

## Slide 85: MUX application: Data Routing
Show how you use 74157 to select which set of BCD counters to display.
BCD counter
BCD counter
CLK#1
BCD counter
BCD counter
CLK#2
BCD to 7-segment decoder
BCD to 7-segment decoder
74ALS157 MUX
74ALS157 MUX
Counter Select
E
S
S
E
I0
9-7 Multiplexer Applications
I1
When Counter Select = 0, Counter #2 gets displayed.
When Counter Select = 1, Counter #1 gets displayed.

## Slide 86: MUX Applications: Logic Function Generation
9-7 Multiplexer Applications
Another MUX application is Logic Function Generation.
When a function cannot be simplified either algebraically or by K-mapping, the gate implementation would require more ICs.
A more efficient method is to use a multiplexer.

## Slide 87: MUX Applications: Logic Fn Generation
Implement the following logic function
Z = A/B/C + /AB/C + ABC
9-7 Multiplexer Applications
How many ICs would be required if MUX is not used?
I deduce, at least 2.

## Slide 88: MUX Applications: Logic Fn Generation
9-7 Multiplexer Applications
Implement the following logic function
Z = A/B/C + /AB/C + ABC using 74LS151MUX
Watch carefully how this is implemented …

## Slide 89: MUX Applications: Logic Fn Generation
74151 MUX
I0 I1 I2 I3 I4 I5 I6 I7
Z
A
B
C
Z = A/B/C + /AB/C + ABC
E
9-7 Multiplexer Applications
Make sure the IC is enabled.
S0
S1
S2
Label the select inputs. e.g. Do we connect C to S2 or S0 ???
It does not matter, but we do have to make a decision.
The decision will determine how input gets selected.
Take note:

## Slide 90: MUX Applications: Logic Fn Generation
74151 MUX
I0 I1 I2 I3 I4 I5 I6 I7
Z
A
B
C
C B A Z
E
9-7 Multiplexer Applications
Then, we may first fill up the truth table
Z = A/B/C + /AB/C + ABC

## Slide 91: MUX Applications: Logic Fn Generation
74151 MUX
I0 I1 I2 I3 I4 I5 I6 I7
Z
A
B
C
C B A Z
0 0 0 0
0 0 1 1
0 1 0 1
0 1 1 0
1 0 0 0
1 0 1 0
1 1 0 0
1 1 1 1
Z = A/B/C + /AB/C + ABC
E
9-7 Multiplexer Applications
S2 S1 S0
S0
S1
S2
I1
I2
I7

## Slide 92: MUX Applications: Logic Fn Generation
74151 MUX
I0 I1 I2 I3 I4 I5 I6 I7
Z
A
B
C
C B A Z
0 0 0 0
0 0 1 1
0 1 0 1
0 1 1 0
1 0 0 0
1 0 1 0
1 1 0 0
1 1 1 1
Z = A/B/C + /AB/C + ABC
E
5V
9-7 Multiplexer Applications
S2 S1 S0
S0
S1
S2
I1
I2
I7
Connect these inputs to ‘1’ – these that will produce a ‘1’ when selected.

## Slide 93: MUX Applications: Logic Fn Generation
74151 MUX
I0 I1 I2 I3 I4 I5 I6 I7
Z
A
B
C
C B A Z
0 0 0 0
0 0 1 1
0 1 0 1
0 1 1 0
1 0 0 0
1 0 1 0
1 1 0 0
1 1 1 1
Z = A/B/C + /AB/C + ABC
E
5V
9-7 Multiplexer Applications
S2 S1 S0
S0
S1
S2
Connect the rest of the inputs to ‘0’.

## Slide 94: MUX Applications: Logic Fn Generation
74151 MUX
Z
Z = A/B/C + /AB/C + ABC
E
5V
9-7 Multiplexer Applications
This implementationneeds only 1 IC.
A
B
C
I0 I1 I2 I3 I4 I5 I6 I7
S0
S1
S2
E

## Slide 95
(optional) Draw up the truth table
For each product term (which produces a ‘1’), connect corresponding MUX data input to HIGH
(3) Connect remaining MUX inputs to LOW
9-7 Multiplexer Applications
Summary of steps: Expression containing only 3 inputs

## Slide 96
Implement Z = /AB/C + AC + /B using 74LS151 MUX
9-7 Multiplexer Applications
Try another exercise

## Slide 97
Implement Z = /AB/C + AC + /B using 74LS151 MUX
9-7 Multiplexer Applications
C B A Z
0 0 0 1
0 0 1 1
0 1 0 1
0 1 1 0
1 0 0 1
1 0 1 1
1 1 0 0
1 1 1 1
Truth table based on the output expression:

## Slide 98
Implement Z = /AB/C + AC + /B using 74LS151 MUX
9-7 Multiplexer Applications
74151 MUX
I0 I1 I2 I3 I4 I5 I6 I7
Z
A
B
C
E
5V
S0
S1
S2
S2 S1 S0
C B A Z
0 0 0 1
0 0 1 1
0 1 0 1
0 1 1 0
1 0 0 1
1 0 1 1
1 1 0 0
1 1 1 1
Connect the circuit:

## Slide 99
Implement Z = /AB/C+ /A/B/CD + /A/BC/D
using 74151 MUX and inverters
9-7 Multiplexer Applications
Now, there are 4 inputs, A, B, C, and D, but the 74151 has only 3 select inputs? What do we do with the extra input?

## Slide 100
74151 MUX
I0 I1 I2 I3 I4 I5 I6 I7
Z
A
B
C
A B C D Z
Z = /AB/C+ /A/B/CD + /A/BC/D
9-7 Multiplexer Applications
S2
S1
S0
Decide to use ABC as select inputs, label them!
Enable the IC.
E
S2 S1 S0

## Slide 101
74151 MUX
I0 I1 I2 I3 I4 I5 I6 I7
Z
A
B
C
A B C D Z
0 0 0 0 0
0 0 0 1 1
0 0 1 0 1
0 0 1 1 0
0 1 0 0 1
0 1 0 1 1
0 1 1 0 0
0 1 1 1 0
1 0 0 0 0
1 0 0 1 0
1 0 1 0 0
1 0 1 1 0
1 1 0 0 0
1 1 0 1 0
1 1 1 0 0
1 1 1 1 0
E
Z = /AB/C+ /A/B/CD + /A/BC/D
9-7 Multiplexer Applications
S2
S1
S0
I0
I1
I2
S2 S1 S0
Drawing up the truth table is optional.

## Slide 102
74151 MUX
Z
E
5V
9-7 Multiplexer Applications
Z = /AB/C+ /A/B/CD + /A/BC/D
I0 I1 I2 I3 I4 I5 I6 I7
S0
S1
S2
C
B
A
A B C D Z
0 0 0 0 0
0 0 0 1 1
0 0 1 0 1
0 0 1 1 0
0 1 0 0 1
0 1 0 1 1
0 1 1 0 0
0 1 1 1 0
1 0 0 0 0
1 0 0 1 0
1 0 1 0 0
1 0 1 1 0
1 1 0 0 0
1 1 0 1 0
1 1 1 0 0
1 1 1 1 0
Term containing only ABC. /AB/C corresponds to ‘010’, this selects I2. Connect it to ‘1’.
S2 S1 S0
I0
I1
I2

## Slide 103
74151 MUX
Z
E
5V
D
9-7 Multiplexer Applications
Z = /AB/C+ /A/B/CD + /A/BC/D
I0 I1 I2 I3 I4 I5 I6 I7
S0
S1
S2
C
B
A
A B C D Z
0 0 0 0 0
0 0 0 1 1
0 0 1 0 1
0 0 1 1 0
0 1 0 0 1
0 1 0 1 1
0 1 1 0 0
0 1 1 1 0
1 0 0 0 0
1 0 0 1 0
1 0 1 0 0
1 0 1 1 0
1 1 0 0 0
1 1 0 1 0
1 1 1 0 0
1 1 1 1 0
Term containing D. /A/B/C corresponds to ‘000’, this selects I0. Connect it to ‘D’
S2 S1 S0
I0
I1
I2

## Slide 104
74151 MUX
Z
E
5V
D
9-7 Multiplexer Applications
Z = /AB/C+ /A/B/CD + /A/BC/D
I0 I1 I2 I3 I4 I5 I6 I7
S0
S1
S2
C
B
A
A B C D Z
0 0 0 0 0
0 0 0 1 1
0 0 1 0 1
0 0 1 1 0
0 1 0 0 1
0 1 0 1 1
0 1 1 0 0
0 1 1 1 0
1 0 0 0 0
1 0 0 1 0
1 0 1 0 0
1 0 1 1 0
1 1 0 0 0
1 1 0 1 0
1 1 1 0 0
1 1 1 1 0
Term containing /D. /A/BC corresponds to ‘001’, this selects I1. Connect it to ‘/D’
S2 S1 S0
I0
I1
I2

## Slide 105
74151 MUX
Z
E
5V
D
9-7 Multiplexer Applications
Z = /AB/C+ /A/B/CD + /A/BC/D
I0 I1 I2 I3 I4 I5 I6 I7
S0
S1
S2
C
B
A
A B C D Z
0 0 0 0 0
0 0 0 1 1
0 0 1 0 1
0 0 1 1 0
0 1 0 0 1
0 1 0 1 1
0 1 1 0 0
0 1 1 1 0
1 0 0 0 0
1 0 0 1 0
1 0 1 0 0
1 0 1 1 0
1 1 0 0 0
1 1 0 1 0
1 1 1 0 0
1 1 1 1 0
Connect the rest to ‘0’
S2 S1 S0

## Slide 106
(optional) Draw up the truth table - if you choose ABC as
select inputs, then use D as the extra input.
(2) Terms containing ONLY A,B,C - connect corresponding MUX data input to HIGH
(3) Terms that also contain D variable – connect the D or /D variable to the MUX input that corresponds to the ABC variable
(4) Connect remaining MUX inputs to LOW
9-7 Multiplexer Applications
Summary of steps: Expression containing 4 inputs

## Slide 107
End of MUX
9-7 Multiplexer Applications

## Slide 108: Demultiplexer (Data Distributor)
A Demultiplexer (in short, DEMUX) has only one input but many outputs. The input data gets transmitted to one of the outputs.
To which output the input data gets transmitted depends on a set of select inputs.
DEMUX’s function is the exact opposite to the MUX’s.
9-6 Multiplexers

## Slide 109: Demultiplexer (Data Distributors)
SELECT inputs
Data Input
O0
O1
ON-1
A DEMUX distribute data to one of several destinations
9-8 Demultiplexer

## Slide 110: Demux e.g. 1-line-to-8-line Demux
9-8 Demultiplexer

## Slide 111: 1-line-to-8-line Demux
O0 = I . /S2/S1/S0
O1 = I . /S2/S1S0
O2 = I . /S2S1/S0
O3 = I . /S2S1S0
O4 = I . S2/S1/S0
O5 = I . S2/S1S0
O6 = I . S2S1/S0
O7 = I . S2S1S0
S0
S1
S2
/S0
/ S1
/ S2
Data Input
I
9-8 Demultiplexer

## Slide 112: Demux e.g. 1-line-to-8-line Demux
O0 = I when select inputs = 000
The rest of the outputs = 0
S0
S1
S2
/S0
/S1
/S2
data input I
9-8 Demultiplexer

## Slide 113: Demux e.g. 1-line-to-8-line Demux
O1 = I when select inputs = 001
The rest of the outputs = 0
S0
S1
S2
/S0
/S1
/S2
data input I
9-8 Demultiplexer

## Slide 114: Demux e.g. 1-line-to-8-line Demux
O2 = I when select inputs = 010
The rest of the outputs = 0
S0
S1
S2
/S0
/S1
/S2
data input I
9-8 Demultiplexer
and so on …

## Slide 115: 1-line-to-8-line Demux Truth Table
S2 S1 S0 O7 O6 O5 O4 O3 O2 O1 O0
0 0 0 0 0 0 0 0 0 0 I
0 0 1 0 0 0 0 0 0 I 0
0 1 0 0 0 0 0 0 I 0 0
0 1 1 0 0 0 0 I 0 0 0
1 0 0 0 0 0 I 0 0 0 0
1 0 1 0 0 I 0 0 0 0 0
1 1 0 0 I 0 0 0 0 0 0
1 1 1 I 0 0 0 0 0 0 0
9-8 Demultiplexer

## Slide 116: Demux – using a Decoder to implement
Draw the waveform at all the outputs when
A2 A1 A0 = 000, what can you conclude?
/E1 (I)
9-8 Demultiplexer
I
/E1 /E2 E3
/O7 /O6 /O5 /O4 /O3 /O2 /O1 /O0
74LS138
1-of-8 decoder
A2 A1A0
5V
Input data I is connected to /E1. When I=0, the decoder is enabled. Since input code is ‘000’. Output /O0 will be ‘0’. Whereas when I=1, the decoder is disabled. All outputs including /O0 will be ‘1’.

## Slide 117: Demux – using a Decoder to implement
/O0
/E1 (I)
9-8 Demultiplexer
Draw the waveform at all the outputs when
A2 A1 A0 = 000, what can you conclude?
This is like /O0 is following I
/E1 /E2 E3
/O7 /O6 /O5 /O4 /O3 /O2 /O1 /O0
74LS138
1-of-8 decoder
A2 A1 A0
5V
I

## Slide 118: Demux – using a Decoder to implement
/O0
/O1 -- /O7
‘1’
/E1 (I)
9-8 Demultiplexer
Draw the waveform at all the outputs when
A2 A1 A0 = 000, what can you conclude?
We see that A2A1A0 become the select inputs of the Demux. When selection code is ‘000’, input data I gets transmitted to output /O0. The rest of the outputs stay at ‘1’
/E1 /E2 E3
/O7 /O6 /O5 /O4 /O3 /O2 /O1 /O0
74LS138
1-of-8 decoder
A2 A1 A0
5V
I

## Slide 119: Application of DeMUX
Clock Demultiplexer -- Figure 9-31
Security Monitoring System -- Figure 9-32
Synchronous Data Transmission System
-- Figure 9-33
9-8 Demultiplexer
These application examples are for self-study.

## Slide 120
End of Demultiplexer
9-8 Demultiplexer

## Slide 121
End of MSI Logic Circuits