## Slide 1: DIGITAL SIGNAL PROCESSING Chapter 4
EEE DSP Teaching Team
Notes: Digital Signal processing chapter 4

## Slide 2: Interpret digital signals and systems mathematically.
At the end of this chapter, students should:
Give examples of discrete-time signals and how they can be represented.
Explain how difference equations are used to model digital systems.
Explain how digital networks are used to describe difference equations.
Summarize the concepts of linearity and time-invariance.
Notes: In this Chapter, we will learn how discrete-time signals be represented
Using difference equations to model digital systems
And digital systems to describe difference equations
Concepts of linearity and time invariance are also explained

## Slide 3: Signals in time domain
Mathematical representation of signals provides a common language in engineering.
Consider a continuous-time signal given by:
f = 1 kHz
0
0.5
1
-1
-0.5
0
0.5
1
x(t)
t(ms)
Notes: This is a normal sinewave with 1 kilo hertz frequency
Period, T = 1/f =1/1000= 1 milli second
It means that the sine wave repeats itself every 1 milli second

## Slide 4: Discrete-time signals
If this signal is sampled at fs = 8000Hz, we have:
0
0.125
0.25
0.375
0.5
0.625
0.75
0.875
1
-1
-0.5
0
0.5
1
t(ms)
x(nT)
Ts=1/8000=0.125msec
0x0.125msec
1x0.125msec
2x0.125msec
3x0.125msec ….
Notes: Sampling frequency is 8 kilo hertz
The number of samples per cycle, n = fs/finput
Since the analog signal frequency is 1 kilo hertz and the number of sample is 8/1 = 8
The first sample is at time 0 millisecond and we denote the amplitude as x(0)
The second sample is at time 0.125 millisecond and we denote the amplitude as x(1)
The third sample is at time 0.25 millisecond and amplitude x(2) and so for

## Slide 5: Discrete-time signals
For discrete-time signals, we are only interested in the sequence of samples.
As such, we usually normalize the time axis.
0
1
2
3
4
5
6
7
8
-1
-0.5
0
0.5
1
n
x(n)
x(0)
x(1)
x(7)
Notes: Now we remove the time information and replace it with n which is an integer value from 0, 1, 2 and so for
x(0) is the amplitude of the signal at time t=0
x(1.5) is undefined and x(4) is 0

## Slide 6: Discrete-time signals
Mathematically, we denote the sampling process by substituting t  nT.
T = sampling time interval =
n = integral time index
x(t) = sin 2ft
after sampling
x(nT) = sin 2fnTs (n=0,1,2…)
Notes: Here we see that t is being replaced by nT
This is the sampling process where t is continuous and nT is discrete
Ts will be removed as it is understood that n is followed by Ts

## Slide 7: Discrete-time signals
We define
known as normalized angular frequency
We can denote discrete-time signal as:
x(n) = sin 2fnT = sin n
We can also show same discrete-time signal as a sequence of numbers:
x(n) = {0.0, 0.7, 1.0, 0.7, 0.0 –0.7, –1.0, …}
n=0
n=1
n=2
………..x (0) =0.0, x(1)=0.7,x(2)=1.0
Notes: Omega is known as normalized angular frequency where fs is the sampling frequencyHence x n is now sine omega nX n is a single array of discrete time signal of a sequence of discretized time signals from n = 0, 1, 2, 3 and so for

## Slide 8: Examples of discrete-time signals
Unit sample sequence (unit impulse)
Unit step sequence
Notes: These are two very important definitions – unit sample sequence and unit step sequence.
The amplitude is one
For unit sample sequence or unit impulse has the value of 1 when n=0 and 0 for any other value of n
For unit step sequence, notice it is a step! It has value of 1 only when n = 0 or positive

## Slide 9: Examples of discrete-time signals
Sinusoidal sequence
Exponential sequence
Notes: These are two common discrete-time sequences: exponential and sinusoidal sequences

## Slide 10: Causal/non-causal sequence
Causal (right handed) sequence | Non-causal (left handed) sequence
Two sided sequence | A causal sine wave
Unless otherwise stated, remainder of this course we will use causal signals!
Notes: A system is said to be causal if the output of the system at any time ‘n’ depends only on present and past inputs, but does not depend on future inputs.
If a system does not satisfy this definition, it is called noncausal. Such a system has an output that depends not only on present and past inputs but also on future inputs.
Notice that the non casual system take the value of negative values for n

## Slide 11: Examples to discrete-time signals
Discrete time sequence x(n) in array form:
  x(n)={1,1.5, 0, -1.5, -1}
As combination of unit impulse function:
x(n)=(n) + 1.5(n – 1) – 1.5(n – 3) – (n –4)
A plot of the signal :
-2
0
2
4
6
8
-2
0
2
d
(n) + 1.5
d
(n - 1) - 1.5
d
(n - 3) -
d
(n - 4)
n
Notes: The one-dimensional array, x(n) has 5 elements.
The plot is shown in discrete time format, there is not values for n more than 4 that is (n –5) is 0 onwards

## Slide 12: Examples of discrete-time signals
Combination of unit step function:
x(n)=u(n) – u(n – 5)
n=0, x(0) = u(0) – u(0 - 5) = u(0) – u(-5)=1 – 0 = 1
n=5, x(5) = u(5) – u(5 - 5) = u(5)-u(0)= 1 -1 =0
u(5)=0
Notes: There are two unit step functions, u(n) and u(n-5)
You can draw the two step functions separately and subtract them.

## Slide 13: Examples of discrete-time signals
u(n)
u(n – 5)
x(n)= u(n)-u(n – 5)
=[1,1,1,1,1]
Notes: Using graphical approach, we can get similar result, shown in RED

## Slide 14: Examples of discrete-time signals
Causal sinusoidal function:
y(n) = cos 0(n – 2)u(n – 2)
Notes: y(n) will only have two sequences, cos w0(n-2) and u(n-2)
Notice that the resulted sequence, y(n) is zero for n less than 2

## Slide 15: Discrete-time systems
x(n) y(n)
The output of the system, y(n), is usually a linear function of the input of the system, x(n).
i.e. y(n) = f { x(n) }
system
Notes: A system is a group of elements that transforms the input signals into new or different signals at the output. In other words, a system takes an input signal, x, modifies or manipulates it according to what it has been designed for, and produces a corresponding output signal, y.
The system can be a filter – low pass, high pass or band pass filter

## Slide 16: Difference equation
The relationship between x(n) and y(n) is usually in the form of:
y(n) = b0x(n) + b1x(n – 1) + b2x(n – 2) + ….
+ a1y(n – 1) + a2y(n – 2) + ….
b0, b1, b2, …. and a1, a2, …. are constants.
The above equation is called the difference equation.
Notes: Difference equation, mathematical involving the differences between successive values of a function of a discrete variable.
The above equation is called the difference equation which gives the relationship between the output, y(n), and input, x(n)
Once the a and b coefficients are known, the output of the system, y(n), can be computed for any input, x(n).
a and b coefficients determine the characteristics of the discrete-time system.

## Slide 17: Difference equation
If a and b coefficients are known, the output of the system, y(n), can be computed for any input, x(n).
These a and b coefficients determine the characteristics of the discrete-time system.
  such as low pass filter, high pass filter etc.
Notes: x(n) is input
x(n) went through the system
y(n) is output
a and b coefficients define what kind of system

## Slide 18: Example – difference equation
Given that output, y(n) = 0.5x(n) + 0.5x(n – 1), compute y(n) when input, x(n) = d(n) + 2d(n – 1).
-1
0
1
2
0
1
2
n
x(n)
When n = 0, y(0) = 0.5x(0) + 0.5x(–1)
= 0.5(1) + 0.5(0) = 0.5
When n = 1, y(1) = 0.5x(1) + 0.5x(0)
= 0.5(2) + 0.5(1) = 1.5
When n = 2, y(2) = 0.5x(2) + 0.5x(1)
= 0.5(0) + 0.5(2) = 1
When n = 2, y(2) = 0.5x(2) + 0.5x(1)
= 0.5(0) + 0.5(2) = 1
y(0)=0.5
y(1)=1.5
y(2)=1
y(3)=0
x(0)=1
x(0)= d(0) + 2d(0 – 1)=1
Notes: The signal, x(n) is input to the system and the output of the system may be computed iteratively for all the values of n starting with n = 0, then 1, 2 and 3

## Slide 19: Example – difference equation
Output sequence:
y(n) = 0.5d(n) + 1.5d(n – 1) + d(n – 2)
-1
0
1
2
3
0
1
2
n
y(n)
Notes: When n = 0, y(0) = 0.5x(0) + 0.5x(–1) = 0.5 × 1 + 0.5 × 0 = 0.5
When n = 1, y(1) = 0.5x(1) + 0.5x(0) = 0.5 × 2 + 0.5 × 1 = 1.5
When n = 2, y(2) = 0.5x(2) + 0.5x(1) = 0.5 × 0 + 0.5 × 2 = 1
When n = 3, y(3) = 0.5x(3) + 0.5x(2) = 0.5 × 0 + 0.5 × 0 = 0

## Slide 20: Example – difference equation
Alternative method:
(if there is no feedback!)
y(n) = 0.5x(n) + 0.5x(n – 1)
= 0.5 {d(n) + 2d(n – 1)} + 0.5 {d(n – 1) + 2d(n – 2)}
= 0.5d(n) + 1.5d(n – 1) + d(n – 2)
x(n)= d(n) + 2 d(n – 1)
x(n-1)= d(n-1) + 2 d(n – 2)
Notes: We can use the mathematical approach.
There is no feedback that is y(n-1) y(n-2) and so for

## Slide 21: Digital networks
Difference equation is made up of 3 basic mathematical operation:
  Multiplication
  Addition
  Delay
y(n) = a0x(n) + a1x(n – 1) + a2x(n – 2) + ….
Multiplication
Delay
Addition
Notes: the difference equation is used to describe the relationship between the output and the input of a system. It is noted that the difference equation is made up of three basic mathematical operations, namely addition, multiplication and delay
Addition, the signals are added
Multiplication, the amplitude of the signal is magnified
Delay, the signal is delayed in discrete time

## Slide 22: Digital network
Digital network shows difference equation in a diagrammatic form.
There are three basic components in digital networks:
  Multiplier
  Adder
  Delay
x(n) kx(n)
k
x(n) x(n)+y(n)
y(n)
x(n) x(n-1)
z-1
Notes: The 3 symbols of multiplication, addition and delay are shown .
For addition, there are two input signals while the other two are just one input and one output signal

## Slide 23: Terminology
Linear system:
A system which obeys the principle of superposition.
Time invariant system:
A system which does not change with time.
Notes: Two important concepts, linear and time invariant
If both are combined, we called LTI (Linear Time Invariant) system

## Slide 24: Linear system
If y3(n) = ay1(n) + by2(n), this is a linear system.
If y3(n)  ay1(n) + by2(n), this is a non-linear system.
System
Notes: For linear system, if the input is multiplied by a factor, a x(n) the output will also increased by the similar proportion a y(n)

## Slide 25: Time-invariant system
If y1(n) = y(n – m), this is a time-invariant system.
If y1(n)  y(n – m), this is not a time-invariant system.
System
Notes: A system is identified as time-invariant if the system characteristics does not change with time. Assume a system in Figure 2.19 outputs y(n) when x(n) is applied to it. We can conclude that system is time-invariant, when a time-shifted version of x(n) is applied, it produces an output which is a time-shifted version of y(n).
A time-invariant system has a time-dependent system function that is not a direct function of time.
A few examples will help to understand

## Slide 26: Summary
Through sampling, discrete time signals can be derived form the continuous time signals.
Difference equations can be used to model digital systems.
From digital networks, difference equations can be obtained.
There are feed forward and feedback loops for digital systems and these are denoted by x(n-m) an y(n-m).
Linear and Time Invariant are also be used to perform on discrete time signals
Notes: In conclusion, we have learn how to obtain discrete time signals through sampling of continuous time signals.
Difference equations can be used to model digital systems
Difference equations can also be obtained from digital networks.
There are basically two types of loops, feed forward and feedback loops
Two very important properties, linear and time invariant concepts are also highlighted and simple examples shown to illustrate the concepts