## Slide 1: DIGITAL SIGNAL PROCESSING Chapter 5
EEE DSP Teaching Team
Notes: Digital Signal Processing Chapter 5

## Slide 2: Understand the analytical tools used in time-domain analysis of digital systems.
At the end of this chapter, students should:
Deduce how impulse response can be obtained in a digital system.
Define discrete linear convolution and explain its properties.
Notes: In this Chapter, it covers the following :
How impulse response can be obtained in a digital system
What is discrete linear convolution
Correlation
Cross correlation
And autocorrelation

## Slide 3: Impulse response
Output response of a system when subjected to a unit impulse input.
Delivers characteristics of the system.
Spectral analysis of the impulse response shows the frequency characteristics of the system.
It is a useful tool for analysing systems
Notes: If the input x(n) is an unit impulse and the output y(n) is called the impulse response or also denoted by h(n)
The impulse response is very useful as it provides information about the characteristics of the digital system.

## Slide 4: Impulse response
System
0
(n)
Impulse response, h(n)
0
2
4
x(n)
y(n)
Notes: Here the impulse response h(n) shoes an exponential decline output.
As n increase, the amplitude of the h(n) decreases and ultimately to zero
We term this system as stable

## Slide 5: Example 1 – impulse response
Find the impulse response of the following system:
From the earlier example, we have
y(n) = x(n) + 0.5y(n – 1)
z-1
x(n)
y(n)
0.5
Notes: Another example here, where x(n) is delta n, impulse unit
There is only one value 1 when n is equal to 1
The rest of the input values will be zero

## Slide 6: Example 1 – impulse response
Input x(n) = (n), or x(n)={1 0 0 0 0 0….}
Assume that y(n) = 0 for n < 0.
When n = 0, y(0) = x(0) + 0.5y(–1) = 1 + 0 = 1
When n = 1, y(1) = x(1) + 0.5y(0) = 0 + 0.51 = 0.5
When n = 2, y(2) = x(2) + 0.5y(1) = 0 + 0.50.5 = 0.25
When n = 3, y(3) = x(3) + 0.5y(2) = 0 + 0.50.25 = 0.125
and so on.
Notes: This is shown by the array of x(n) where the first term is 1 followed by zeroes
It also means that x(0) = 1 and the rest of the x values are zero
Carrying out the equation, y(0) is 1 and y(1) is 0.5 and so for
The amplitude of y(n) decreases as n increases

## Slide 7: Example 1 – impulse response
Hence, the impulse response is:
-1
0
1
2
3
4
5
0
0.5
1
1.5
n
h(n)
Impulse response
y(n) = h(n)={1,0.5,0.25,0.125,…}
Notes: The value of y(n) decreases….

## Slide 8: Discrete linear convolution
In many applications, the output is calculated using the input and the impulse response of the system.
System
h(n)
x(n)
y(n)
Notes: For a linear, time-invariant system, the relationship between the output of the system, its input and its impulse response can be described by a discrete linear convolution function:

## Slide 9: Discrete linear convolution
The input/output relationship is given by:
where the symbol * denotes linear convolution.
The definition of discrete linear convolution is given by the right hand side of the above equation.
Notes: Discrete linear convolution can be described by the above function
.
Linear convolution is a mathematical operation.
It is NOT multiplication

## Slide 10: Example 2 - convolution
Find the output, y(n), of a system whose impulse response is:
h(n) = 0.5d(n) + 0.5d(n – 1)
and the input is:
x(n) = d(n) + d(n – 1) + 0.5d(n – 2).
Notes: We have two sequences, h(n) and x(n)
We are going to perform a linear convolution between these two sequences

## Slide 11: Quiz
h(n) = 0.5d(n) + 0.5d(n – 1)
Select the correct representation.
a) h(n) ={0, 0.5,0.5, 0}
b) h(n) ={ 0.5,0.5, 0, 0}
c) h(n) ={0.5, 0, 0, 0}
d) h(n) ={0, 0, 0, 0}
Notes: Answer b

## Slide 12: Quiz
x(n) = d(n) + d(n – 1) + 0.5d(n – 2)
Select the correct representation.
a) x(n) ={0, 1, 1, 0.5, 0}
b) x(n) ={0, 1, 1, 0, 0}
c) x(n) ={1, 1, 0.5, 0, 0}
d) x(n) ={0, 0, 0, 0, 0}
Notes: Answer c

## Slide 13: Example - convolution
To find y(n), we evaluate:
for every value of n.
We can do that graphically:
Notes: We shall calculate the output signal by using the definition of convolution and visualizing the steps of the operation graphically. Each value of can be found by multiplying with point by point at the corresponding time bins and then taking the summation of the result for the entire time axis from positive infinity to negative infinity .

## Slide 14: Evaluation of convolution
When n = 0,
Notes: We begin our calculation with n = 0, which gives the x(0-k). Here implies a mirror image of at negative time axis by flipping the x(k) over the y axis and perform the multiplication between h(k) and x(0-k) term by term to obtain the product on the right of the slides and obtain the summation of all the amplitudes to give y(0)

## Slide 15: Evaluation of convolution
When n = 1,
Notes: for n = 1, we have x(0-k) to be shifted by one sample or unit time delay . It implies that is shifted towards the positive time axis right by one sample.
Perform the multiplication of x(1-k) and h(k) and sum up the values of the amplitudes of the products to give y(1)

## Slide 16: Evaluation of convolution
When n = 2,
Notes: Similarly we perform another shift right for x(1-k) to obtain x(2-k) and the rest is similar to the previous slides to get y(2)

## Slide 17: Evaluation of convolution
When n = 3,
Notes: Same for n=3 and y(3)

## Slide 18: Evaluation of convolution
When n = 4,
Notes: Continue with n=4 and y(4) is zero as there is no overlapping between h(k) and x(4-k) and their products of the amplitudes at each n will result in zero values

## Slide 19: Evaluation of convolution
Hence, the output, y(n), is:
Notes: Finally, the final result y(n) is obtained.
y(0) =0.5
Y(1)=1
Y(2)=0.75
Y(3)=0.25

## Slide 20: Evaluation of convolution
The length of the sequence y(n) is not equal to length of x(n) or h(n).
if Ny is the length of y(n)
Nx is the length of x(n)
Nh is the length of h(n)
then Ny = Nx + Nh – 1.
Notes: We can also when to stop computing for which n value.
In the above example, Nx = 2 and Nh = 3, so Ny = 2+3 -1 =4

## Slide 21: Properties of convolution
Commutative
h(n) * x(n) = x(n) * h(n)
Linear
h(n) * { x1(n) + x2(n) } = h(n) * x1(n) + h(n) * x2(n)
Time invariant
If h(n) * x(n) = y(n), then h(n – m) * x(n) = y(n – m)
Integral property of impulse function
h(n) * (n) = h(n)
Notes: Convolution is commutative and linear time invariant.
These are very useful properties to help us find the linear convolution of two functions

## Slide 22: Properties of convolution
With the help of the above properties, we are able to compute the convolution without using the graphical approach.
Notes: The properties also provide another way to compute the linear convolution between two functions non graphically.

## Slide 23: Example
Given h(n) = 0.5(n) + 0.5(n – 1) and
x(n) = (n) + (n – 1) + 0.5(n – 2),
find y(n) = h(n) * x(n)
We have
y(n) = h(n) * x(n)
= h(n) * { (n) + (n – 1) + 0.5(n – 2) }
= h(n) * (n) + h(n) * (n – 1)
+ h(n) * 0.5(n – 2)
 Linear property
Notes: The two functions , h(n) and x(n) are given.
We are to perform the linear convolution of these two functions non-graphically

## Slide 24: Example
y(n)= h(n) * (n) + h(n) * (n – 1) + h(n) * 0.5(n – 2)
y(n) = h(n) + h(n – 1) + 0.5h(n – 2)
= {0.5(n) + 0.5(n – 1) }
+ { 0.5(n – 1) + 0.5(n – 2) }
+ { 0.25(n – 2) + 0.25(n – 3) }
= 0.5(n) + (n – 1) + 0.75(n – 2)
+ 0.25(n – 3)
 time invariant and integral property of impulse function
Notes: We uses the properties time invariant and also the integral property of the impulse function for each term of x(n)
And carry out the 3 steps for x(n) equals delta n, delta n-1 and delta n-2
Next we at up the various coefficients for each x(n-m) coefficients

## Slide 25: Discrete-Time Convolution Example
x[n]  [1 4 -2]
h[n]  [0 1 3]
_______________
0 0 0 First Row times (0)
1 4 -2 First Row times (1)
3 12 -6 First Row times (3)
------------------------------
0 1 7 10 -6 Summation of columns
Notes: Another way is to use the “slide rule” method.
The first row is obtained by multiplying 1 4 -2 with the first value of h(n) which is 0. Hence we obtained 0 0 0
The second row is computed by multiplying 1 4 -2 with the second value of h(n) which is 1. Note that the output value is also shifted and we obtained 1 4 -2
The last row 1 4 -2 with 3 and we get 3 12 -6
Summing up all the columns we obtained the linear convolution result, y(n) = 0 1 7 10 -6

## Slide 26: Combination of systems
h(n)=h1(n)*h2(n)
h(n)=h1(n)+h2(n)
Notes: Systems can be combined in series and parallel
For series, the individual systems are convoluted with each other
For parallel connection, they are added up

## Slide 27: Quiz
Given the following system where h1(n) ={1,2} and h2(n)={3,4}, find h(n).
a) h(n) ={1,2,3,4}
b) h(n) ={4,3,2,1}
c) h(n) ={4,6}
d) h(n) ={6,4}
Notes: Answer c

## Slide 28: Quiz
Given the following system where h1(n) ={1,4,-2} and h2(n)={0,1,3}, find h(n).
a) h(n) ={0,1,7,10,-6}
b) h(n) ={1,4,-2,0,1,3}
c) h(n) ={4,6}
d) h(n) ={0,0,0,0,0}
Notes: Answer a, h1(n) *h2(n)

## Slide 29: Example
h(n)={h1(n)+h3(n))*(h2(n)+h4(n)) *h5(n)
Notes: There are two parallel systems connected in series with one h5(n)

## Slide 30: Deconvolution
The reverse operation of convolution is known as deconvolution.
An unknown input signal, x(n),can be determined from impulse response, h(n), and the output signal, y(n).
In most cases we are interested in positive time axis hence:
Notes: For linear convolution, we obtain y(n) with known h(n) and x(n). By doing deconvolution the reverse operation of convolution , iIt is possible to determine an unknown input signal, x(n), if the impulse response of the system, h(n), and the output signal, y(n), are known.

## Slide 31: Deconvolution
By rearranging we have
for n=0, x(0)
and for n>0
Notes: The steps of the deconvolution are given in these few slides starting from n=0

## Slide 32: Example
Find x(n), if and
Solution:
We start with n=0
for n=1
Notes: Applying the procedure starting from n=0, we obtain the value of x(0) = 1
And for n=1, x(1) = 1

## Slide 33: Example
n=2
n=3
….
x(n)={1,1,0.5,0,0….}
Notes: Similar, n= 2 x(2)= 0.5 and n=3, x(3) = 0
The length of Ny is 4 and Nh is 2
So Nx= 4-2+1=3
You can stop at n=3
Note that all the above apply for feed forward systems that is x(n-m)
There is no y(n-m) feedback difference equations for the linear convolution and deconvolution

## Slide 34: Correlation
In many applications, it is necessary to establish the similarity or interdependence between signals.
Correlation is used to measure the degree of similarity between two signals.
It is often used to detect
  a known waveform in a noisy background,
  to detect periodicity,
  to measure delays.
Notes: In many applications, it is necessary to establish the similarity or interdependence between signals.
Correlation, similar to convolution, is a mathematical operation that is used to measure the degree of similarity between two signals.
It is also often used to detect a known waveform in a noisy background, or to detect periodicity of a signal, or to measure delays between two signals. For example, a radar system sends out a short pulse of electromagnetic energy. Objects along the path of the transmitted pulse will cause some of the energy to be reflected back to the system. This reflected signal is a time-shifted and scaled version of the transmitted waveform, plus some random noises. Hence, the distance from the radar to the object can be determined by simply measuring the time delay between the signals sent and received.

## Slide 35: Correlation
The mathematical definition of correlation is given as:
R12=0.5x0.5+1X1+1X1=2.25
R12=0.5x0.5+1X0.5+1X0.5=1.25
R12=2.25
R12=1.25
Good correlation
Not so good correlation
Notes: Two signals x1(n) and x2(n)
Multiplying the individual amplitude n values that is x1(0) with x2(0) and so for
We obtain the correlation value for the two sequences.
The higher values will show the good correlation

## Slide 36: Cross-correlation
In some cases, signals may be highly correlated but out of phase which produce a poor result.
To over come this, one of the signal is kept stationary and the other one is shifted in time axis as in convolution.
Hence, cross correlation defined as:
Notes: For cases, where the one of the sequences may be one-sample time-shift and when performing the correlation it yields poor result.
Hence we use another operation called cross correlation

## Slide 37: Example
Calculate the cross correlation of
x1(n)=[1 0 1 2 2 1] and x2(n) = [2 2 1]
x2(0)=2; x2(1)=2; x2(2)=0
Notes: The cross correlation is quite similar to convolution and the two signals are multiplied together sample by sample and then summed.
r12(m) is called the cross-correlation. It indicates the correlation between two signals as a function of position.
You can use the graphical approach similar to linear convolution except the following.
If j = - 2, then, then x2(n+2) is a x2(n) shifted to left by 2-sample time-shift, multiply with x1(n) and sum up for r12(-2)

## Slide 38: Example
.
Notes: If j = - 2, then, then x2(n+2) is a x2(n) shifted to left by 2-sample time-shift, multiply with x1(n) and sum up for r12(-2)
Similar for j =-1 to j=3, we find the rest of r12 sequence
At lag index 3, the maximum correlation occurs. It can also indicate the position

## Slide 39: Autocorrelation
If a signal is correlated with itself, the resulting signal is called the autocorrelation.
It is a mathematical tool for finding repeating patterns, such as the presence of a periodic signal which has been buried under noise.
When j = 0, the autocorrelation is the energy E of a waveform
Notes: If x1 and x2 are the same signal, then the resulting signal is called autocorrelation

## Slide 40: Example
Calculate the autocorrelation of signal:
n= -2 -1 0 1 2 3 4
.
.
.
.
.
Notes: Given x1(n)=x2(n)= 1 2 2
At lag index 0, the maximum correlation occurs which is not surprising

## Slide 41: Convolution and Cross-correlation relationship
Convolution and cross correlation are similar operations.
if we time reverse the sequence which is sliding through the time axis in a convolution, we obtain cross-correlation
That is convolution can be used to calculate cross correlation.
Notes: Convolution and correlation are quite similar but they are not the same
By time reversing the sequence and sliding through the time axis as in the convolution, cross-correlation can also be obtained by this method

## Slide 42: Summary
How to derive impulse response from a digital system.
How to compute the discrete linear convolution, correlation, cross correlation and auto correlation.
Notes: If the input is an unit impulse then the system out will be the impulse response, y(n) = h(n)
We have also learnt how to do discrete linear convolution using the graphical and slide rule methods
Concepts and examples of correlation and cross correlation of two different signals are also covered
Autocorrelation is computed if both signals are the same.