## Slide 1: Unit 1 Quantities & Units
Part D: Metric Prefixes

## Slide 2
What will you learn?
  Use metric prefixes to represent exponent values in scientific and engineering notations.
  Convert from one metric prefix to another.

## Slide 3
Metric Prefix, centi (c)
  The length 0.0538 m can be expressed in
scientific notation as: 5.38 × 10−2 m
  The exponential term, 10−2, can be replaced by “centi” (symbol “c”).
  Hence the length 0.0538 m = 5.38 cm.
    This makes reading and understanding of the figure simple.
  The letter “c” is a metric prefix.

## Slide 4
Metric Prefix, milli (m)
  The length 0.0538 m can be expressed in
engineering notation as: 53.8 × 10−3 m
  The exponential term, 10−3, can be replaced by “milli” (symbol “m”).
  Hence the length 0.0538 m = 53.8 mm.
    This makes reading and understanding of the figure simple.
  “m” is an other metric prefix.

## Slide 5
Table of metric prefixes
Prefix | Symbol | Exponential | Multiplier
tera | T | 1012 | 1000000000000
giga | G | 109 | 1000000000
mega | M | 106 | 1000000
kilo | k | 103 | 1000
hecto | h | 102 | 100
deca | da | 101 | 10
deci | d | 10−1 | 0.1
centi | c | 10−2 | 0.01
milli | m | 10−3 | 0.001
micro | µ | 10−6 | 0.000001
nano | n | 10−9 | 0.000000001
pico | p | 10−12 | 0.000000000001

## Slide 6
Represent large and small numbers with metric prefixes
A current in a smart phone circuit
  0.0000000812 A = 81.2 × 10−9 A
      = 81.2 nA
Smart phone
High voltage power lines
  400,000 V = 400 × 103 V
    = 400 kV
Microwave frequency of a microwave oven
  25,000,000,000,000 Hz = 25 × 1012 Hz
    = 25 THz

## Slide 7
Convert the length 220 cm to millimetres.
∵ 1 cm = 10−2 m
1 mm = 10−3 m
∴ 1 cm = 10 mm
∴ 220 cm = 2200 mm
cm mm
 10

## Slide 8
Convert the voltage 30,000 kV to megavolts.
∵ 1 kV = 103 V
1 MV = 106 V
∴ 1 kV = 10−3 MV
∴ 30,000 kV = 30,000  10 −3 MV
= 30 MV
kV MV
÷ 1000

## Slide 9
Convert the current 0.0035 kA to milliamperes.
∵ 1 kA = 103 A
1 mA = 10−3 A
∴ 1 kA = 106 mA
∴ 0.0035 kA = 0.0035  106 mA
= 3500 mA

## Slide 10
What you have learned?
  Represent numbers in metric prefixes.
  Convert from one metric prefix to another.
  Metric prefixes are commonly used, such as TV channels (MHz in VHF, GHz in UHF), memory size (Mb, Gb), vehicle velocity (km/hr), and etc.

## Slide 11
Coming Up Next
  Unit 2: Electric Charge, Voltage and Current