## Slide 1: Unit 10 AC Voltage and Current
Part A: Generation of AC Waveform

## Slide 2
What will you learn?
  The meanings of DC and AC.
  Right hand rule.
  How AC voltage and current can be generated.
  Some characteristics of an AC generator.

## Slide 3
What is meant by dc
  In the previous units, we have learned about the “dc” or direct current in our circuit analysis.
  In a dc circuit,
    the polarities of the voltages remain the same throughout, and
    the current directions also remain the same.

## Slide 4
0
+
–
What is meant by dc
The voltmeter shows no voltage is detected

## Slide 5
0
+
–
What is meant by dc

## Slide 6
What is meant by ac
  In electrical and electronic engineering, the term “alternating current” (or ac) refers to a condition where
    the voltage across each component of a circuit changes (or alternates) its polarity repetitively and/or
    the current direction changes (or alternates) repetitively.

## Slide 7
What is meant by ac
  Examples of some common ac waveforms:
    Sinusoidal
    Triangular
    Square
    Saw-tooth

## Slide 8
Generating ac voltage and current
  The electricity that we get from an electrical socket on the wall is alternating current (ac).
E
(Earth)
L
(Live)
N
(Neutral)

## Slide 9
Generating ac voltage and current
  Imagine that there is a battery behind the socket connected across L and N terminals (holes).

## Slide 10
Generating ac voltage and current
  When we use a voltmeter to measure the outlet holes of the socket, we get a reading on the voltmeter (positive).
–
0
+

## Slide 11
Generating ac voltage and current
  When the battery is turned upside down . . .
  The reading on the voltmeter is of the opposite polarity (negative)
–
0
+

## Slide 12
Generating ac voltage and current
  If we turn the battery round and round continuously, we get . . .
0
–
+

## Slide 13
Generating ac voltage and current
  Therefore if we plot a graph of the voltage reading of the voltmeter against time, we get the pulsating waveform.
V
time
0

## Slide 14
Generating ac voltage and current
  Of course, in reality, there isn’t a battery behind the electrical socket in the wall.
  The electricity comes from the power station.
  Electricity is generated by changing flux linkage through coils in a power generator.

## Slide 15
Generating ac voltage and current
  Generating an ac waveform is achieved through the cutting of magnetic flux lines by the rotating coils of wire called the rotor.
  The direction of the current flow follows Right Hand Rule or “Generator Rule”.
  The direction reverses as the coil changes position (say, Red conductor from nearer to N pole initially to nearer to S pole now).

## Slide 16
Generating ac voltage and current
  The effective rate of cutting flux lines depends on the instantaneous position of the coil conductor.
    If the coil is positioned horizontally, the conductor is moving vertically to the flux lines and will have the maximum cutting rate.
    If the coil is now positioned vertically, the conductor is moving in parallel to the flux lines and will have zero cutting rate.
    If the coil is positioned at an angle tilted to the flux lines, the rate of cutting is lying between zero and the maximum rate.

## Slide 17
N
N
N
Example 1: Which one of the following motion produces the most voltage across the conductor?
  Motion (C)
S
S
S
(A)
(B)
(C)

## Slide 18
Right Hand Rule
  Memorising the directions of the three variables: field, motion and current can be made simple by using the right hand rule.
  Both fingers and the thumb must be pointing out perpendicularly to each other.
  The Right Hand Rule:
    If the first finger of the right hand is pointing the direction of the magnetic field,
    the thumb pointing the direction of the motion,
    then the second finger is pointing the direction of the induced current.

## Slide 19
Right Hand Rule
  Frist finger points along with the magnetic field direction.
    Magnetic field direction: north to south.
  Thumb points along with the motion direction of the conductor.
Motion
S
N
  Then, the second finger will tells you the current direction in the conductor bar)
  Induced current flowing towards you when the conductor bar cuts across the magnetic field.
Fleming’s right hand rule by Douglas Morrison DougM /CC-BY-SA-3.0 https://commons.wikimedia.org/wiki/File:RightHandOutline.png

## Slide 20
Frequency f and Rotational Speed n
  One revolution of conductor through magnetic field:
    One cycle of induced sinusoidal voltage.
  Conductor’s rotational speed determines time to complete of one cycle.
  Frequency of a periodic waveform, number of cycles per second.
  The unit of frequency is hertz (Hz).
  Faster conductor’s rotational speed,
    Higher frequency of induced voltage.
N
S
N
S

## Slide 21
N
N
S
S
Frequency f and Rotational Speed n
  Faster conductor’s rotational speed, higher frequency of induced voltage
  Frequency of the ac voltage can also be increased by
    increasing number of magnetic poles.
  Frequency
    where = number of pole pairs.
      one pole pair = a set of N and S poles
    = rotational speed, in number of revolutions per second (rps or rev/s).

## Slide 22
Frequency f and Rotational Speed n
  By Faraday’s law, we can derive that the peak induced voltage, .
    where n is the rotational speed, and
    N is the number of turns of the coil.
  However, increasing n will increase the frequency f of the sinewave, which is undesirable. .
  The frequency of the electricity supply is usually fixed at 50 Hz or 60 Hz.
  Hence, we can generate high AC voltage by increasing the number of turns of the coil N.

## Slide 23
Example 2: The conductor loop (rotor) of a simple two-pole generator rotates at a rate of 50 rev/s. What is the frequency of the output voltage?
  Note: p = 1 pole pair = 2 poles (combined one N and one S as one pair)

## Slide 24
Example 3: In order to produce a 400 Hz sinusoidal voltage, at what speed must a four-pole generator be operated?
  Rotational speed
  where p = 2 pole pairs (4 poles)

## Slide 25
Generating ac voltage and current
  The symbol of an ac voltage source.
  Its voltage is in root mean square (rms) value.
    If it is required, its value can be converted to peak value .
Sinusoidal
voltage
Source
symbol
VS

## Slide 26
Sources of ac waveform
  Two main types of ac sources are available:
    AC generator
    Function generator

## Slide 27
Sources of ac waveform
  AC generator supplies us the sinusoidal voltage and current to power up our lights, home appliances and electronic gadgets.
  It can be generated from
    power plants, or
    standby power generators.

## Slide 28
Sources of ac waveform
  Most function generators can generate a few types of periodic signals, such as sinusoidal wave, square wave and triangular wave.
  The output signal is too weak to drive loads that require heavy current.
  Function generators are found in laboratories for lab work, repairing and R & D.

## Slide 29
You have learned that
  AC voltages and currents alternate in voltage polarities and current directions repetitively.
  Right hand rule or generator rule.
  Waveforms of ac voltages and currents are sinusoidal in nature.
  In an AC generator, and
  AC waveforms can be generated by power generators for power consumption and by function generators for laboratory and research work.

## Slide 30
Coming Up Next
  Descriptions of an ac waveform