## Slide 1: Unit 10 AC Voltage and Current
Part C: AC Circuit Analysis

## Slide 2
What will you learn?
  Apply circuit laws and rules in ac analysis.
  Use rms values in voltage and current calculations.
  Determine the resultant waveform of superimposing ac and dc components.

## Slide 3
Circuit laws and rules in ac circuits
  All circuit laws and rules apply to ac circuits in the same way they apply to dc circuits.
  For an ac circuit, all ac voltages and currents are in rms values unless otherwise specified.
R
VS
I

## Slide 4
Example 1: Determine the voltage drops across each resistor and the circuit current.
VS
230 V
R1
1 k
R2
560 
V1
I
V2
  All voltages and currents are in rms values.
  The total resistance RT = 1 kΩ + 560 Ω = 1.56 kΩ
  Apply Ohm’s law to find current, I
  Voltage drop across R1, V1 = I × R1 = 147.4 mA × 1 kΩ = 147.4 V
  Voltage drop across R2, V2 = I × R2 = 147.4 mA × 0.56 kΩ = 82.5 V
    You can also apply VDR to find the voltage drops.

## Slide 5
Superimposed dc and ac voltages
  In many circuit practices, you will find both ac and dc voltages combined.
R
Vac
Vdc
+
−
Vac + Vdc
Vmax = Vp + Vdc
Vmin = −Vp + Vdc

## Slide 6
Superimposed dc and ac Voltages
  Case 1: If Vdc > Vp,
  The combined voltage waveform shows that
Vdc
Vmax = Vdc + Vp
Vmin = Vdc − Vp
Vp
Vp
t
    Sine wave does not reverse its polarity and is non-alternating.
  A dc offset sine wave
    Offset = Vdc

## Slide 7
Example 2: Determine the maximum and minimum voltage drops across resistor R.
Vmax = Vdc + Vp = 12 + 10 = 22 V
Vmin = Vdc − Vp = 12 − 10 = 2 V
12 V
22 V
2 V
10 V
t
R
+
−
VP
10 V
Vdc
12 V

## Slide 8
Superimposed dc and ac voltages
  Case 2: If Vdc < Vp,
  The combined voltage waveform shows that
    Sine wave is negative during certain portion of its lower half-cycle and is alternating.
Vdc
Vmax = Vdc + Vp
Vmin = Vdc − Vp
Vp
t

## Slide 9
Example 3: Now the Vdc is reduced to 6 V. Determine the new maximum and minimum voltage drops across resistor R.
Vmax = Vdc + Vp = 6 V + 10 V = 16 V
Vmin = Vdc − Vp = 6 V − 10 V = −4 V
Vp = 10 V
Vdc = 6 V
R
+
−
6 V
16 V
−4 V
10 V
t

## Slide 10
You have learned that
  Circuit laws and rules are applicable in ac circuit analysis.
  RMS values of voltages and currents are assumed in ac circuits unless otherwise stated.
  An ac voltage can be superimposed on a dc voltage in a circuit.
  Resultant waveform of the combined ac and dc voltages can be alternating or non-alternating.

## Slide 11
Coming Up Next
  Unit 12 Capacitors