## Slide 1: Unit 12 Capacitors
Part B: Charging and Discharging
Processes of Capacitors

## Slide 2
What will we learn?
  The charging process of capacitor
  The discharging process of capacitor

## Slide 3
  In neutral (uncharged) state, both plates of a capacitor contain equal number of electrons.
How a Capacitor Stores Charges

## Slide 4
When connected to a voltage source,
  Plate A: electrons removed
  Plate B: electrons deposited
+
Plate A loses electrons  becomes more positively charged.
Plate B gains electrons  becomes more negatively charged.
Capacitor gets increasingly charged.
During this process, electrons flow through the connecting leads and the voltage source.
Plate A
Plate B
VS
The charging process…
How a Capacitor Stores Charges

## Slide 5
Electron movement stops at the plates because they cannot flow through the insulating dielectric.
Voltage builds up across plates.
Plate A
Plate B
+
VS
vC
+
Movement of electrons stops when voltage across capacitor equals source voltage, Vs. The external source cannot move charge any more: the capacitor is now fully charged.
Insulating dielectric
How a Capacitor Stores Charges
=

## Slide 6
If capacitor is now disconnected from source, it can retain the stored charge for a long time.
A capacitor with stored charge can act as a temporary battery.
Plate A
Plate B
VS
+
+
VS
Charges still stored
How a Capacitor Stores Charges
−

## Slide 7: RC Charging Circuit

## Slide 8
Time is required for a capacitor to charge or discharge fully.
Amount of time required depends on time constant of the circuit.
Time Constant & Charging Curves
where
= time constant (s)
R = resistance (Ω)
C = capacitance (F)
Greek letter, tau

## Slide 9
τ is the amount of time required to charge a capacitor to approximately 63% of its final value.
At time = 5τ, capacitor can be considered to be fully charged.
Note that every capacitor circuit has some amount of resistance present.
Time Constant & Charging Curves

## Slide 10
Graphical Plot of Charging Curves
0  2 3 4 5
63%
86%
95%
98%
99%
Capacitor voltage during charging
Capacitor current during charging
t
When , is 63% of final value.
When t = 5τ, is 99% of final value (considered fully charged).

## Slide 11
increases exponentially.
decreases exponentially.
It takes (transient time) to change the voltage cross the capacitor by 99% and stabilise.
In a steady state (),
and .
A fully charged
capacitor appears
as an open circuit
At ,
An uncharged
capacitor appears
as a short circuit
Graphical Plot of Charging Curves
0 1 2 3 4 5 t
63%
86%
95%
98%
99%

## Slide 12
RC Discharging Circuit
When switch S closes, excess electrons move from plate B to plate A
Energy stored in an electric field by capacitor is converted back into discharging electric current
  During charging and discharging, current flows from one plate to another only through the external circuit
Direction of current
  Discharge current opposite that of Charging current

## Slide 13
It takes 5τ (transient time) to change voltage by 99%.
In dc steady state (), and .
Discharging curve is a decreasing exponential curve.
0  2 3 4 5
100%
37%
14%
5%
2%
1%
t
At t = τ, voltage or current is 63% of journey to zero.
At t = 5τ, voltage or current is 99% of journey to zero.
Graphical Plot of Discharging Curves

## Slide 14
RC Discharging Circuit
Electrons stop moving when number of free electrons on both plates are again equal and charge is neutralized.
When a capacitor is fully discharged, .

## Slide 15
You have learned about
  how a capacitor store charges,
  the circuits, curves and equations of charging and discharging a capacitor, and
  the time constant and how it relates to the charging and discharging curves.

## Slide 16
Coming Up Next
  Analyse Capacitors Connected in Series and Parallel Circuits