## Slide 1: Unit 2: Electric Charge, Voltage & Current
Part C: Current

## Slide 2: What will you learn?
What is current?
How current is quantitatively defined?
What is the difference between conventional current direction and electron current direction?

## Slide 3: What is Current?
-
-
-
-
-
-
-
-
In the absence of an external voltage source, free electrons move randomly inside the conductor.
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
Notes: Free electrons in a conductive material drift randomly in the absence of a voltage

## Slide 4: What is Current?
When a voltage is applied, electrons move in an orderly fashion.
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
+
_
High Potential
Low
Potential
Notes: When a voltage is applied between 2 ends of the wire, energy is available for electrons to move in a fixed direction
When electrons move, current is said to flow.
Electrons flow out from the negative terminal of the voltage source, through the conductor, and return to the positive terminal.

## Slide 5: Current
The magnitude of an electric current is determined by how much charge flowing per sec.
-
-
-
-
-
-
-
-
-
-
-
-
-
-

## Slide 6: Unit & Symbol
Current is measured in amperes (or amps in short) named after the French physicist Marie Andre Ampere.
The unit symbol is A.
A current of 1 A means that the electric charge moves at a rate of 1 C per second.
Marie Andre Ampere
Notes: Think of how can you can increase current from 1A to 2A? Pause.
Either double the no. of charges flowing per second or allow 1 C of charges to flow through in 0.5 seconds

## Slide 7: Example 1
15 C of charge passes through a given point in a circuit in 3 s. What is the magnitude of the current?
Notes: 15 coulombs of charge

## Slide 8: Example 2
  The current flows through the filament of a lamp is 2 A. How much charge moves through the filament in 2.5 s?

## Slide 9: Typical Current Values

## Slide 10: Electron Current vs. Conventional Current
Electron Current direction
V
+
_
Electron
current flow
Conventional current direction
V
+
_
Conventional
current flow
Conventional Current is used throughout this course
High Potential
Low
Potential

## Slide 11: What have you learned?
Current is the movement of electric charge between a potential difference.
Unit of current is ampere, A.
Conventional current moves from high to low potential in a conductor.
Electron current moves from low to high potential in a conductor.

## Slide 12: What’s coming up next?
Unit 3 Part A, Resistance.