## Slide 1: Unit 3 Resistance & Ohm’s Law
Part A: Resistance
Notes: Hi! Welcome to Unit 3: Resistance and Ohm’s Law, Part A on Resistance.

## Slide 2: What will you learn?
What is resistance?
Factors affect resistance value
Use of resistance
Different types of resistors

## Slide 3: What is resistance?
Electric resistance is the hindrance to the flow of charges or current.
Analogy between water circulation system and electric circuit.
I
V
+
−
∼
Copper wire is a good conductor because of large quantity of free electrons in it.
Nichrome wire has much less free electrons in it, not a good conductor.
Nichrome wire restricts the current flow.

## Slide 4: Factors affect Resistance
The symbol for resistance is R.
Unit of resistance: ohm (Ω).
where
= resistivity (Ωm)
= length (m)
A = cross-sectional area (m2)
CC-BY-SA-3.0
https://en.wikipedia.org/wiki/File:Resistivity_geometry.png
Greek letter rho,

## Slide 5: Factors affect Resistance
Different materials have different resistivities.
More free electrons ⇒ Lower resistance
Dimensions affect the resistance too.
  Longer a wire ⇒ Higher the resistance
  Thicker a wire ⇒ Lower the resistance
CC-BY-SA-3.0
https://en.wikipedia.org/wiki/File:Resistivity_geometry.png

## Slide 6: Resistivity
Resistivity is a property of a material.
Lower the resistivity, better the material for making conducting wire.
Resistance (Ω) ≠ Resistivity (Ωm)
,
Resistivity is temperature dependent.
Material | Resistivity  (Ωm) at 20oC
Silver | 1.59 × 10-8
Copper | 1.68 × 10-8
Aluminium | 2.65 × 10-8
Tungsten | 5.6 × 10-8
Iron | 9.71 × 10-8
Hard Rubber | 1.59 × 1013
PVC | 5.4 × 1015
PTFE or Teflon | 10 × 1022

## Slide 7
Example 1: A 2-m long copper wire has a uniform cross-sectional area of 4 mm2. Given that resistivity of copper is 1.68 × 10−8 Ωm, determine its resistance.
    = 8.4 mΩ
Enter all data in SI units
Notes: You have a camera sitting beside you. Its screen view indicates a low battery. You retract it and notice a label on it reads: 3.7 V, 1000 mAh; Minimum 940 mAh or 3.5 Wh.
Another big question for you.

## Slide 8
Example 2: An aluminium sheet with a uniform cross-sectional area of 8 mm2 is used to form a common junction of two points in an electric circuit. The resistivity of aluminium is 2.65 × 10-8 Ωm. If the resistance of the sheet must not exceed 2 mΩ, determine the maximum length of the aluminium sheet.
    = 603 mm
Notes: You have a camera sitting beside you. Its screen view indicates a low battery. You retract it and notice a label on it reads: 3.7 V, 1000 mAh; Minimum 940 mAh or 3.5 Wh.
Another big question for you.

## Slide 9: Use of Resistance
Resistance can generate heat (on purpose, of course) so that you can use it to
  iron clothing
  make toast
  dry your hair
  heat up water

## Slide 10: Use of Resistance
Other use:
  To limit the current in a circuit.
  Varying resistance can dim or brighten your room.
  You can have resistance arrangements to produce current division and voltage division.

## Slide 11: Resistor
3 Board Types of Resistors:
  Wirewound resistors
  Composition resistors
  Film resistors
Notes: You have a camera sitting beside you. Its screen view indicates a low battery. You retract it and notice a label on it reads: 3.7 V, 1000 mAh; Minimum 940 mAh or 3.5 Wh.
Another big question for you.

## Slide 12: Resistor
Wirewound Resistor
    Thin metal alloy (such as nichrome) wire wound onto a ceramic former in a spiral helix
    Low resistance value, 0.01Ω to 100 kΩ
    High precision value
    Able to withstand high current and high power
Notes: You have a camera sitting beside you. Its screen view indicates a low battery. You retract it and notice a label on it reads: 3.7 V, 1000 mAh; Minimum 940 mAh or 3.5 Wh.
Another big question for you.

## Slide 13: Resistor
Composition Resistor
    Made of carbon dust or graphite paste.
    Popular in the 60s & 70s.
    Good for high frequency applications
    Large tolerances, typically ±20%. 100 Ω ± 20% = 80 Ω to 120 Ω Lower tolerance, less deviation.
Notes: You have a camera sitting beside you. Its screen view indicates a low battery. You retract it and notice a label on it reads: 3.7 V, 1000 mAh; Minimum 940 mAh or 3.5 Wh.
Another big question for you.

## Slide 14: Resistor
Film Resistor
    Carbon film, metal film, metal oxide film resistors
    Resistance value is controlled by varying the thickness of the deposited film and by cutting the film in a helical manner along its length.
    Low tolerance, as low as ±0.1% for some metal film resistors.
Notes: You have a camera sitting beside you. Its screen view indicates a low battery. You retract it and notice a label on it reads: 3.7 V, 1000 mAh; Minimum 940 mAh or 3.5 Wh.
Another big question for you.

## Slide 15: Resistor
SMT or SMD Film Resistor
    SMT stands for surface mount technology. SMD stands for surface mount device.
    It is also called chip resistor.
    Mounted or placed directly onto the surface of printed circuit boards (PCBs).
Notes: You have a camera sitting beside you. Its screen view indicates a low battery. You retract it and notice a label on it reads: 3.7 V, 1000 mAh; Minimum 940 mAh or 3.5 Wh.
Another big question for you.

## Slide 16: Resistor
A resistor is a two-terminal device.
The symbol used in schematic and electrical drawings for a resistor can either be a “zig-zag” type line (IEEE symbol) or a rectangular box (IEC symbol).
We will follow the IEEE symbol.
Notes: You have a camera sitting beside you. Its screen view indicates a low battery. You retract it and notice a label on it reads: 3.7 V, 1000 mAh; Minimum 940 mAh or 3.5 Wh.
Another big question for you.

## Slide 17: Variable Resistor
Two types of resistors: fixed value & variable value.
You have learned about the fixed value resistors.
The resistance of a variable resistor is adjustable.
Symbol for a variable resistor:
Notes: You have a camera sitting beside you. Its screen view indicates a low battery. You retract it and notice a label on it reads: 3.7 V, 1000 mAh; Minimum 940 mAh or 3.5 Wh.
Another big question for you.

## Slide 18: Variable Resistor
A
A
B
B
W
W
W
A
B
A variable resistor is often obtained from a potentiometer, which has a third terminal W with rotating dial (or wiper) so that a variable resistance can be achieved between the terminals A & W, and between terminals B & W.
  Resistance between terminals A & B is fixed at RAB
  Resistance between A & W = RAW
  Resistance between B & W = RBW
Notes: You have a camera sitting beside you. Its screen view indicates a low battery. You retract it and notice a label on it reads: 3.7 V, 1000 mAh; Minimum 940 mAh or 3.5 Wh.
Another big question for you.

## Slide 19: Variable Resistor
A variable resistor (VR) is supposed to be a 2-terminal device.
A potentiometer is a 3-terminal device.
  To use a 3-terminal potentiometer as a 2 terminal VR, we can either
    leave terminal A or B unconnected,
    or connect either (A or B) to W.
A
B
W
W
A
B
A
W
A
B
W
E.g. Not use terminal B
Notes: You have a camera sitting beside you. Its screen view indicates a low battery. You retract it and notice a label on it reads: 3.7 V, 1000 mAh; Minimum 940 mAh or 3.5 Wh.
Another big question for you.

## Slide 20: Variable Resistor
  To use a 3-terminal potentiometer as a 2-terminal VR.
W
A
B
A
B
W
A
W
A
B
W
Notes: You have a camera sitting beside you. Its screen view indicates a low battery. You retract it and notice a label on it reads: 3.7 V, 1000 mAh; Minimum 940 mAh or 3.5 Wh.
Another big question for you.

## Slide 21: Potentiometer
  Trimmer potentiometer or trim-pot is potentiometer not designed for frequent adjustment.
  Trimmers are much smaller in size, and usually not so conveniently to be adjusted.
trimmer potentiometer (or trim-pot)
trimmer potentiometer (or trim-pot)
potentiometer
Notes: You have a camera sitting beside you. Its screen view indicates a low battery. You retract it and notice a label on it reads: 3.7 V, 1000 mAh; Minimum 940 mAh or 3.5 Wh.
Another big question for you.

## Slide 22: What you have learned?
  Electric resistance is a hindrance to current flow.
  resistivity, a material dependent property. Unit is Ωm.
  Application of resistance: heating element and dimmer.
  Types of resistor: wirewound resistor, composition resistor, film resistor, through-hole resistor and surface mount resistor.
  Use potentiometer as variable resistor.

## Slide 23: Coming Up Next
Unit 2, Part B: Resistor Colour Code