## Slide 1: Unit 3 Resistance & Ohm’s Law
Part C: Conventional Current and Reference Ground
Notes: Hi! Welcome to Unit 1: Quantities and Units, Part A on Electrical Units.

## Slide 2
What will you learn?
  Conventional current,
  its relationship with electron current, and
  reference ground.
Notes: The objective of this unit is to get familiar with and to explain commonly used electrical quantities and their units.

## Slide 3
Flow of electrical charges
  In the early 19th century, scientists assumed that current was a flow of positive charge from a high potential point (positive terminal) to a low potential point (negative terminal).
  Actual current is the flow of free electrons.
  This conceptual current of positive charge is referred to as conventional current.
Notes: There is a label to every electric appliance. When you pick up an electric kettle, you may notice its label stating the numbers: 220 V to 240 V, 50 or 60 Hz, 2000 – 2400 W.
You wonder what information these numbers are telling us.

## Slide 4
Conventional current vs electron flow
  Conventional current flows from the anode (positive terminal) of voltage source (V), around the circuit and returns to the cathode (negative terminal) of the source.
V
+
_
Conventional
current flow
Notes: There is a label to every electric appliance. When you pick up an electric kettle, you may notice its label stating the numbers: 220 V to 240 V, 50 or 60 Hz, 2000 – 2400 W.
You wonder what information these numbers are telling us.

## Slide 5
Conventional current vs electron flow
  Electrons, being negative charges, flow from the cathode (negative terminal) of voltage source (V), around the circuit and returns to the anode (positive terminal) of the source.
V
+
_
Electron
current flow
Notes: There is a label to every electric appliance. When you pick up an electric kettle, you may notice its label stating the numbers: 220 V to 240 V, 50 or 60 Hz, 2000 – 2400 W.
You wonder what information these numbers are telling us.

## Slide 6
A simple circuit
  Schematic diagram of a basic circuit:
A voltage source V
A load such as a resistor or lamp
Wires that provide the path for the current to flow
V
+
_
Notes: You have a camera sitting beside you. Its screen view indicates a low battery. You retract it and notice a label on it reads: 3.7 V, 1000 mAh; Minimum 940 mAh or 3.5 Wh.
Another big question for you.

## Slide 7
Potential and Voltage
  In electrical and electronic engineering, the 2 terms potential and voltage can be used interchangeably.
  Potential or voltage are the energy to move charge from one point to another point. As water only flows when there is a pressure difference, we always talk about a potential difference or a voltage difference between two points conceptually. However the word, ‘difference’, is sometimes omitted because it is understood.
    The voltage of a battery
    The voltage difference across the battery terminals
    The voltage difference across a resistor
    The voltage of a resistor

## Slide 8
Ground
  The negative terminal of a voltage source is often referred to as the reference ground of a circuit.
  It has a circuit symbol as
or

## Slide 9
Ground
  In many circuits, it is more convenient to show more ground points.
V
+
_
V
+
_
V
+
_

## Slide 10
Reference Ground
  Voltage at point A with respect to the ground is equal to 12 V.
  It means that the voltage at point A is 12 V higher than the reference ground.
  The words, “with respect to the ground” are often dropped for convenience.
  Simply write, the voltage at point A, VA = 12 V.
  Another concept: The voltage at a point, instead of between 2 points, can be defined if we assume that the voltage at the reference ground is 0 V.
12 V
+
_
12 V
A
0 V

## Slide 11
You have learned that
  The conventional current flows from high to low potential.
  Flow of free electrons constitutes the true current.
  A ground can be used as a reference to define the ‘absolute’ voltage at any one point in a circuit.

## Slide 12
Coming Up Next
  Ohm’s Law