## Slide 1: Unit 4 Energy & Power
Part B: Power in an Electric Circuit

## Slide 2
What will you learn?
  What voltage source and current source are.
  Calculate power of a simple circuit.

## Slide 3
Power source
  Scenario 1: When you switch on your torch, it lights up...
    Where is the source of energy that lights up your torch?

## Slide 4
Power source
  Scenario 2: When you play your electric guitar, you sing to the tune …
    What is the source of energy that amplifies the sound from the strings?

## Slide 5
Power source
  Scenario 3: When you play with your toy robot at home, it moves with lights flickering and perhaps saying hello to you …
    Where is the source of energy of the robot?

## Slide 6
Power source
  A gadget requiring electricity to operate is said to be powered by electricity.
  The source of the electrical energy for a circuit is referred to as the power source of the circuit.
  An electrical power source can be a voltage source or a current source.
Current source
Voltage source

## Slide 7
Voltage Source
  An ideal voltage source is able to provide stable output voltage with constant amplitude regardless of the power consumption of the load.
  Examples of voltage sources: Car battery, Li-ion battery, battery charger, power adaptor for LED display, and etc.
  Voltage source is also called voltage supply.

## Slide 8
Current Source
  An ideal current source is able to provide stable output current with constant amplitude regardless of the power consumption of the load.
  Unlike voltage sources, a current source is in fact an electronic circuit which provides a stable output current. This electronic circuit in itself is powered by a voltage source.
  Applications:
    Battery charger
    Power up dc motor for fixed torque, T ∝ I.

## Slide 9
Power flow
P
Source
Power Flow Direction
    In this circuit, the power source is a dc voltage source, e.g. a battery or a dc power adaptor.
    The power source delivers (outputs) power to the load.
Load
+
_
R
V
+
_
I
I
I
    A load can be a resistor, a light bulb, or an electric appliance.

## Slide 10
Power Formula
where
W is the work done or energy,
Q is the charge.
  Rearrange the two equations.
    In Unit 2, you learned
  The power delivered from a power source
  = Voltage of the power source × Current of the power source.
  The power consumed or dissipated by a component
  = Voltage across of the component × Current in the component.

## Slide 11
Power Formula
    Ohm’s law:

## Slide 12
Power Formula
  All 3 formulas can be applied to calculate the power consumption or power dissipation of any resistive components or devices, such as, resistor, incandescent light bulb and any resistive wire.
  P = VI can also be used to calculate the output power of any electrical power sources.

## Slide 13
Power Expressions
  Ohm’s law and power expressions relating to V, I and R are depicted in the pictorial diagram.

## Slide 14
Example 1: A 12 V supply is connected across a 120 Ω resistor. Determine the power dissipation of the resistor.
V
+
_
I
R

## Slide 15
Example 2: A 100 V supply is connected across a 50 W light bulb. Determine the current in the circuit.
V
+
_
I
R

## Slide 16
Example 3: A 100 W light bulb is connected to a voltage supply. The circuit current is 500 mA. Determine the supply voltage.
V
+
_
I
R

## Slide 17
What have you learned?
  A voltage or current source supplies power to an electric circuit.
  Voltage supply provides a stable output voltage regardless of the load.
  Current supply provides a stable output current regardless of the load.
  Power formulas: .

## Slide 18
Coming Up Next
  Resistor Power Ratings