## Slide 1: Unit 4 Energy & Power
Part D: Energy Conversion and Perfect Conductor
Notes: Hi! Welcome to Unit 3: Resistance and Ohm’s Law, Part A on Resistance.

## Slide 2
What will we learn?
  How electrical energy is converted to heat in a resistive material.
  The lost in electrical energy results in voltage drop across a resistive material.
  Know the characteristics of perfect conductor.

## Slide 3
Heat Dissipation and Voltage Drop
  When the electron current passes through a resistive material, such as a resistor,
    the free electrons collide with ions in the resistive material,
    the free electrons are scattered in random motion and do not move in the well-aligned manner as inside a conductor.
  This causes conversion of electrical energy to heat energy.
  The lost of electrical energy results in a voltage drop across the resistive material.
+
_
V

## Slide 4
Example 1: A resistive material has 30 ×1020 electrons flowing through it. The heat energy dissipated from the material is 2 kJ. Determine the resultant voltage drop.
  Recall that 6.25×1018 electrons carry 1 C of negative charge.
Notes: You have a camera sitting beside you. Its screen view indicates a low battery. You retract it and notice a label on it reads: 3.7 V, 1000 mAh; Minimum 940 mAh or 3.5 Wh.
Another big question for you.

## Slide 5
Perfect Conductor
  A perfect conductor has zero resistivity, thus zero resistance for whatever dimensions and shapes.
  A perfect conductor consumes no power.
    .
  The potential difference between any two points in a piece of perfect conductor is zero (zero voltage drop).
    .
  We always assume that perfect conducting wires are used unless otherwise stated.

## Slide 6
Perfect Conductor
  The voltage at the reference ground is 0 V.
  ∵ The potential difference between any two points in a piece of perfect conductor is zero.
12 V
+
_
I
R
A
B
C
D
E
F
G
  ∴ The voltage at any point on the black wire is 0 V.
  The black wire is referred to as the ground wire. The voltage of the ground wire is 0 V.
  The voltage at point A with respect to (w.r.t.) the ground is .
  ∵ The assumption of no voltage drop across a conducting wire. ∴ The voltage at any point on the red wire is 12 V.

## Slide 7
You have learned that
  When a current passes through a resistive material,
    the electrical energy, W, is converted to heat energy, and
    a voltage drop occurs across the material, .
    Remark: this voltage drop can also be calculated by and
  A perfect conductor has zero resistance and does not consume any power.
  The potential difference between any two points in a piece of perfect conductor is zero.

## Slide 8
Coming Up Next
  Unit 5, Series Circuits