## Slide 1: Unit 5 Series Circuits
Part A: Identify Series Circuits

## Slide 2
What will you learn?
  Identify a series connection.

## Slide 3
Identifying a series connection
  You have seen a Christmas tree lighting.
  When its power is turned on
    all the lights glow at the same time.
    If they twinkle, they twinkle together too.
    Yes, they display a variety of colours.
  The supply voltage can be about 100 V or 200 V (only a few volts across each bulb).
  These light bulbs are wired in a string or “in series” to receive the power

## Slide 4
Identifying a series connection
  You have used a torch light.
  The light bulb receives its power from its battery pack.
  The pack consists of a stack of three 1.5 V batteries connected in series providing the required 4.5 V EMF.

## Slide 5
Identifying a series connection
  In many applications, batteries (or dry cells) are commonly connected in series to provide a higher voltage or EMF.

## Slide 6
Identifying a series connection
  When you come to identifying a series connection of components in a schematic diagram, you look out for the following features:
  Between two chosen points (A and B) in a given circuit
    There are two or more components connected.
    The same current flows through each component.
I
I

## Slide 7
Identifying a series connection
  Note:
    Components need not be in a straight line.
    The same current flows through each component.

## Slide 8
Example 1: Identify a series connection in the circuit.
Can you identify another series connection in the diagram?
  There are two resistances (24 Ω and 36 Ω) having the same current flowing along the path B-A-D
in series
in series
not in series

## Slide 9
Example 2: Identify the series connection in the schematic diagram.
I
  There is one path along B-C-D-E that resistances R3, R4 and R6 are receiving the same current.
  So resistances R3, R4 and R6 are connected in series across B and E.

## Slide 10
Identifying a series connection
  The same concept also applies to connection of cells.
    The effective voltage and polarities at A and B depend on the connection of the cells

## Slide 11
You have learned that
  a series connection consists of two or more components, and
  the same current flows through each component.

## Slide 12
Coming Up Next
  Laws and Rules Governing Series Circuits