## Slide 1: Unit 5 Series Circuits
Part D: Voltage Measurement with respect to Circuit Ground

## Slide 2
What will you learn?
  The differences between voltage across a component and voltage at a node w.r.t. a reference ground.
  Apply node voltage and reference ground for circuit analysis.
  Advantages of using node voltage and reference ground.

## Slide 3
Measure Voltage across Components
  To measure voltage drops across resistors R1, R2 and R3, connect a voltmeter in turn as shown below.
VR1
VR2
VR3

## Slide 4
Measure Note Voltage w.r.t. Ground
  VA = the voltage at node A with respect to the ground.
  VB = the voltage at node B with respect to the ground.
  VC = the voltage at node C w.r.t. the ground.
VC
VB
VA
  Voltage difference across a component can be calculated from node voltages.

## Slide 5
Example 1: (a) Determine or calculate VD , VA, VC, and the circuit current I. (b) calculate VR1, VR2 and VB.
∵ 12 V > 3 V, ∴ the circuit current flows out from the +ve terminal of the 12 V supply and returns to its −ve terminal.
1.2 kΩ
+
_
12 V
+
_
+
_
3 V
+
_
300 Ω
B
C
A
D
The 12 V supply provides a voltage rise of 12 V from its −ve terminal to its +ve terminal.
The 3 V supply provides a voltage rise of 3 V from its −ve terminal to its +ve terminal.

## Slide 6
Example 1: (a) Determine or calculate VD , VA, VC, and the circuit current I. (b) calculate VR1, VR2 and VB.
1.2 kΩ
+
_
12 V
+
_
+
_
3 V
+
_
300 Ω
B
C
A
D
∵ From A to B, a voltage drop of 1.8 V
∵ From C to B, a voltage rise of 7.2 V
Another way:

## Slide 7
Example 2: (a) Calculate the total resistance and the circuit current. (b) Calculate the voltages drops across the resistors and the voltages at nodes A to E.
The 20 mA circuit current flows counter-clockwise.
A
30 V
24 V
100 Ω
B
C
200 Ω
E
12 V
D

## Slide 8
Example 2: (a) Calculate the total resistance and the circuit current. (b) Calculate the voltage drops across the resistors and the voltages at nodes A to E.
∵ Current flows counter-clockwise.
A
30 V
24 V
100 Ω
B
C
200 Ω
E
12 V
D
∴ A voltage drop occurs from D to C

## Slide 9
Example 2: (a) Calculate the total resistance and the circuit current. (b) Calculate the voltages drops across the resistors and the voltages at nodes A to E.
A
30 V
24 V
100 Ω
B
C
200 Ω
E
12 V
D

## Slide 10
Effects of Changing Reference Ground
  No change in: circuit current and voltage difference across a component.
  All node voltages change.
30 V
24 V
100 Ω
200 Ω
12 V
_
+
_
+
30 V
24 V
100 Ω
200 Ω
12 V
_
+
_
+

## Slide 11
Two ways to Measure Voltages
VR1
VR2
VR3
VC
VB
VA
Measure voltage difference across a component without using reference ground.
Measure node voltage using reference ground. If the reference ground is changed to node B, connection of the meters will all be changed.

## Slide 12
Advantages of using Node Voltage & Reference Ground
30 V
24 V
12 V
_
+
_
+
_
+
_
+
  Easy and fast measurement.
  Easy to compare voltages at different nodes.
  Straight forward to record voltage values.
  Easy for circuit analysis.

## Slide 13
Uses of Ohm’s law, KVL and VDR
  Circuit Analysis:
    Calculate voltages and currents in a circuit
    Understand how the components affects the circuit operation and performance.
  Repair and Maintenance
  Circuit Design

## Slide 14
You have learned
  The differences between voltage across a component and voltage at a node w.r.t. a reference ground.
  Connections of voltmeter to measure voltage across a component and node voltage.
  VR = VAB = VA − VB = IR
  Apply node voltages and a reference ground for circuit analysis.
  Advantages of using node voltage and reference ground.
+
_

## Slide 15
Coming Up Next
  Parallel Circuits