## Slide 1: Unit 6 Parallel Circuits
Part D: Effects of Adding Parallel Branches

## Slide 2
What will you learn?
  Effects of adding a parallel branch to a parallel connection.

## Slide 3
Adding a branch to a parallel circuit
  Consider a parallel circuit as shown here.
  All 4 branches receive currents from the power source VS.
  The total resistance RT can be calculated from the 4 resistors.
  Total current IT depends on RT for a constant voltage source VS.
  If a new branch is added to the circuit,
    RT will decrease, and
    IT will increase.

## Slide 4
Example 1: Adding a parallel branch
  All three branches receive currents from the 12 V voltage supply.
  The total resistance RT is given by
    = 0.0016 S
    RT = 625 Ω
  ,

## Slide 5
Example 1: Adding a parallel branch
RL
10 kΩ
IL
IT(new)
  The new branch current,
  New total resistance,
  New total current IT(new) = IT + IL
    IT(new) = 19.2 mA + 1.2 mA
    = 20.4 mA
  Alternative solution:

## Slide 6
You have learned that
  adding a parallel branch to an existing parallel circuit will
    lower the equivalent or total resistance, and
    increase the total current flowing into the circuit if the circuit is connected to a constant voltage source.

## Slide 7
Coming Up Next
  Series-Parallel Circuits