## Slide 1: Lesson on Chapter 8: Superposition Theorem
ET1005: Principles of Electrical and Electronic Engineering

## Slide 2: Objectives
At the end of the lesson, you will be able to:
  Appreciate the fundamental differences between ideal and practical voltage and current sources
  State the Superposition Theorem
  Apply Superposition Theorem to simplify the analysis of complex resistive circuits

## Slide 3: Introduction
In this chapter we will learn the characteristics of an ideal voltage source and ideal current source
We will learn the equivalent circuit of a practical voltage source and that of a practical current source
Apply the Superposition Theorem in circuit analysis by computing the effects on the circuits due to individual sources

## Slide 4
The voltage source is the source of electrical energy.
The ideal voltage source has zero internal resistance and provides a constant voltage to a load regardless of the load resistance.
8.1 The Voltage Source

## Slide 5
VS
+
_
A
B
Unloaded
With a load, the entire source voltage, VS, is dropped across RL.
Symbol of ideal voltage source
RL
+
_
VS
+
_
A
B
Loaded
VAB = VRL = VS
Ideal Voltage Source

## Slide 6
With no load,
VS = IRS + VAB
VAB = VS – IRS = VS as I = 0
The output voltage, VAB is equal to VS. This voltage is called the open circuit voltage.
VS
+
_
A
B
RS
RS : internal resistance
A practical voltage source has non-zero internal resistance and is represented by a resistor in series with an ideal voltage source.
Practical Voltage Source

## Slide 7
Loading of the Voltage Source
RL
VS
+
_
A
B
RS
I
VOUT
+
_

## Slide 8
EXAMPLE 8-1: Determine the output voltage.
RL = 100 W
VS
100 V
+
_
A
B
I
VOUT
+
_
RS = 10 W

## Slide 9
The current source is another type of electrical energy source.
An ideal current source produces a constant current through a load, regardless of the value of the load.
It has an infinitely large internal parallel resistance.
A
IS
B
Unloaded
Loaded
Ideal
Current
Source
IL = IS
IS
A
B
RL
IL
8.2 The Current Source

## Slide 10
A
B
RL
Practical Current Source
IS
RS
IL
A practical current is represented by a resistor in parallel with an ideal current source.
Practical Current Source With Load

## Slide 11
EXAMPLE 8.2: Calculate the load current for RL = 1000W.
For RL = 1kW,
A
B
RL
IS
2A
RS
10 kW
IL

## Slide 12
Superposition Theorem states that the current in any branch of a linear circuit is the algebraic sum of the currents produced by each source acting independently.
8.3 The Superposition Theorem

## Slide 13: Procedure For Applying Superposition Theorem
Consider one source at a time and replace other sources in the circuit with their internal resistances. (Short circuit for voltage source and open circuit for current source.)
Determine the magnitude and direction of the current of the desired branch due to the single source.
Repeat the above steps using each source in turn until the desired branch currents have been calculated for all sources.
Algebraically sum the currents due to each individual source to obtain the resultant branch current.

## Slide 14
EXAMPLE 8-3:
Use Superposition Theorem to find I2
R1
VS2
5V
I2
R3
R2
VS1
10V
100W
100W
100W

## Slide 15
Step 1: With source VS1 only
R1
I2’
R3
R2
VS1
10V
Short replaces VS2
100W
100W
100W
Note that this current is flowing downward through R2.

## Slide 16
Step 3:
Step 2: With source VS2 only
I2(total) = I2’ + I2” = 33.33m + 16.67m
= 50mA
R1
I2’’
R3
R2
VS2
5V
Short replaces VS1
100W
100W
100W
Note that this current is also flowing downward through R2.

## Slide 17
EXAMPLE 8-4: Find the current I2 .
I2
R1 = 100 Ω
VS = 10 V
R2 = 200 Ω
IS
30 mA

## Slide 18
Step 1: With source VS only
Note that this current is flowing downward through R2.
I2’
R1 = 100 Ω
VS
10 V
R2 = 200 Ω
IS (opened)

## Slide 19
Step 3:
Step 2: With source IS only
I2 = I2’ - I2”
= 33.33 mA – 10 mA = 23.33 mA
Note that this current is flowing upward through R2.
Since both component currents are flowing in opposite directions
through R2, the resultant current I2 can be obtained by taking the
difference of I2’ and I2”.
I2”
R1 = 100 Ω
R2 = 200 Ω
IS
30 mA
VS
(shorted)

## Slide 20
An ideal voltage source has zero internal resistance. It provides a constant voltage across its output terminals regardless of the load resistance.
A practical voltage source is represented by an ideal voltage source in series with a resistor.
An ideal current source has infinitely large internal resistance. It provides a constant current through a load regardless of the load resistance.
A practical current source is represented by an ideal current source in parallel with a resistor.
The Superposition Theorem is useful for determining voltages and currents in multiple-source circuits.
Summary

## Slide 21: End of Chapter 8 Lesson