## Slide 1
Chapter 11: Phasors and Complex Numbers (Part 1)
Phasors

## Slide 2
After completing Part 1 of this chapter, you should be able to :
  Understand how a phasor can be used to represent a sine wave.
  Draw a phasor diagram to represent a sine wave.
  Draw a phasor diagram to show the relative relationship between 2 or more sine waves.
  Write the angular and time domain expressions of a sine wave.
Objectives

## Slide 3
A phasor is a vector with a constant magnitude that rotates at a constant angular velocity.
Phasors are useful in :
  • providing a graphic means for representing sine waves in terms of their magnitude and phase angle
  • for analysis of ac circuits with sinusoidal sources.
11-1 Introduction

## Slide 4
Phasor diagrams
   abstract method of representing quantities that have both a magnitude & a direction
In Sinusoidal voltages and currents,
  magnitude = amplitude
  direction = phase angle
Hence AC waveforms can be represented using Phasor diagrams
Introduction

## Slide 5
2
45o
0o
180o
270o
90o
Phasor :
magnitude = 2
phase angle = 45o
Phasor Diagrams
Length of the phasor "arrow"  magnitude of a sinusoidal quantity
Angle, θ,  angular position (a positive angle in this example)
Magnitude

0o
180o
270o
90o

## Slide 6
Phasor Diagrams
Phasor
  magnitude = 3
  phase angle = 180o
0o
3
90o
180o
270o
1
-45o
0o
180o
270o
90o
Phasor
  magnitude = 1
  phase angle = -45o
  or +315o

## Slide 7
Full cycle of a sine wave  represented by rotation of a phasor through 360o
Instantaneous value of sine wave at any point = vertical distance from the tip of phasor to the horizontal axis
Phasor Representation of a Sine wave
Notes: 08/22/99
1

## Slide 8
Instantaneous value of sine wave is related to both position and length of phasor
Vertical distance from phasor tip down to horizontal axis represents instantaneous value of sine wave at that point
Voltage phasor at angular position of 45o and corresponding point on sine wave
Phasors and the Sine wave Formula
Notes: 08/22/99
1

## Slide 9
Position of a phasor at any instant can be expressed as a positive angle or as an equivalent negative angle
Positive angles  counter-clockwise from 0o
Negative angles  clockwise from 0o
Positive and Negative Phasor Angles
Notes: 08/22/99
2

## Slide 10
Example 11-1
For each phasor, determine the instantaneous voltage.

## Slide 11
Example 11-1 (cont’d)
Determine instantaneous sine wave value.

## Slide 12
Related Problem
If a phasor is at 30o and its length represents 24 V (peak), what is the instantaneous value of the sinusoidal voltage?
Solution
v = VP sin  = 24 sin 30o = 24 x 0.5 = 12 V

## Slide 13
A phasor diagram may be used to show the relative relationship between 2 or more sine waves of same frequency
A phasor in a fixed position represents a complete sine wave
Phase angle between two or more sine waves of same frequency remains constant throughout cycles
Phasor Diagrams for Multiple Sine Waves

## Slide 14
Wave B leads Wave A by 30o
It has smaller amplitude than Wave A
This is indicated by lengths of phasors
These two sine
waves can
represented by
a phasor diagram

## Slide 15
Example 11-2:
Use a phasor diagram to
represent the 3 sine waves
Phasor diagram
representing the 3 sine waves

## Slide 16
One cycle of a sine wave is traced out when a phasor is rotated through 2π radians (360o)
Time required to go through 2π radians is the period (T) of the sine wave.
The velocity of rotation of the phasor is the angular velocity and is designated ω.
The frequency is related to the angular velocity of the phasor by :
Angular Velocity of a Phasor

## Slide 17
Equation for instantaneous value of a sinusoidal voltage can be written as :
Instantaneous value can be calculated at any point in time if the frequency and peak value are known
The angle θ through which the phasor has rotated at any instant of time t is given by :
θ = ωt = 2π ft
v(θ) = Vp sin θ (angular domain expression)
or
v(t) = Vp sin2π ft (time domain expression)

## Slide 18
Write the time domain sinusoidal expression for each phasor.
The voltages indicated in the phasor diagram are peak voltages and the phasors have a frequency of 1 kHz.
Solution :
The time domain sinusoidal expression is given by :
v(t) = Vp sin(2πft + ) V
vA = 5 sin [(2π x 1000 x t) + 45o] = 5 sin (2000πt + 45o) V
vB = 7.5 sin [(2π x 1000 x t) + 0o] = 7.5 sin (2000πt) V
vC = 10 sin [(2π x 1000 x t) - 60o] = 10 sin (2000πt - 60o) V
Additional Example (not in textbook)

## Slide 19
In the preceding examples, the magnitudes of the phasors are expressed in peak values of the sinusoidal ac voltages.
However, sinusoidal AC waves are usually defined by the RMS values of the ac voltages and currents.
Thus, magnitudes of phasors may also be expressed in RMS values.
In AC circuit analysis, the magnitude portion of a phasor will be taken to represent the RMS Value of an AC voltage or current unless otherwise specified
Important Note

## Slide 20
A phasor diagram can be drawn to represent a sine wave.
The angular position of the phasor represents angle of sine wave with respect to a reference, and length of a phasor represents the amplitude.
A phasor diagram can also be used to show the phase relationship between 2 or more sinusoidal quantities.
The time domain sinusoidal expression is given by v(t) = Vp sin(2ft + Φ) V
Summary

## Slide 21
End of Chapter 11 (Part 1)