## Slide 1
1
Chapter 13: Inductors (Part 3)
Inductors in AC Circuits

## Slide 2
After completing Part 3 of this chapter, you will be able to:
  Analyse an AC Inductive Circuit
  Find the power in an ac Inductive Circuit
Objectives

## Slide 3
Recall
Hence an inductor:
  behaves like a short circuit in DC circuits (it becomes “invisible”)
  But generates some voltage in an AC circuit
13-6 Inductors in AC Circuits

## Slide 4
VS
L
VS
VS
L
DC Source
AC Source
VS
vL
Inductor in DC acts like a short Circuit
Inductor in AC acts like a voltage source
Inductors in AC Circuits

## Slide 5
Take Note
  You cannot make a current flowing through an inductor to change instantaneously because this will give rise to an infinite voltage
  If this happens, the inductor will be destroyed
  Hence current must only change over a period of time
Inductors in AC Circuits

## Slide 6
When a sinusoidal AC voltage is applied across an inductor, a sinusoidal AC current is generated
However, V and I are NOT in phase with each other
Instead they are 90o out of phase with V leading I
Another way of saying this is that I lags V by 90o
V-I Phase relationship in Inductor Circuit

## Slide 7
Voltage
Current
AC Voltage and Current in a purely Resistive Circuit
V in phase with I
Occurs in a Resistive Circuit
V-I Phase relationship in Inductor Circuit

## Slide 8
Voltage
Current
AC Voltage and Current in a purely Inductive Circuit
V Leads I
I Lags V
Occurs in an Inductive Circuit
or
Phase Diff = 90o
In a purely Inductive Circuit, V leads I by 90o
V-I Phase relationship in Inductor Circuit

## Slide 9
Figure 13-18: Phase relationship of VL and IL in an inductor. Current always lags the inductor voltage by 900.
In a purely inductive circuit, Voltage leads Current by 90o
V-I Phase relationship in Inductor Circuit

## Slide 10
Mathematically, this is also consistent
Assume i(t) = I sin t
Since v(t) = L (di/dt)
v(t) = LI (d(sin t)/dt)
= LI cos t
Leading Current by 900
V-I Phase relationship in Inductor Circuit

## Slide 11
If applied voltage is used as reference and assigned an angle of 0o, it can be expressed as
Then the current in the circuit expressed in polar form will be
V-I Phase relationship in Inductor Circuit

## Slide 12
If circuit current is used as reference and assigned an angle of 0o:
Then the voltages in the circuit
Thus, in a purely inductive circuit :
Inductor current always lags inductor voltage by 90° or
Inductor voltage always leads the inductor current by 90°.
V-I Phase relationship in Inductor Circuit

## Slide 13
Inductors provide a certain amount of opposition to AC currents (like resistors in a DC circuit)
This opposition is called the inductor’s Inductive Reactance or Impedance
Inductive Reactance, XL, is found as follows
Once XL is found, Impedance, ZL, can also be found:
Note that Impedance is dependent on both Inductance and frequency (when f = 0, what is XL?)
Circuit Impedance and Reactance

## Slide 14
Once impedance is found, inductive circuits follow Ohm’s Law and all other electrical laws with R replaced with XL
Ohm’s Law is now expressed as complex numbers because of the introduction of phase angles
Note that ZL always has a 90o angle attached to its magnitude and is written as XL 90o or jXL.
ZL =
Impedance of an Inductor

## Slide 15
Example 13-6
A sinusoidal voltage is applied to the circuit in Figure 13-20. Determine the inductive reactance.
Figure 13-20
VS
1 kHz
XL = 2fL
= 2(1x103)(5x10-3)
= 31.4 Ω
Solution
Related problem:
What is XL in Figure 13-20 if the frequency is increased to 3.5 kHz?
What is XL when f = 0?
(Answer:110 Ω; 0W)
Impedance of an Inductor

## Slide 16
Example 13-7
Calculate the current, I in the figure below.
Vs = 5 V
f = 10 kHz
L=100 mH
I
Figure 13-21
AC Analysis of Inductive Circuits

## Slide 17
Related Problem
Calculate the current I in Figure 13-21 if the source voltage is 12 V, f = 4.9 kHz, and L = 680 µH. Answer: 573-90o mA
AC Analysis of Inductive Circuits

## Slide 18
There are 3 types of power in an AC Inductive Circuit
  Instantaneous Power
  True Power
  Reactive Power
Power in a Purely Inductive Circuit

## Slide 19
Instantaneous Power, p(t)
  Voltages and currents in an AC Inductor circuit are always varying
  The product of v(t) and i(t) at any point in time gives instantaneous power p(t) (Unit in Watts)
I
V
P
Instantaneous Power, p(t)

## Slide 20
Instantaneous Power
  It can be seen from Graph that
    Sometimes power is positive (power supplied by source is stored in Inductor)
    Other times, power is negative (power stored in inductor is returned to source)
Instantaneous Power, p(t)

## Slide 21
True Power ( P)
  Net power consumed by Inductor
  For a purely inductive circuit (no resistance is present), value of P is zero
  Unit is Watt
Reactive Power, ( Q)
  Power stored by Inductor in its magnetic field
  Reactive Power does not represent a power or energy loss
  Unit is volt-ampere reactive (VAR)
Power in a Purely Inductive Circuit

## Slide 22
The reactive power (Q) is given by :
Therefore,
Q can also be found using:
Note that both voltage and current are expressed as RMS values.
Reactive Power, Q

## Slide 23
Example 13-8
A 10V, 1kHz signal is applied to a 10mH coil with negligible winding resistance. Determine Q.
Solution
XL = 2fL = 2(1 x 103 Hz)(10 x 10-3 H) = 62.8 Ω
Q = I2 XL = (159 x 10-3)2 x (62.8 Ω) = 1.59 VAR
What is the true power?
Answer: 0W
Reactive Power, Q

## Slide 24
Related Problem
What happens to the reactive power if the frequency increases?
Reactive Power decreases with increased frequency
Freq increases
Impedance increases
Reactive Power decreases
Reactive Power, Q

## Slide 25
In a purely inductive ac circuit, voltage leads current by 90°.
The true power consumed in a purely inductive ac circuit is zero. There is no energy loss.
Summary

## Slide 26
End of Chapter 13