## Slide 1
Chapter 18 (Part 2): Semiconductors

## Slide 2
After completing Part 2 of this chapter, you will be able to:
To understand the V-I Characteristics of a Diode.
To understand the Practical Diode Model.
To perform calculations to find the voltage and current in a diode circuit.
Objectives

## Slide 3
A diode is a device that allows current to flow in one direction but not the opposite direction
Because of the above capability, a p-n junction is also known as a p-n junction diode or a rectifier diode or simply, a diode
Symbol
Anode (+)
Cathode ( - )
p-region
n-region
The PN Junction Diode

## Slide 4
VBIAS = 0V
VBIAS = 0 V
Hence VF = 0 V
IF = 0 A
No current flows
Experimental Setup
18-8 V-I Characteristics of Diode

## Slide 5
0.7V
+VBIAS
VBIAS is large
Hence VF = 0.7V
Forward current IF is large
Forward Bias Condition
V-I Characteristics of Diode

## Slide 6: Forward Bias
Forward current very small when forward voltage across diode < 0.7 V
Beyond this point, forward voltage remains at approximately 0.7 V, but IF increases rapidly
Normal operation for a forward-biased diode is above the knee of the curve (at point C)
0.7V
IF (mA)
VF
A
B
C
Knee
Graphically,
V-I Characteristics of Diode

## Slide 7: Reverse Bias
VBIAS +
Breakdown voltage
VBIAS is reversed and not too large (<50V)
VR < breakdown value
IR is extremely small
V-I Characteristics of Diode

## Slide 8: Reverse Bias
Breakdown voltage
VBIAS +
VBIAS is reversed and large (>50V)
VR > breakdown value
IR rapidly increases and may get out of control
Excessive heat generated can destroy the semi-conductor
We DO NOT operate a Diode at VR > VBR
V-I Characteristics of Diode

## Slide 9: Reverse Bias
When VR is applied to diode, only an extremely small reverse current (IR) is present.
When VR increases, IR remains very small but voltage across the diode increases.
Once VR reaches breakdown value (VBR), the reverse current begins to increase rapidly.
IR (mA)
VR
A
B
Knee
VBR
Graphically,
V-I Characteristics of Diode

## Slide 10: Complete Curve
IR (mA)
VR
Knee
VBR
0.7V
IF (mA)
VF
Notice that IF scale is in mA while IR scale is in mA.
Combining the 2 curves:
V-I Characteristics of Diode

## Slide 11: V-I Characteristics for Diode
VF
VR
0.7 V
0
IF
IR
0
Instead of the combined curve in the previous slide, a practical diode model is usually used for circuit calculation
18-9 Practical Diode Model

## Slide 12: Forward Bias
When diode is forward-biased, it acts as a closed switch in series with a small voltage, VF.
VF=0.7V (Silicon)
VF=0.3V (Germanium)
+VBIAS -
IF
+VF -
R
A
K
Using Kirchoff’s Voltage Law,
VBIAS = IFR + VF
Practical Diode Model

## Slide 13: Reverse Bias
When the diode is reverse-biased, it acts as an open switch
IR = 0 A VDIODE = VBIAS
R
A
K
VBIAS +
VBIAS +
I = 0
Practical Diode Model

## Slide 14
EXAMPLE 18-1
Determine the forward voltage and forward current for the diode below using the practical diode model.
Find the voltage across the limiting resistor.
R
8V
+
VBIAS
1KW
Solution
Using the practical diode model, VF = 0.7V
VR = IF R = (7.3 mA)(1 kW) = 7.3 V
+
0.7V
-

## Slide 15
EXAMPLE 18-2
Determine
the diode voltage and diode current for the diode below using the practical diode model.
the voltage across the limiting resistor.
R
8V
+
VBIAS
1KW
Solution
Using the practical diode model:
IR = 0 A
VDIODE = VBIAS = 8V
VRESISTOR = 0V
Practical Diode Model

## Slide 16
A diode is a device that allows current to flow in one direction but not the opposite direction
Since a PN junction allows current to flow in one direction (when it is forward biased) but not the opposite direction (when it is reversed biased), a pn junction is also known a diode
The diode forward current is very small when its forward voltage is less than 0.7V
When a diode is forward biased, its forward voltage is equal to its barrier potential of 0.7V while its forward current increases exponentially with an increase in the bias voltage
Summary

## Slide 17
When a diode is reversed biased, with the bias voltage below its breakdown voltage, its reverse voltage is equal to the bias voltage while its reverse current is extremely small (almost zero) and remains constant
Once the reverse voltage reaches the diode’s breakdown voltage, the reverse current begins to increase rapidly
In the Practical Diode Model, the forward voltage is equal to 0.7V while the reverse current is equal to zero
Summary

## Slide 18
End of Chapter 18