## Slide 1
Rectifier Circuits
Chapter 19: Diode Applications (Part 1)

## Slide 2
After completing Part 1 of this chapter, you will be able to:
Analyse and explain half-wave rectification
Analyse and explain full-wave rectification
Objectives

## Slide 3
There are three basic types of rectifiers:
Half-wave rectifier
Full-wave rectifier with centre-tapped transformer
Full-wave bridge rectifier (the most commonly used)
Rectifiers

## Slide 4
The diode will convert input voltage (Vin) waveform into half wave output (Vout).
Vout
t
Only the positive half-cycles appear across the load.
Output is a pulsating dc voltage.
Vin
t
19-1 Half-wave Rectifiers

## Slide 5
When the input (Vin) goes positive, the diode is forward-biased and conducts current through the load resistor RL.
This will develop an output voltage Vout across it which has the same shape as the positive half-cycle of the input voltage
Positive Half Alternations

## Slide 6
When the input goes negative during the second half of this cycle, the diode is reverse-biased.
No current flows into the load RL(i.e. Io=0), so the voltage across the load resistor is 0 V (Vout= Io x RL= 0 x RL= 0 V).
Negative Half Alternations

## Slide 7
The average value of the half-wave voltage can be mathematically expressed as
t
VP
2p
VAVG
Average Value of Half –wave Voltage

## Slide 8: Example 19-1
What is the average value of the half-wave rectified voltage in the diagram shown below?
Average Value of Half –wave Voltage

## Slide 9
During the positive half-cycle, the input voltage must overcome the barrier potential before the diode becomes forward-biased
+
Vout
-
Vin
RL
+ 0.7V -
I
+
Vp(in)
t
0
Vp(out)
t
0
Vp(out) = Vp(in) – 0.7
Effect of Barrier Potential on Half –wave Rectifier Output

## Slide 10
The maximum value of reverse voltage (PIV) occurs at the peak of each negative alternation of the input voltage when the diode is reverse-biased.
 PIV = Vp(in)
Vin = IRL + VDIODE
At tp, -VP = 0 + VDIODE
Vin
t
0
tp
-Vp(in)
I = 0
Vin
RL
+
+
+
Peak Inverse Voltage (PIV)

## Slide 11
A transformer is often used to couple the ac input voltage from the source to the rectifier.
It provides two advantages:
1) It allows the source voltage to be stepped up or down as needed
2) The ac source is electrically isolated from the rectifier, thus preventing a shock hazard in the secondary
Npri : Nsec
Vpri
Vsec
RL
transformer
Vin
Half –wave Rectifier with Transformer-coupled Input Voltage

## Slide 12
Example 19-2
What is the peak value of the output voltage in the circuit below if Vin = 10V(peak) ?
2 : 1
Vpri
Vsec
1 KΩ
transformer
Vin
Solution
Half –wave Rectifier with Transformer-coupled Input Voltage

## Slide 13
Most commonly used type in dc power supplies
Allows unidirectional (one-way) current to the load during the entire input cycle
Output frequency is twice that of input frequency
Average value for a full-wave rectified sinusoidal voltage is twice that of half-wave
p
p
AVG
V
V
2
=
Vin
t
0
Vout
t
0
Full-wave
rectifier
19-2 Full–wave Rectifiers

## Slide 14
This uses two diodes connected to the secondary of a centre-tapped transformer
D1
RL
Vin
D2
2
Vsec
2
Vsec
CT
The Full–wave Centre-tapped Transformer Rectifier

## Slide 15
D1 is forward biased, D2 is reverse-biased
Current path is through D1 and load resistance RL
During Positive Half-cycles

## Slide 16
D2 is forward biased, D1 is reverse-biased
Current path is through D2 and load resistance RL
During Negative Half-cycles

## Slide 17
Current through the load resistor is in the same direction during the entire input cycle, so the output voltage always has the same polarity
Vin
t
0
t
0
Vout
0
0
RL
D1
D2
CT
Summary

## Slide 18
The peak output voltage of a full-wave centre-tapped rectifier is always one-half of the total peak secondary voltage less the barrier potential (or diode drop).
Once the peak output voltage is known, the average output can be calculated :
Re-arranging the above equation,
Peak Output Voltage

## Slide 19
When D2 is reverse biased, the peak inverse voltage (PIV) across D2 is the potential difference between the cathode and anode.
Peak Inverse Voltage (PIV)

## Slide 20
V
V
PIV
out
p
7
.
0
2
)
(
+
=
Peak Inverse Voltage (PIV) is twice the peak output voltage plus a diode drop.
As derived previously :
Therefore,
Peak Inverse Voltage (PIV)

## Slide 21
Example 19-3
Calculate : (a) half of the secondary winding peak voltage
(b) peak value of the output voltage
What is the PIV rating of the diodes used?
Peak Inverse Voltage (PIV)

## Slide 22
V
V
PIV
out
p
7
.
0
2
)
(
+
=
Solution
Peak Inverse Voltage (PIV)

## Slide 23
This circuit uses four diodes
RL
D1
D2
t
0
Vin
t
0
Vout
D4
D3
Full-wave Bridge Rectifier

## Slide 24
D1 and D2 are forward-biased and conduct current in the direction shown
A voltage is developed across load resistance RL
D3 and D4 are reverse-biased
During Positive Half-cycles

## Slide 25
D3 and D4 are forward-biased and conduct current in the same direction through RL as during the positive half-cycle
D1 and D2 are reverse-biased
During Negative Half-cycles

## Slide 26
Two diodes are always in series with the load resistor during both half-cycles. Consider each has a voltage drop of 0.7 V,
The average output voltage will hence be
Vin
t
0
RL
D1
D2
t
Vout
0
D4
D3
Bridge Output Voltage

## Slide 27
V
V
PIV
out
p
7
.
0
)
(
+
=
RL
PIV
V
V
V
p
out
p
4
.
1
(sec)
)
(
-
=
- 0.7 V
Peak Inverse Voltage of Bridge rectifier

## Slide 28
Summary of Power Supply Rectifiers

## Slide 31
End of Chapter 19 (Part 1)