## Slide 1
Copyright © 2010 Christopher Teoh, Tan HJ & Wong WY Singapore Polytechnic. All rights reserved.
Power Supply Filters
Chapter 19: Diode Applications (Part 2)

## Slide 2
After completing Part 2 of this chapter, you will be able to:
Understand the function of a power supply filter circuit
Explain how a capacitor filter works
Understand ripple voltage and ripple factor
Objectives

## Slide 3
Filtered Output
19-3 Power Supply Filters
A power supply filter eliminates (or reduces) fluctuations in output voltage of a rectifier
It produces a (near) constant-level dc voltage.
Filtering is necessary because electronic circuits require a constant source of dc voltage and current to provide power and biasing for proper operation.
The small amount of fluctuation in the filter output is called ripple

## Slide 4
During the positive first-quarter cycle of the input, the diode is forward-biased, allowing the capacitor to charge to within 0.7V of the input peak
Capacitor Filter

## Slide 5
When the input decreases below its peak, the capacitor retains its charge and diode becomes reverse-biased because the cathode is more positive than the anode.
Capacitor discharges only through the load resistance at a rate determined by the RLC time constant (normally long)
The larger the time constant, the less the capacitor will discharge.

## Slide 6
During the first quarter of the next cycle, the diode will again become forward-biased when the input voltage exceeds the capacitor voltage by approximately 0.7

## Slide 7
The capacitor charges at the beginning of each cycle
It slowly discharges through RL after the positive peak (when diode is reverse-biased).
The variation in the capacitor voltage due to the charging and discharging is called the ripple voltage.
Ripple is undesirable. The smaller the ripple, the better the filtering action is.
Ripple Voltage

## Slide 8
Half-wave ripple voltage (solid line)

## Slide 9
For a given input frequency, the output frequency of full-wave rectifier is twice that of a half-wave rectifier
Ripple Frequency

## Slide 10
When filtered,the full-wave rectified voltage has a smaller ripple than a half-wave voltage for the same load resistance and capacitor values

## Slide 11
The ripple factor ( r ) is an indication of the effectiveness of the filter.
It is defined as
Where Vr(rms) is the rms of the ripple voltage and Vdc is the dc (average) value of the filter’s output voltage.
Vp(rect)
VDC
Vr(pp)
Ripple Factor

## Slide 12
The ripple voltage Vr(rms) can be derived by approximating the ripple waveform to a triangular shape.
Hence the factor 3 to the equation:
The lower the ripple factor, the better the filter.
The ripple factor can be lowered by increasing the value of the filter capacitor or increasing the load resistance
Where Vr(p-p) is the peak to peak ripple voltage.
Vp(rect)
VDC
Vr(p-p)
Ripple Factor

## Slide 13
Surge Current in the Capacitor Filter
Before the switch is closed, the filter capacitor is uncharged.
At the instant the switch is closed, voltage is connected to the bridge and the uncharged capacitor appears as a short.
This produces an initial surge of current Isurge through the two forward-biased diodes D1 and D2.

## Slide 14
A surge-limiting resistor is sometimes used to protect the diodes
The value of this surge-limiting resistor must be small compared to the RL
Diodes must have a maximum forward surge current rating that can withstand momentary surge of current – specified as IFSM
Minimum surge value:

## Slide 15
A capacitor filter can provide a dc output voltage that is slightly less than the peak voltage at its input.
The charging and discharging of the filter capacitor result in a ripple voltage being produced. The smaller the ripple voltage, the better is the filter.
The smaller the ripple factor, the better is the filter.
Summary

## Slide 16
End of Chapter 19 (Part 2)