## Slide 1
Copyright © 2010 Christopher Teoh, Tan HJ & Wong WY Singapore Polytechnic. All rights reserved.
Voltage Regulators
Chapter 19: Diode Applications (Part 3)

## Slide 2
After completing Part 3 of this chapter, you will be able to:
Understand the block diagram of a basic power supply
Determine line regulation and load regulation
Understand the function of a linear IC voltage regulator and differentiate between positive and negative voltage regulators.
Objectives

## Slide 3
A power supply is an essential part of each electronic system from the simplest to the most complex.
The dc supply converts the standard 230V, 50Hz ac available at wall outlets into a constant dc voltage
This is used to power all types of electronic circuits such as:
  Television receivers
  Stereo systems
  VCRs
  CD players
  Lab equipment
Basic DC Power Supply
19-4 Voltage Regulation

## Slide 4
Transformer - steps down the ac voltage at the primary
Rectifiers - convert ac voltage into dc voltage
Filter – eliminates the fluctuations in the rectified voltage and produces a relatively smooth dc voltage
Voltage regulator - maintains a constant dc voltage for variations in the input line voltage or in the load
Load – a circuit for which the power supply is producing the dc voltage and load current
Basic DC Power Supply

## Slide 5
AC input
Step-down
Transformer
Filter
Voltage
Regulator
Rectifier
Load
Block Diagram of a
DC Power Supply
230V, 50Hz
Rectified
Voltage
Filtered
Voltage
Step-downed
Voltage
Regulated Voltage

## Slide 6
The main function of a voltage regulator is to maintain constant output voltage when
(a) its input voltage changes
(b) the load connected to it changes
Two basic categories of voltage regulation are
  Line regulation
  Load regulation
Line regulation maintains a nearly constant output voltage when the input voltage varies.
Load regulation maintains a nearly constant output voltage when the load varies
Voltage Regulation

## Slide 7
Line Regulation

## Slide 8
When the dc input (line) changes, voltage regulator must maintain a nearly constant output voltage.
This is defined as the percentage change in the output voltage for a given change in the input (line) voltage
Line Regulation

## Slide 9
When the amount of current through a load changes due to a varying load resistance, the voltage regulator must maintain a nearly constant output voltage across the load.
This is defined as the percentage in output voltage for a given change in load current
Voltage regulator
Voltage regulator
VIN
Increase
(or decrease)
VIN
No change
Load Regulation

## Slide 10
EXAMPLE 19-4

## Slide 11
Generally, the linear regulators are three-terminal devices that provide either positive or negative output voltages that can be either fixed or adjustable.
Fixed Positive Linear Voltage Regulators
Although many types of IC regulators are available, the 7800 series of IC regulators are representative of three-terminal devices that provide a fixed positive output voltage.
19-5 Integrated Circuit Voltage Regulator

## Slide 12
The three terminals are input, output, and ground.
The last two digits in the part number designate the output voltage.
Positive
input
Positive
output
The output capacitor acts basically as a line filter to improve transient response.
The input capacitor is used to prevent unwanted oscillations when the regulator is some distance from the power supply filter such that the line has high inductance

## Slide 13
Fixed Negative Linear Voltage Regulators
The 7900 series is typical of three-terminal IC regulators that provide a fixed negative output voltage.
This series is the negative-voltage counterpart of the 7800 series and shares most of the same features and characteristics.

## Slide 14
A dual-polarity power supply schematic.
230Vac
Can you identify the various components in the power supply?

## Slide 15
Voltage regulators maintain a constant dc output voltage as long as the input voltage or load varies within limits.
Three terminal linear IC regulators are available to provide either fixed-value or variable value output voltages of positive or negative polarities.
The 7800 and 7900 series regulators provide fixed-value positive and negative output voltages respectively.
Summary

## Slide 16
End of Chapter 19 (Part 3)