## Slide 1
Zener Diodes
Chapter 20: Special Purpose Diodes (Part 1)

## Slide 2
After completing Part 1 of this chapter, you will be able to:
To understand the characteristics and operation of a Zener diode.
To determine Zener impedance
Objectives

## Slide 3
Zener diodes behave like ordinary diodes when forward-biased
However, they are designed to breakdown in a controlled manner at a pre-determined voltage when reverse-biased
Once breakdown takes place, voltage across the diode is almost constant
Breakdown voltage is set by carefully controlling doping level during manufacture
Zener Diodes

## Slide 4
In contrast to junction diodes, zeners are designed to operate in the reverse-breakdown region
Recall that a junction diode operated in the reverse-breakdown region may cause overheating and damage
Cathode (K)
Anode (A)
Zener diode symbol
Zener Diodes

## Slide 5
VF
VR
IR (mA)
IF (mA)
0.7V
VZ
Zener-breakdown region
Operating Region of a Zener Diode
Forward-bias region
VF
VR
IR(mA)
IF (mA)
0.7V
VBR
Reverse-breakdown
Reverse-bias region
Operating Region of a Rectifier Diode
Normal Operating Region
Zener Diode vs Rectifier Diode

## Slide 6
2 types of reverse biased breakdown in Zeners
  Zener breakdown
    Occurs at low reverse voltage (typically < 5V) because of heavy doping
    Ordinary working region of Zener
  Avalanche breakdown
    Occurs typically at reverse voltage >> 5V
    Should avoid operating in this region as the Zener diode will be damaged
Breakdown in Zener Diode

## Slide 7
Operating Region
Zener Breakdown region
Avalanche Breakdown region
VZ (zener voltage) is usually specified at IZT (the zener test current), and is designated VZT
V-I Characteristic of Zener Diode
Avoid this Region
Breakdown in Zener Diode

## Slide 8
An ideal Zener is one where the breakdown characteristic is vertical
  i.e. voltage of Zener is constant regardless of current passing through
In practical Zeners, however, voltage changes in response to changes in current
DIZ in a Zener produces small changes DVZ
Practical Zener Diode

## Slide 9
ZZ is assumed constant over the full linear range of Zener current values and is purely resistive
Hence
Practical Zener Diode

## Slide 10
Hence a practical zener can be modeled as the equivalent of
  A voltage source
  A “resistor-like” property known as impedence
Model of ideal vs. practical zeners
Using Ohm’s Law, impedance of Zener Zz is
or
Practical Zener Diode

## Slide 11
EXAMPLE 20-1
A Zener diode exhibits a certain change in VZ for a certain change in IZ on a portion of the linear characteristic curve between IZK and IZM as illustrated.
What is the Zener impedance?
12mA
18mA
 IZ =6mA
IZK
IZM
IR
VR
 VZ = 30mV
Solution :
Worked example

## Slide 12
Example 20-2
IN4736 Zener diode has ZZT = 3.5, VZT = 6.8V, IZT = 37mA and IZK = 1 mA.
What is the voltage across the diode terminals when:
(i) IZ = 50 mA and (ii) IZ = 25 mA ?
Worked example

## Slide 13
IZT = 37 mA
IZ = 50 mA
 IZ = ?
IZK = 1 mA
IZM
IR
VR
 VZ
VZT = 6.8 V
Vz = ?
VZ= VZT +  VZ
 VZ
IZ = 25 mA
 IZ = ?
Vz = ?
Worked example

## Slide 14
Solution 2(i)
ΔIZ = IZ – IZT = 50 - 37 = 13mA
ΔVZ = ΔIZ x ZZT = 13mA x 3.5Ω = 45.5mV
VZ = VZT + ΔVZ = 6.8V + 45.5mV = 6.8455V
Solution 2(ii)
DIZ = IZ – IZT = 25 - 37 = -12mA
DVZ = DIZ x ZZT = (-12mA) x 3.5W = -42mV
VZ = VZT + DVZ = 6.8V + (-42mV) = 6.758V
Worked example

## Slide 15
In the past Zener Diodes were widely used to regulate D.C. voltages
But IC voltage regulators are now more commonly used for this purpose
10V
R1
R2
VZT
+
-
Voltage across R2 is always less than or equal to VZT regardless of R1 and R2 values
Zener Diode Applications

## Slide 16
A Zener diode is normally operated in the reversed-bias mode.
When a Zener diode reaches its reverse breakdown voltage level, it maintains a nearly constant voltage.
The Zener characteristics curve shows important characteristics such as Zener test voltage, Zener test current and Zener maximum voltage.
Zener impedance is defined as :
Summary

## Slide 17
17
End of Chapter 20 (Part 1)