## Slide 1: Chapter 20: Special Purpose Diodes (Part 2)
Optical Diodes

## Slide 2
This part of the chapter covers the following 2 common optical diodes :
Light Emitting Diode (LED)
Photodiode
Optical Diodes

## Slide 3
Understand and explain the characteristics and operation of an LED
Know the semiconductor materials used for different coloured LEDs
Know the common applications of LEDs
Understand and explain the characteristic and operation of a photodiode
Know the relationship between photodiode reverse current and irradiance
Know the common applications of photodiodes
After completing Part 2 of this chapter, you will be able to:
Objectives (Part 2)

## Slide 4
330W
5V
IF
Open
Close
LED Lights up
1kW
LED still lights up but becomes Dimmer
How to make LED brightness variable?
Use Variable Resistor (Trimpot)
LED are typically RED in colour. What other colours of LEDs are available?
Current Flows
What if we increase R to 1kW?
Demonstration of LED

## Slide 5: LED
Special diode that emits light when forward biased
When forward-biased, electrons cross the p-n junction recombine with holes
These recombining electrons release energy in the form of heat (a little) and light (mostly)
This process is called electroluminescence.
Cathode
Anode
LED Symbol

## Slide 6: LED
Different impurities are added during doping process to obtain different coloured light
LEDs may also emit light in the invisible part of the colour spectrum (infrared)
Typical LEDs

## Slide 7: LED
Light energy
p region
n region
+
+
Large exposed area here permits visible light to be emitted to the outside world

## Slide 8: LED – Material and Colour
LED is made of either
  Gallium Arsenide (GaAs) – Infrared light
  Gallium Arsenide Phosphide (GaAsP) – either Red or Yellow light
  Gallium Phosphide (GaP) – either Red or Green light.
Red is the most common LED colour
LED producing Blue light also available
Si and Ge are not used because they produce heat rather than light

## Slide 9: LED Brightness
Forward current
Light output
Amount of power output translated into light in an LED is directly proportional to the forward current, IF.
This means that Brightness of LED depends on IF
IF in an LED circuit is typically controlled by the resistance present in the circuit
Note, however, that too high a IF may cause LED to be damaged

## Slide 10: LED - Forward and Breakdown Voltages
LED emits light when there is sufficient forward current.
Forward voltage across an LED is greater than for diode (typically 1.2 to 3.2 V)
Reverse breakdown is also much less compared to junction diode (typically 3 to 10V)
R
+VBIAS -
IF
+VF -

## Slide 11: 7-Segment Displays
LEDs can be used as Indicator Lamps or Warning Lights
When arranged in the figure “8” they can be used to display numbers 0 - 9
This arrangement of LED is called the 7-segment display

## Slide 12: 7-Segment Displays
Each segment has a name “a” – “g”
7-segment displays come in either common anode or common cathode arrangement
Cathode
Cathode
Anode
Anode
E
D
E
D
C
Dec
C
Dec
G
F
G
F
A
B
A
B
Common Anode
Common Cathode

## Slide 13
A special diode whose reverse biased current depends on amount of light shining on it
When dark, behaves like a normal diode and allows only very little current through
  This current is the reverse biased leakage current, also called dark current
Photodiode

## Slide 14
When lighted, property changes and allows much higher current through it.
Current is proportional to light intensity
Small transparent window present to allow light to shine in
Photodiode

## Slide 15
Typical Photodiode
Symbol
l
Photodiode

## Slide 16
LIGHT OFF
LIGHT ON
Photodiode

## Slide 17
Amount of reverse current (Il) depends on amount of light irradiating the photodiode
Irradiance, H
Reverse Current (I )
Reverse-bias operation
- VR +
Il
l
Photodiode

## Slide 18
Sensitivity of different photodiodes may differ
V-I characteristic of photodiode is represented using graphs with light intensity as a 3rd variable
Intensity of light measured in mW/cm2 or in lumens/m 2 (lux)
Photodiode

## Slide 19
From these graphs, resistance of photodiode at different luminance can be calculated

## Slide 20
0.5mW/cm2
H = 20mW/cm2
From graph,
When irradiance = 0.5 mW/cm2, and reverse bias voltage VR=10V, reverse current=1.4mA.
Device Resistance
Photodiode can be used as a variable-resistance device controlled by light-intensity
At 20 mW/cm2, VR = 10 V,
current = 55mA,

## Slide 21
Applications of Optical Diodes

## Slide 22
Remote Control
Ambient Light Detector
Photodiode
Auto Flush
Consumer Devices

## Slide 23
An LED-photodiode pair for path tracking
Path Tracking

## Slide 24
Path Tracking and Obstacle Avoidance in AGV
Automated Guided Vehicle

## Slide 25
Measuring Motor Speed and Position in Optical Encoders
Optical Encoders

## Slide 26
Counting Items Passing Through a Production Line
Item Counter

## Slide 27
LEDs and Photodiodes can also be used to create a primitive colour sensor.
How do you think this can be done?
Use photodiodes with R, G and B filters
Simple Colour Sensor

## Slide 28
Light Emitting Diode (LED)
LEDs are made from special semiconductor materials such as Gallium Arsenide (GaAs) and Gallium Arsenide Phosphide (GaAsP).
A variety of LEDs emitting different coloured lights are available.
For an LED to emit light, sufficient forward bias voltage (typically about 2V) has to be applied.
Applications of LED include lamp indicators and read-out displays.
Summary

## Slide 29
PHOTODiode
A photodiode is normally operated in the reverse biased mode. A dc voltage source is used to provide the reverse bias.
The photodiode resistance decreases in response to increased light intensity. A significant reverse current flows through the photodiode as a result of the drop in photodiode resistance.
Summary

## Slide 30
End of Chapter 20