## Slide 1
Chapter 21: Bipolar Junction Transistors (Part 1)
Basic Characteristics of BJT

## Slide 2
After completing Part 1 of this chapter, you will be able to:
Describe the basic structure of the Bipolar Junction Transistor (BJT).
Differentiate between NPN and PNP transistor.
Explain how a transistor is biased and analyse transistor currents and their voltages.
Differentiate between dc alpha and dc beta of a transistor.
Differentiate between active, cut-off and saturation regions of operation.
Objectives

## Slide 3
Bipolar Junction Transistor is a device constructed using 3 alternately doped semiconductor regions
The 3 regions are either P-N-P or N-P-N.
Hence BJT is either of PNP type or NPN type
Whichever the type, the 3 doped regions are called:
    The Emitter (heavily doped)
    The Base (thin layer that is lightly doped)
    The Collector (moderately doped)
Each semiconductor region may carry a current
21-1 Transistor Structure

## Slide 4
Both PNP and NPN BJTs also have 2 p-n junctions called
  Base-Emitter junction
  Base-Collector junction
Each junction of the BJT may carry a voltage
Transistor Structure

## Slide 5
Bipolar Junction Transistor construction
Transistor Structure

## Slide 6
Collector
Base
Emitter
NPN Transistor
Collector
Base
Emitter
PNP Transistor
Standard bipolar junction transistor symbols
Transistor Structure

## Slide 7
For a BJT to operate properly, its 2 p-n junctions must be connected to appropriate circuits
These circuits are said to “bias” the transistor
21-2 Basic Transistor Operation

## Slide 8
In an NPN BJT, biasing is done as follows:
VBB
IB
B-E forward
biased
+
-
VCC
B-C reverse
biased
+
-
Base-Emitter Biasing Circuit
Collector-Emitter Biasing Circuit
IC
n
n
p
IC
IB
IE
E (n jtn)
C (n jtn)
B (p jtn)
Basic Transistor Operation

## Slide 9
In a PNP BJT, biasing is done in the reverse direction
VBB
IB
B-E forward
biased
-
+
VCC
B-C reverse
biased
-
+
Base-Emitter Biasing Circuit
Collector-Emitter Biasing Circuit
IC
p
p
n
IC
IB
IE
E (p jtn)
B
(n jtn)
C (p jtn)
Basic Transistor Operation

## Slide 10
In practice,
  VCC is usually taken directly from a power supply
  VBB is usually obtained from a voltage divider
VCC
IB
IC
VBB
+
-
Basic Transistor Operation

## Slide 11
VBB
IB
VCC
IC
IE
RB
RC
+
VBE _
+
_
VCE
+
VCB
_
VBE: dc voltage at base with respect to the emitter
VCB: dc voltage at collector with respect to the base
VCE: dc voltage at collector with respect to the emitter
Definition of Currents and Voltages
IB : dc base current
IE : dc emitter current
IC : dc collector current
Transistor Currents and Voltages

## Slide 12
IE = IC + IB
IC  IB
IB
IC
IE
NPN BJT
IB
IC
IE
PNP BJT
If IB and IC are known:
Note also that:
IE  IC
And
Transistor Currents and Voltages

## Slide 13
The ratio of IC and IE is called DC Alpha
And ratio of IC and IB is called DC Beta
DC Beta is also called hFE in transistor data sheets
DC Beta
bDC
Typical values from 20 to 200 or higher
DC Alpha
aDC
Typical values from 0.95 to 0.99 or higher but less than 1
21-3 Transistor Characteristics and Parameters

## Slide 14
DC Alpha and DC Beta are in turn related to each other as follows:
Relationship of bDC and aDC
Transistor Characteristics and Parameters

## Slide 15
VBB
IB
VCC
IC
IE
RB
RC
+
VBE _
+
_
VCE
+
VCB
_
Base Emitter Circuit Analysis to find IB
Since VBE is a forward biased p-n junction
Using circuit analysis about BE Circuit,
Transistor Circuit Analysis

## Slide 16
VBB
IB
VCC
IC
IE
RB
RC
+
VBE _
+
_
VCE
+
VCB
_
Collector Emitter Circuit Analysis to find IC
Using circuit analysis about CE Circuit,
In addition, note that
Recall also that
Transistor Circuit Analysis

## Slide 17
Example 21-1
Determine IB, IC, IE, VBE, VCE and VCB in the circuit below. The transistor has a bDC of 150
+
+
RC
120 
RB
10 k
VBB
4 V
VCC
12 V
Transistor Circuit Analysis

## Slide 18
Solution
VBE = 0.7 V
IE = IC + IB = 49.5 mA + 0.33 mA = 49.83 mA
VCC
12 V
+
+
RC
120 
RB
10 k
VBB
4 V
Using
Transistor Circuit Analysis

## Slide 19
Solution
VCC
12 V
+
+
RC
120 
RB
10 k
VBB
4V
Transistor Circuit Analysis

## Slide 20
IC vs. VCE curve for one value of IB
IE
IC
IB
RC
RB
+
VBB
_
+
VCC
_
+
_
VCE
+
VCB
_
VBE
+
_
As VCC increases, IC and VCE will also increase.
0
IC
VCE
0.2V or 0.3V
VCE(max)
A Collector Characteristic Curve governs the relationship between IC and VCE
Collector Characteristic Curves

## Slide 21
Active region
IC
VCE
Breakdown region
Saturation region
Operating Regions of a Transistor
Collector Characteristic Curves

## Slide 22
Family of IC vs VCE curves for different values of IB
IC
VCE
0
Cutoff region
IB=0
IB1
IB2
IB3
IB4
ICEO
IB1 < IB2 < IB3
Collector Characteristic Curves

## Slide 23
Transistors can be operated in:
  The cut-off region
  The active region (linear region)
  The saturation region
They should, however, NEVER be operated in the breakdown region
Collector Characteristic Curves

## Slide 24
When IB = 0 or very small (VBE<0.7V), transistor is in the cut-off region
A very small amount of collector leakage current ICEO (usually ignored) is present
VCE (cutoff) ≈ VCC
Hence,
ICEO
IB = 0
RC
RB
+ VCC
_
+
_
VCE(cut-off)
Transistor C-E circuit acts like an open switch
Since
Operation in Cut-off Region

## Slide 25
When IB = IB(sat), IC = IC(sat)
Then VCE = VCE(sat) = 0.2 or 0.3 V
IC
IB
RC
RB
+
VBB
_
+
VCC
_
+
_
VCE( SAT)
If IB is increased further, transistor reaches SATURATION.
At saturation, IC cannot increase further regardless of increases in IB
Transistor C-E circuit acts like an closed switch
Operation in Saturation Region

## Slide 26
As IB increases, IC also increases and VCE drops.
This is now the ACTIVE region of the BJT
In active region, relationship between IC and VCE are governed by the following equations:
This equation shows how IC is related to VCE and is sometimes called the DC Load Line
OR
Operation in Active Region

## Slide 27
Transistor operating in Active Region acts like an amplifier
Here IC = bIB
We have already covered this mode of operation in the previous block
Operation in Active Region

## Slide 28
Active region lies between the saturation and cut-off points.
DC Load Line
Active Region
Operation in Active Region

## Slide 29
The BJT (bipolar junction transistor) is constructed with three regions: base, collector, and emitter.
The BJT has two pn junctions
    the base-emitter junction and
    the base-collector junction.
Current in a BJT consists of both free electrons and holes, thus the term bipolar.
The base region is very thin and lightly doped compared to the collector and emitter regions.
The two types of bipolar junction transistor are the npn and the pnp.
Summary

## Slide 30
The 3 currents in the transistor are the base current (IB), emitter current (IE), and collector current (IC).
IB is very small compared to IC and IE.
The dc current gain of a transistor is the ratio of Ic to IB and is designated βDC. Values typically range from less than 20 to several hundred.
βDC is usually referred to as hFE on transistor data sheets.
The ratio of IC to IE is called αDC . Values typically range from 0.95 to 0.99.
A transistor can operate in the cut-off, active and saturation regions.
Summary

## Slide 31
End of Chapter 21 (Part 1)