## Slide 1
Chapter 21: Bipolar Junction Transistors (Part 2)
Operation Modes of a BJT Circuit

## Slide 2
After completing Part 2 of this chapter, you will be able to:
Differentiate between active, cut-off and saturation regions of operation.
Understand how a transistor is used as an electronic switch
Objectives

## Slide 3
and
21-4 The Transistor as a Linear Amplifier
A Bipolar Junction Transistor (BJT) can be used to amplify a small signal to a larger version without loss of wave shape.
For a BJT to function as a linear amplifier, it is biased to operate in its active or linear region.
Under all conditions of operation, the following relationships are observed:

## Slide 4
A BJT is commonly used as an electrically controlled electronic switch
This switch is controlled by the base current
  When IB = 0, transistor is cut-off & switch is open
  When IB is large, transistor is saturated and switch will close
Transistor is hence operated alternately in the cut-off and saturated region
21-5 Transistor as a Switch

## Slide 5
Conditions for cut off (Switch is open)
VCE(CUTOFF) = VCC – ICEORC = VCC
It is as if a switch is open between collector and emitter
RC
RB
+VCC
0V
IB = 0
IC = ICEO  0
VCE  +VCC
RC
+VCC
C
E
 +VCC
Transistor as a Switch

## Slide 6
Conditions for saturation
Base current is large, hence transistor reach saturation
VCE(SAT) = VCC – IC(SAT)RC  0.2 to 0.3V
≈ 0V
+VCC
IC(sat)
RC
C
E
VCE(sat) = 0.2 to 0.3V
+VBB
IB(min)
IC(sat)
+
_
RC
RB
+VCC
Transistor as a Switch

## Slide 7
This can be modelled as a short circuit between collector and emitter which in turn means that switch is closed
Saturated collector current and minimum base current required is given by:
Transistor as a Switch

## Slide 8
Example 21-2
  a) For transistor shown, find VCE when VIN = 0V
  b) Find minimum value of IB to saturate transistor if bDC = 100. Neglect VCE(SAT)
  c) Find maximum value of RB if VIN = 4V
+
+
RC
1k
RB
Vin
VCC
15 V
Transistor as a Switch

## Slide 9
Solution
  a) When VIN = 0V, transistor is in cut off region
  VCE = VCC = 15V
  b) Since VCE(SAT) is neglected, assume VCE(SAT) = 0
  This is the minimum value of IB to drive transistor into saturation
Transistor as a Switch

## Slide 10
c) In the base emitter circuit,
Transistor as a Switch

## Slide 11
Assume a square wave input of period 2s is applied.
When input is at 0 V, transistor is in cutoff, there is no collector current, hence LED is off.
When input is high, the transistor saturates, collector current flowing through LED causes it to emit light.
Hence, LED turns on for 1s and off for 1s.
VCC
Vin
RB
RC
LED
ON
ON
OFF
A transistor can be used to switch an LED on & off
Transistor as a Switch

## Slide 12
Example 21-3
An LED requires at least 20mA to light up sufficiently. Assume VLED = 2V when forward biased
Given that VCC = 9V, VCE(SAT) = 0.3V, RC = 270W, RB=3.3kW and bDC=50.
Determine the amplitude of the square wave input voltage to make sure the transistor saturates.
Use double the minimum value of base current to ensure saturation
Transistor as a Switch

## Slide 13
Solution
Assume VLED = 2V
Transistor as a Switch
9V
Vin
3.3kW
270W
LED
ON
ON
OFF
0.3V
b=50

## Slide 14
A transistor operates as an amplifier in the active region.
A transistor operates as an electronic switch in cutoff and saturation regions.
During cutoff, the transistor behaves like an open switch between collector and emitter.
During saturation, the transistor behaves like a closed switch between collector and emitter.
Summary

## Slide 15
End of Chapter 21