## Slide 1
Chapter 22: Transducers

## Slide 2
After completing this chapter, you will be able to:
Know three types of transducers or sensors.
Describe the principle of operation of light dependent resistors (LDRs).
Understand how an automatic lighting circuit works.
Explain how thermistors are used for temperature sensing.
Understand the operation of an automatic fire alarm circuit.
Appreciate the use of a free-wheeling diode to protect the transistor used for switching applications.
Understand the operation of a moisture sensing device and circuit.
Objectives

## Slide 3
Transducers and Sensors are devices that
  convert energy from one form to another
  produce electrical output (V or I) that is proportional to a physical change like temperature, light, sound or pressure
The following transducers are covered in this chapter :
  Light Dependent Resistor (LDR)
  Thermistor
  Moisture Sensor
Introduction

## Slide 4
LDR is a Light sensor whose resistance changes when light shines on it
Resistance of LDR depend on intensity of light received
Circuit Symbol
22-1 Light Dependent Resistor (LDR)

## Slide 5
Application: Automatic Lighting Circuit
LDR
R1
Bulb
VCC
BC108
R2
VB
+
Transistor operates when VBE = 0.7V
But VBE is dependent on VB
And VB depends on resistance across LDR which is controlled by light intensity shining on it
Remember Why?
Light Dependent Resistor (LDR)

## Slide 6
When light is bright
  resistance of the LDR is small
  VB is small
  transistor is in cut-off region
  bulb is OFF as no current flows through transistor
When it is dark
  Resistance in LDR increases
  VB is large
  Transistor is in active or saturation region
  current flows through bulb and turns it ON
Light Dependent Resistor (LDR)

## Slide 7
Other Applications
  Displays that automatically become brighter when surroundings become darker
  Security systems where alarm triggers when a beam of light is disturbed
  Automatic adjustment of shutter speed in automatic cameras based on amount of ambient light
Light Dependent Resistor (LDR)

## Slide 8
Semiconductor devices whose resistance varies with temperature
  Sensitivity about -4% / oC (-ve coefficient of temp.)
  When temperature rises, resistance decreases
Good for temperature range from –50oC to +300oC
Inexpensive and stable
Thermistor probes come in the shape of beads, thin rods, disks or washers depending on how they are used
22-2 Thermistor

## Slide 9
Very sensitive to temperature changes because of large coefficient of temperature
  Changes in resistance measurable by multimeter without need for amplification
Consider the following circuit
15 V
+
thermistor
mA
Thermistor

## Slide 10
Assume resistance at 0oC and 100oC is 60kW and 16kW respectively
With 15V supply, this would give a current range from
Thus a 0 to 1 mA ammeter calibrated for temperatures from 0oC to 100oC can be used for measuring temperature without signal amplification
Thermistor

## Slide 11
Automatic Fire Alarm Circuit
Thermistor RTH
Diode
Relay
Electric Bell
R1
VCC
R2
VB
+
Thermistor

## Slide 12
Electric bell is activated whenever temperature rises above a pre-determined level
A magnetic relay is connected at the collector terminal of the transistor
  Relays allow a low voltage circuit to control a high voltage circuit
  Also allows high current devices to be switched on/off by a circuit using much smaller current
Thermistor

## Slide 13
Relay contact
= OFF (open)
Switch = OFF
Relay contact
= ON (closed)
Switch = ON
Relay
I
Relay
Thermistor

## Slide 14
Transistor requires VBE = 0.7V to operate
Normally no fire.
Thermistor resistance is high and VBE < 0.7V. Hence transistor is OFF and alarm is not activated
Thermistor RTH
Diode
Relay
Electric Bell
R1
VCC
R2
VB
+
Thermistor

## Slide 15
When a fire breaks out, temperature increases
Thermistor resistance drops which causes VB to rise
Increase in VB results in VBE increasing until it reaches the 0.7V necessary to activate the transistor
With transistor activated, current flows through the coil of the relay
This closes the relay contact thereby triggering the electric bell
Thermistor

## Slide 16
When transistor switches from ON to OFF, there is a collapse in the magnetic field around the coil
This causes a back emf to be induced in the coil (polarity shown in Figure)
Energy created by this back emf must be discharged
The only possibility now is through the transistor – this will cause it to be damaged in the process
+
Back
emf
VCC
Purpose of Free-Wheeling Diode
Thermistor

## Slide 17
If a free-wheeling diode is inserted, energy can now be discharged safely through it.
This protects the transistor from being damaged
Under normal operating conditions, the diode does not affect the operation of the circuit as it is reversed bias - equivalent to an open circuit
Free Wheeling Diode
VCC
+
Back
emf
I
Purpose of Free-Wheeling Diode
Thermistor

## Slide 18
Other thermistor applications
  To automatically switch a kettle off when water has reached boiling point
  To maintain constant temperature in air-conditioning and heating systems
Thermistor

## Slide 19
Operates on principle that water is a better conductor of electricity compared to air
Resistance between the moisture sensor contacts changes in the following manner
  High resistance (open circuit) when dry
  Low resistance (closed circuit) when wet
22-3 Moisture Sensor

## Slide 20
AC Supply
Diode
Relay
VCC
R
Moisture
Sensor
Motor
Moisture Sensor Circuit
Moisture Sensor

## Slide 21
Under dry conditions
  moisture sensor is a virtual open circuit
  No current flows into base of BJT
  Transistor is in cut-off region and motor is off
Moisture Sensor

## Slide 22
When raining
  Droplets of water fall onto the plate gap of sensor
  Base current now flows into the transistor
  Transistor becomes active (or saturated) and current flows through the relay coil
  Relay contacts change from “open” to “closed”
  Motor (connected to window closing mechanism or clothes-line retractor) will then be activated
Moisture Sensor

## Slide 23
Other Applications of Moisture Sensor
  Parent Alert System for Baby Soiling his bed
  Monitoring of Soil Moisture condition
  Automatic wind screen wiper
Moisture Sensor

## Slide 24
The 3 commonly used transducers are Light Dependent Resistor (LDR), Thermistor and Moisture Sensor.
An LDR can be used in an automatic lighting circuit.
A thermistor, together with a voltage source and a milli-ammeter, can be set up to measure temperature.
A thermistor is used in an automatic fire alarm circuit.
A moisture sensor can be used to automatically close windows when it rains
Summary

## Slide 25
End of Chapter 22