## Slide 1
Op Amp Characteristics & Negative Feedback
Chapter 23: Operational Amplifiers (Part 1)

## Slide 2
Understand the characteristics of an amplifier.
List the characteristics of ideal and practical op-amps.
Identify the three input modes of op-amps.
Explain the importance and advantages of applying negative feedback in op-amp circuits.
After completing Part 1 of this chapter, you will be able to:
Objectives

## Slide 3
Components like resistors, diodes, transistors are discrete components.
These components are individually packaged and have to be interconnected with each other to form a complete, functional unit.
Linear integrated circuits (ICs) are devices with many discrete components fabricated onto a single chip of semiconductor material
They are packaged in a single component to form a functional circuit.
Introduction

## Slide 4
An IC is treated as a single device – i.e. we are interested in what the circuits can do from an external viewpoint.
We have already encountered ICs which are logic gates in Digital Electronics
In this chapter, we will study the operational amplifier IC
Op-amps are among the most versatile and widely used of all ICs
Introduction

## Slide 5
To understand the characteristics of an ideal op-amp and how they differ from that of a real amplifier, it is necessary for us to understand the following:
  The need for an amplifier
  Amplification (gain)
  Bandwidth
  Input & output impedances, and
  Distortion
Background on Characteristics of Amplifiers

## Slide 6
Amplifiers
When watching the news on TV, you increase the volume if you were unable to hear the newscaster’s voice.
When the picture on your TV gets too dark, you increase the brightness control.
In both of these cases, you are taking a relatively weak ac signal and making it stronger (increasing its power).
The process of increasing the power of an ac signal is called amplification.
The circuits used to perform this function are called amplifiers.
The most common types of amplifiers are voltage, current and power amplifiers.

## Slide 7
Infinite voltage gain, AV = 
Infinite input impedance, Zin = 
Zero output impedance, Zout = 0
Infinite bandwidth, BW = 
Zero Distortion (or Input/output relationship = linear)
( i.e. Vo is proportional to Vi )
An Ideal Amplifier should have
Ideal Amplifier Characteristics

## Slide 8
Gain
Amplifiers are circuits that exhibit a property called gain.
E.g., if an amplifier has a voltage gain of 100, the output voltage is 100 times larger than the input voltage under normal operating conditions.
The gain of an amplifier is determined by the amplifier’s circuit component values.
VIN
VOUT
= AV VIN
Voltage
Gain,
AV
Voltage Amplifier
The gain of an amplifier is a multiplier that exists between the input and output.

## Slide 9
Bandwidth
Voltage Gain
Frequency
AV
Lower cutoff frequency
Upper cutoff frequency
0.7071AV
The gain of the amplifier is not uniformed – it falls after a certain frequency
The range of frequencies over which a useful gain is available is called the bandwidth of the amplifier.
Bandwidth of an amplifier depends on the circuit component values and the type of active component(s) used.
Bandwidth

## Slide 10
Input Impedance
Impedance measured
between the input terminals
Output Impedance
Impedance measured
between the output terminals
Input
Output
Amplifier
Impedance is a resistance-like property
Input Impedance ()
and Output Impedance ()

## Slide 11
While output signal > input signal, it must also retain the same shape as the input signal – linear input and output relationship
If the shape of the output signal no longer resembles the input signal, the output signal is distorted – this is undesirable.
Amplifier
VIN
VOUT
Undistorted Output
Distorted Output
Distortion

## Slide 12
Early op-amps were used mainly to perform mathematical operations like addition, subtraction, integration and differentiation – hence the term “operational”
Symbol and Terminals
23-1 Introduction to Op Amps

## Slide 13
Introduction to Op Amps

## Slide 14
Small size of an
Opertional Amplifier
(op-amp)

## Slide 15
The Ideal Op Amp
infinite voltage gain
infinite bandwidth
infinite input impedance
zero output impedance
Input voltage Vin appears between the two input terminals
Output voltage is AvVin , as indicated by the internal voltage source symbol.
AV Vin
ZOUT= 0
AV = ∞
ZIN = ∞
+
VOUT
VIN
Ideal op-amp representation

## Slide 16
AV Vin
ZOUT
ZIN
+
VIN
Practical op-amp representation
very high voltage gain
very high input impedance
very low output impedance
wide bandwidth
Characteristics of a practical op-amp
Peak-to-peak output voltage usually limited to slightly less than the two supply voltages.
Output current also limited by internal restrictions such as power dissipation and component ratings.
The Practical Op Amp

## Slide 17
+
+VS
-VS
VO
Modes of Signal Operation
Op-amp circuits use one of three basic input modes of operation:
- Single-Ended Input
- Differential Input
- Common-Mode Input
Single-ended input mode has one input connected to the input signal and the other connected to ground.
23-2 Op Amp Input Modes

## Slide 18
The inputs of a differential input circuit are connected to different signal sources.
In the case of common-mode input, both inputs are connected to the same signal source.
+
+VS
-VS
VO
V1
V2
+
+VS
-VS
VO

## Slide 19
The limit on the output voltage is set by the supply voltages.
The upper limit is called the positive saturation voltage (+Vsat) and it is approximately within 1V of +V.
The lower limit is called the negative saturation voltage (-Vsat) and it is approximately within 2V of -V.
With a supply voltage of +/-15V, +Vsat = +14V and -Vsat = -13V. Therefore Vo is restricted to a symmetrical peak-to-peak swing of +/-13V.
Output Voltage

## Slide 20
The open-loop voltage gain of an op-amp is the internal voltage gain of the device and represents the ratio of output voltage to input voltage when there are no external components.
The open-loop voltage gain is set entirely by the internal design.
Open-loop voltage gain can range up to 200,000 and is not a well-controlled parameter.
Data sheets often refer to the open-loop voltage gain as the large-signal voltage gain.
23-3 Op Amp Open Loop Voltage Gain ()

## Slide 21
Negative feedback is one of the most useful concepts in electronics, particularly in op-amp applications.
Negative feedback is the process whereby a portion of the output voltage of an amplifier is returned to the input with a phase angle that opposes (or subtracts from) the input signal
23-4 Op Amp with Negative Feedback ()

## Slide 22
Why Use negative Feedback?
Very high (usually greater than 100,000) inherent open-loop voltage gain of a typical op-amp
Extremely small input voltage drives the op-amp into saturation
For example, assume VIN = 1 mV and Aol = 100,000. Then,
Since the output level of an op-amp can never reach 100 V, it is driven deep into saturation and the output is limited to its maximum output levels, for both a positive and a negative input voltage of 1 mV.
VOUT = Vin Aol = (1 mV)(100,000) = 100V

## Slide 23
With negative feedback, the closed-loop voltage gain (Aol) can be reduced and controlled so that the op-amp can function as a linear amplifier.
Without negative feedback, a small input voltage drives output to its limits and becomes non-linear
-1mV
+
+VS
-VS
VO
+Vsaturation
+
+VS
-VS
VO
+1mV
-Vsaturation

## Slide 24
In addition to providing a controlled, stable voltage gain, negative feedback also provides for control of the input and output impedances and amplifier bandwidth.
 | Voltage Gain | Input Impedance | Output Impedance | Bandwidth
Without negative feedback | Aol is too high for linear amplifier applications | Relatively high | Relatively low | Relatively narrow (because the gain is so high)
With negative feedback | Aol is set to desired value by the feedback circuit | Can be increased or reduced to a desired value depending on type of circuit | Can be reduced to a desired value | Significantly wider

## Slide 25
The extremely high open-loop gain of an op-amp creates an unstable situation
  small input noise voltage amplified such that amplifier is driven out of its linear region
  can also cause unwanted oscillations
Open-loop gain parameter of an op-amp can vary greatly from one device to another
Negative feedback creates an effective reduction in gain by taking a portion of the output and applies it back out of phase the input
Closed-loop gain is usually much less than the open-loop gain and independent of it
Op Amp Configurations with Negative Feedback

## Slide 26
The closed-loop voltage gain
   voltage gain of an op-amp with external feedback
The amplifier configuration
   op-amp and an external negative feedback circuit connecting output to the inverting input
The closed-loop voltage gain
   determined by external component values and can be precisely controlled by them
Closed-loop Voltage Gain ()

## Slide 27
Effects of Negative feedback
Applying negative feedback to an op-amp gives rise to two important conditions which are:
  The input voltages at the inverting and non-inverting terminal are forced to be equal.
  i.e. V_ = V+
The input currents to both the inverting and non-inverting terminals are zero ( ie. no input current flowing into the op-amp).
IIN = 0
IIN = 0
V
V+
+
-VS
VS
VO
Equal

## Slide 28
A basic op-amp has 2 input terminals (one inverting and the other, non-inverting) as well as one 0utput terminal.
A practical op-amp has very high input impedance, very low output impedance, very high open-loop voltage gain and a very wide bandwidth.
The 3 input modes of an op-amp are :
- single-ended input mode
- differential input mode
- common mode input
Summary

## Slide 29
Open-loop op-amp operation does not have external feedback connections
Closed-loop op-amp operation involves external feedback connections.
The output of an op-amp is limited to +Vsat and –Vsat.
The advantages of incorporating negative feedback are :
- closed-loop gain can be controlled
- wider bandwidth
- input and output impedance can be controlled
Summary

## Slide 30
End of Chapter 23 (Part 1)