## Slide 1
Non-inverting Amplifiers & Voltage Followers
Coverage :
Section 22-5 (Pg 455 – 460) of textbook
Chapter 23: Operational Amplifiers (Part 2)

## Slide 2
• Understand how an op amp can be configured as an non-inverting amplifier and a voltage follower.
• Analyse and solve problems involving non-inverting amplifier and voltage follower circuits.
After completing Part 2 of this chapter, you will be able to:
Objectives

## Slide 3
Recap : Amplifier Performance
Amplifier
Voltage Gain
AV
VIN
VOUT
Undistorted
Output
Distorted
Output
VOUT = AV VIN
Good
Bad

## Slide 4
With negative feedback, the closed-loop voltage gain (Aol) can be reduced and controlled so that the op-amp can function as a linear amplifier.
Without negative feedback, a small input voltage drives output to its limits and becomes non-linear
-1mV
+
+VS
-VS
VO
+Vsaturation
+
+VS
-VS
VO
+1mV
-Vsaturation
RECAP : OP AMP in Open Loop Configuration (No negative Feedback)

## Slide 5
Negative feedback is one of the most useful concepts in electronics, particularly in op-amp applications.
Negative feedback is the process whereby a portion of the output voltage of an amplifier is returned to the input with a phase angle that opposes (or subtracts from) the input signal
23-5 Basic Op Amp Configurations

## Slide 6
RECAP : OP-AMP CONFIGURATIONS WITH NEGATIVE FEEDBACK
The extremely high open-loop gain of an op-amp creates an unstable situation
  small input noise voltage amplified such that amplifier is driven out of its linear region
  can also cause unwanted oscillations
Open-loop gain parameter of an op-amp can vary greatly from one device to another
Negative feedback creates an effective reduction in gain by taking a portion of the output and applies it back out of phase the input
Closed-loop gain is usually much less than the open-loop gain and independent of it

## Slide 7
RECAP : Closed-Loop Voltage Gain, Acl
The closed-loop voltage gain
   voltage gain of an op-amp with external feedback
The amplifier configuration
   op-amp and an external negative feedback circuit connecting output to the inverting input
The closed-loop voltage gain
   determined by external component values and can be precisely controlled by them

## Slide 8
RECAP : Effects of Negative Feedback
Two important conditions must be remembered when we analyse the closed-loop circuit with negative feedback:
  The input voltages at the inverting and non-inverting terminal are equal.
  i.e. V_ = V+
The input currents to both the inverting and non-inverting terminals are zero ( ie. no input current flowing into the op-amp).
IIN = 0
IIN = 0
V
V+
+
-VS
VS
VO
Equal

## Slide 9
Since the input current to the op-amp can be considered as zero, the same current that flows through Rf will also flow into Ri
Due to negative feedback, V+ = V-
Vout = I Ri + I Rf = I (Ri + Rf )
I
V+
Hence
IIN = 0
+
Vin
-VS
VS
Vout
Rf
Ri
V
Since V+ = Vin and V- = I Ri
therefore, Vin = I Ri
Non-Inverting Amplifier

## Slide 10
The expression is positive and this indicates that the output signal is in-phase with the input signal.
The closed loop voltage gain for non-inverting amplifier is 
The output voltage is 
The input impedance Zin = extremely high
(approx. infinity)
The output impedance Zout = extremely low
(approx. zero)
Non-Inverting Amplifier

## Slide 11
EXAMPLE 23-1
For the amplifier above :
  Determine the voltage gain, Av .
  Determine the output voltage, Vo .
  Sketch the input and output voltage waveforms with phase relation.
  Sketch the output waveform if the value of Rf is first changed to 90 kW and later 190 kW.
+
-
Rf
Vo
V-
V+
Ri
Vi
10kW
(40kW)
2 V(p-p)
+15V
-15V

## Slide 12
+
-
Rf
Vo
V-
V+
Ri
Vi
10kW
(40kW)
2 V(p-p)
+15V
-15V
Solution :
The voltage gain,
Vo = Acl Vi
= 5 x 2Vp-p
= 10 V(p-p)
The output voltage,
Vi
1V
5V
Vo1 (Acl = 5)

## Slide 13
+
-
Rf
Vo
V-
V+
Ri
Vi
10kW
(40kW)
2 V(p-p)
+15V
-15V
d. Value of Rf is
changed to 90 kW
90 kW
Vo = Acl Vi
= 10 (2)
= 20 V(p-p)
Vi
1V
Vo2 (Acl = 10)
10V

## Slide 14
+
-
Rf
Vo
V-
V+
Ri
Vi
10kW
(40kW)
2 V(p-p)
+15V
-15V
d. Value of Rf is
changed to 190 kW
190 kW
Vo = Acl Vi
= 20 (2)
= 40 V(p-p)
Vi
1V
Output voltage forced into saturation causing the output waveform to be distorted
Vsat
-Vsat
Vo3 (Acl = 20)
Distortion
Distortion
Vsat depends on supply to op-amp.
It is typically 1 or 2 volts smaller

## Slide 15
This is a special case of non-inverting amplifier where:
Rf = 0 and Ri = 
Due to extremely large voltage gain of op-amp, differential input voltage is zero when the –ve feedback loop is closed.
For voltage follower: Vout = Vin
The voltage gain, Av of voltage follower is hence:
V+
V
+
Vin
-VS
VS
Vout
Hence V+ = Vi
Voltage Follower

## Slide 16
A voltage follower has the following characteristics:
  Extremely high input impedance
  Extremely low output impedance
  Capable of driving a relatively low resistive load due to its very small output impedance
  Often used as buffer circuit to match a high internal resistance signal source to a low resistive load (illustration on the next slide)
Voltage Follower

## Slide 17
1Vp-p
VS
0.1Vp-p
VO
1Vp-p
VS
9 kW
1 kW
Source
Load
9 kW
1 kW
Source
Load
-VS
VS
+
VO
1Vp-p
Smaller output voltage due to high source resistance
Output voltage equals the
input voltage since Vin = Vout
Example of an application of a voltage follower

## Slide 18
With negative feedback, the op-amp can be configured as an non-inverting amplifier and a voltage follower.
The closed loop voltage gain for non-inverting amplifier is
The output signal of a non-inverting amplifier is in-phase with the input signal.
For voltage follower: Vout = Vin. This means that the voltage gain of a voltage follower is 1.
A voltage follower is often used as buffer circuit to match a high internal resistance signal source to a low resistive load
Summary

## Slide 19
End of Chapter 23 (Part 2)