## Slide 1
Inverting & Summing Amplifiers
Chapter 23: Operational Amplifiers (Part 3)

## Slide 2
• Understand how an op amp can be configured as an inverting amplifier.
• Understand summing, scaling, averaging and other types of amplifier circuits.
After completing Part 3 of this chapter, you will be able to:
Objectives

## Slide 3
+
Vin
-VS
VS
Vout
Rf
Ri
As V- is not physically connected to the ground unlike V+, it is referred to as virtual ground.
Since V+ is connected to ground, V- will also be at ground potential.
V+
V
Virtual ground
With negative feedback applied,
V- = V+
Inverting Amplifier

## Slide 4
Inverting Amplifier
Current flowing through Ri is:
Ii
Current flowing through Rf is:
If
Since no current flows into the input terminals, Ii is fully diverted into the feedback resistor Rf. Thus
I = 0
0V
+
Vin
-VS
VS
Vout
Rf
Ri

## Slide 5
Inverting Amplifier
The negative sign in the expression denotes that the output signal is 180 ° out-of-phase with the input signal.
The output voltage is:
The input impedance Zin = Ri
The output impedance Zout = output impedance of op-amp
The closed loop voltage gain for Inverting Amplifier is:

## Slide 6
Example 23-2
For the circuit shown above,
  Determine the output voltage, Vo .
  Sketch the input and output voltage waveforms with phase relation.
  If the input voltage is doubled, what will the new value of the output voltage, Vo ?
+
-
R1 (1 kW)
Vi
Vo
V-
V+
R1 (10 kW)
2 V(p-p)
+15V
-15V
Solution:
a)

## Slide 7
+
-
R1 (1 kW)
Vi
Vo
V-
V+
R1 (10 kW)
2 V(p-p)
+15V
-15V
  b) Sketch the input and output voltage waveforms with phase relation.
10V
20Vp-p
Vout
Vi
1V
2Vp-p
14V
+Vsat
-14V
-Vsat

## Slide 8
Vout
+
-
R1 (1 kW)
Vi
Vo
V-
V+
R1 (10 kW)
2 V(p-p)
+15V
-15V
  c) If the input voltage is doubled, what will the new value of the output voltage, Vo ?
Vi
2V
4Vp-p
14V
+Vsat
-14V
-Vsat
4V(p-p)

## Slide 9
Summing Amplifiers
Variation of the inverting amplifier
Has two or more inputs, and its output voltage is proportional to the negative of the algebraic sum of its input voltages
Variations of the summing amplifier includes the
  averaging amplifier and
  scaling amplifier

## Slide 10
Summing Amplifier
Since virtual ground exists at the inverting input terminal,
V+
V
+
-VS
VS
Vout
Rf
R1
Virtual ground
R2
V IN1
V IN2
I1
I2
If
Current flowing through Rf is:

## Slide 11
Summing Amplifier
If
Since no current flows into the op-amp input terminals, I1 and I2 are fully diverted into the feedback resistor Rf. Thus
If = I1 + I2
Since
V+
V
+
-VS
VS
Vout
Rf
R1
R2
V IN1
V IN2
I1
I2
If
Virtual Ground

## Slide 12
If all the three resistors are equal i.e.
(R1 = R2 = Rf = R)
+
-VS
VS
Vout
R
R
R
V IN1
V IN2
Summing Amplifier with Unity Gain

## Slide 13
+
-VS
VS
R
R
R
V IN1
V IN3
R
V IN2
R
V INn
Summing Amplifier with “n” Identical Input Resistors

## Slide 14
When Rf is larger than the input resistors, the amplifier has a gain of Rf /R
The general expression for the output is:
+
-VS
VS
Vout
Rf
R
R
V IN1
V IN3
R
V IN2
R
V INn
Summing Amplifier with Gain Greater Than Unity

## Slide 15
Multi-channel Scaling Amplifier
+
-VS
+VS
2 kW
V IN1
V IN3
V IN2
5 kW
10 kW
Rf = 20 kW
Vout
Example:
By using different values of R1, R2, R3 …….Rn, the inputs of a summing amplifier can be subjected to different voltage gains
The output voltage can thus be expressed as:

## Slide 16
Example 23-3
+
-VS
VS
Vout
15kΩ
V IN1 = 1V
V IN2 = 2V
15kΩ
15kΩ
15kΩ
V IN3 = 3V
Calculate Vout for the circuit below

## Slide 17
Example 23-4
Determine the output voltage for the amplifier shown
+
-VS
VS
Vout
R1 = 1kΩ
V IN1 = 0.2V
V IN2 = 0.5V
R2 = 1kΩ
Rf = 10kΩ

## Slide 18
Example 23-5
A four-input amplifier has 4 equal-value resistors of 120kΩ each and a feedback resistor of 30kΩ. Calculate the amplifier output voltage if the 4 input signals are 1V, 2V, 3V and 4V respectively.
Solution
Since the input resistors are all equal to 120kΩ, the output voltage is :

## Slide 19
A summing amplifier can be made to produce the mathematical average of the input voltages.
+
-VS
VS
3 kW
V IN1
V IN3
V IN2
3 kW
3 kW
Rf = 1 kW
Ratio Rf /R equal to the reciprocal of no. of inputs (n)
Averaging Amplifier

## Slide 20
With negative feedback, the op-amp can be configured as an inverting amplifier.
The closed loop voltage gain for an inverting amplifier is
The output signal of an inverting amplifier is 180o out of phase with the input signal.
A summing amplifier has two or more inputs, and its output voltage is proportional to the negative of the algebraic sum of its input voltages.
Summary

## Slide 21
If the input and feedback resistors of a summing amplifier has identical values, the gain of the amplifier will be 1. The output voltage is given by :
Vout = VIN1 + VIN2 + VIN3 + ….. + VINn
If the feedback resistor, Rf, has different values from the input resistors, R, the amplifier has a gain of Rf /R. The output voltage is given by :
Summary

## Slide 22
By using different values of R1, R2, R3 …….Rn and Rf, the inputs of a summing amplifier can be subjected to different voltage gains. This type of summing amplifier is also known as Multi-Channel Scaling Amplifier and its output voltage is given by :
A summing amplifier can be made to produce the mathematical average of the input voltages if
Summary

## Slide 23
End of Chapter 23 (Part 3)