## Slide 1
Comparators
Chapter 23: Operational Amplifiers (Part 4)
Coverage :
Section 23-7 (Pg 468 – 474) of textbook

## Slide 2
Understand the operation of basic comparator circuits.
Understand the use of hysteresis to reduce the effect of noise.
After completing Part 4 of this chapter, you will be able to:
Objectives

## Slide 3
COMPARATORS
Op-amps used as comparators:
  compare amplitudes of one voltage with another
  determines when an input voltage exceeds a certain level
Achieved by operating in open-loop configuration - input voltage on one input and a reference on the other
Can you recall the implications of operating op-amps in the open-loop configuration? (hint: it has to do with the voltage gain)

## Slide 4
+
-15V
+15V
Vout
V_
V+
Vout = Aol Vin
= Aol ( V+ - V- )
Op Amp in the Open-loop Configuration

## Slide 5
3 major types of Op-Amp Comparators:
Zero level comparator (or detector)
Non-zero level comparator
Comparator with hysteresis
23-7 Op Amp Comparators

## Slide 6
+
Vin
-15V
+15V
Vout
Very small difference in voltage between the two inputs drives the amplifier into saturation
E.g. If Aol = 100,000 & voltage difference between the inputs = 0.25mV
Output voltage = (0.25mV)(100,000) = 25V
The op-amp will be driven into saturation.
Zero Level Comparator

## Slide 7
Vout
+Vo(sat)
-Vo(sat)
To predict the output voltage of a comparator is to compare the voltages at V+ and V_
V+ > V_ causes Vout = +Vsat
t
t
Vin = V+
V_ = 0V
V+> V_
V_> V+
V_> V+ causes Vout = -Vsat
+
Vin
-15V
+15V
Vout
V_
V+

## Slide 8
V+
+
Vin
-15V
+15V
Vout
V_
Vref
V+
+
Vin
-15V
+15V
Vout
V_
Vref
R1
R2
V+ > V_ Vout = +Vo(sat)
V_ > V+ Vout = -Vo(sat)
Non-zero Level Comparator

## Slide 9
V+> V_
V+> V_
V+
+
Vin
-15V
+15V
Vout
V_
Vref
Vout
+Vo(sat)
-Vo (sat)
t
t
V_ = Vref
Vin = V+
V+ > V_ Vout = +Vo(sat)
V_> V+
V_ > V+ Vout = -Vo(sat)
Non-zero Level Comparator

## Slide 10
Copyright © 2005 Tan Hua Joo, Singapore Polytechnic
EXAMPLE 23.6
10
23-32
23-32
23-33

## Slide 11
In many practical situations, unwanted voltage fluctuation (noise) appear on the input line
Sine wave with
superimposed noise
This noise voltage becomes superimposed on the input voltage and can cause a comparator to erratically switch output states
Effects of Input Noise on Comparator Operation

## Slide 12
Effects of noise on comparator circuit

## Slide 13
+
Vin
-VS
+VS
Vout
R2
R1
To make the comparator less sensitive to noise, applying positive feedback in an op-amp circuit - hysteresis
Hysteresis  higher reference level when the input voltage goes from a lower to a higher value than when it goes from a higher to a lower value
The two reference voltages are referred to as the upper trigger point (UTP) and the lower trigger point (LTP)
Reducing Noise Effect with Hysteresis

## Slide 14
Assuming that the output voltage is at its positive maximum, +Vo(sat)
The voltage fed back to the non-inverting input is VUTP expressed as:
Vin<VUTP
+Vo(sat)
VUTP
Output at the maximum positive voltage
+
-VS
+VS
R2
R1
-Vo(sat)
VUTP
+Vo(sat)
Vin
VUTP
+
-VS
+VS
R2
R1
Input exceeds VUTP , output switches from the maximum positive voltage to the maximum negative voltage

## Slide 15
When the input voltage exceeds VUTP, the output voltage drops to its negative maximum, -Vo(sat)
Now the voltage fed back to the non-inverting input is VLTP expressed as:
Vin>VLTP
-Vo(sat)
VLTP
Output at the maximum negative voltage
+
-VS
+VS
R2
R1
Input goes below LTP, output switches from the maximum negative voltage to maximum positive voltage
VLTP
-Vo(sat)
+Vo(sat)
Vin
VLTP
+
-VS
+VS
R2
R1

## Slide 16
V- = Vin
V+ = VLTP
V+ = VUTP
0
+Vout(max)
-Vout(max)

## Slide 17
To switch from the maximum negative voltage back to the maximum positive voltage, input voltage must now fall below VLTP
Small amount of noise voltage therefore has no effect on the output
A comparator with hysteresis is also called a Schmitt trigger
The amount of hysteresis is defined by the difference of the two trigger levels
VHYS = VUTP - VLTP

## Slide 18
EXAMPLE 23-7
Calculate the upper and lower trigger points for the comparator circuit shown below. Assume +Vsat = 8V and –Vsat = -8V
+
Vin
-VS
+VS
Vout
R2 = 120KΩ
R1 = 120KΩ
Solution

## Slide 19
Comparators consist of op-amps that operate in the open-loop mode.
The zero-level comparator (or detector) compares the input signal with zero voltage level.
With the hysteresis feature, a comparator switches output states only when the input signal exceeds either the preset upper trigger point (UTP) or lower trigger point (LTP).
Summary

## Slide 20
Summary

## Slide 23
End of Chapter 23