## Slide 1
Chapter 17: RLC Circuits (Part 1)
Series RLC Circuits

## Slide 2
At the end of the chapter (Part 1), the student will be able to:
Know the types of RLC circuits
Determine AC impedance of series RLC circuits
To analyse a series RLC circuit
Understand the phasor relationship between applied voltages and circuit current in series RLC circuits
Draw impedance and phasor diagrams of series RLC circuits
Objectives

## Slide 3
The 3 main topics covered in this chapter:
Analysis of series RLC circuits
Analysis of parallel RLC circuits (in Part 2)
Power and power factor in RLC circuits (in Part 2)
Introduction

## Slide 4
Impedance of capacitor is –jXC (imaginary).
where XC is called the capacitive reactance.
In an ac circuit, opposition to current flow is called impedance. Unit is ohm (Ω)
  Impedance of resistor is R(real).
Revision

## Slide 5
Impedance of inductor is jXL.
where XL is called the inductive reactance.
Impedances in series: ZT = Z1 +Z2 + …+Zn
Impedances in parallel:
2 impedances in parallel:
Revision

## Slide 6
Impedance of Series RLC Circuit
The total impedance of the series RLC circuit shown is the sum of the impedance of the resistor, inductor and capacitor.
VC
VS
I
VR
VL
R
-jXC= XC-90o
jXL= XL90o
17-1 Analysis of series RLC Circuits

## Slide 7
Real part of is contributed by resistors.
Imaginary part of is contributed by inductors and capacitors.
In Polar form, this is:
Impedance of Series RLC Circuit

## Slide 8
the imaginary part of Z can be either positive or negative depending on the value of XL and XC
If XL > XC, then the imaginary part of Z will be positive and the RLC circuit is net inductive.
If XL < XC, then the imaginary part of Z will be negative and the RLC circuit is net capacitive.
Impedance of Series RLC Circuit

## Slide 9
For case of XL > XC
R
jXL
-jXC
Z

OR
R

j(XL-XC)
Z
j(XL-XC)
Impedance Diagram

## Slide 10
For case of XC > XL (not in text book)
R
jXL
-jXC
-
Z
-j(XL-XC)
OR
R
-
-j(XL-XC)
Z
Impedance Diagram

## Slide 11
I is the common electrical quantity in a series circuit.
I chosen as reference phasor
Supply voltage:
 is the phase between and
Voltages and Current in Series RLC Circuit

## Slide 12
Ohm’s Law relates the voltages, current and impedances in the circuit
Kirchhoff’s Voltage Law relates the voltages in the circuit
Applying Circuit laws to Series RLC Circuit

## Slide 13

VR
VS
VL
I
VC
VS leads I by  where
(For case of VL > VC)
VL-VC
OR
VS

I
VR
VL-VC
Phasor Diagram

## Slide 14
1. Impedance diagram and phasor diagram are similar and are related by I since the impedance diagram when multiplied with the circuit current becomes the phasor diagram.
2. The phase of the circuit impedance and the phase of the applied voltage is the same:
Relationship Between Impedance Diagram and Phasor Diagram

## Slide 15
1. Calculate circuit impedance:
2. Calculate the circuit current:
3. Calculate:
4. Draw phasor and impedance diagrams if necessary
Analysis Procedure

## Slide 16
Example 17-1
Calculate total circuit impedance, current and the voltage drops across the resistor, inductor and capacitor.
(b) Draw the impedance diagram.
(c) Draw the phasor diagram.
(d) Write the time domain sinusoidal expression of the source voltage and the circuit current.
A 75  resistor, an inductor with 25  reactance and a capacitor with 60  reactance are connected in series to a 10 V, 10 kHz ac source. Assume

## Slide 17
Solution:

## Slide 18
R=75Ω
jXL=j25Ω
-jXC= -j60Ω
j(XL-XC)=-j35Ω
-25o
Z=82.8Ω
Solution:
(b) Impedance Diagram

## Slide 19
Solution : (c) Phasor Diagram
9.08 V
VR
7.26 V
VC
VL
3.03 V
I
121 mA
i(t) = 121√2 sin(2 x 10 x 103 x t) mA
v(t) = 10√2 sin[(2 x 10 x 103 x t) – 25o] V
VL - VC
10 V
VS
-25o
(d)
Time domain sinusoidal expression

## Slide 20
Summary
The resistor voltage is in phase with the current that flows through it.
The inductor voltage leads the current that flows through it by 90o.
The capacitor voltage lags the current that flows through it by 90o.
In a series RLC circuit:

## Slide 21
End of Chapter 17 (Part 1)