## Slide 1
Chapter 17: RLC Circuits (Part 2)
Parallel RLC Circuits and Power

## Slide 2
Objectives
After completing Part 2 of this chapter, you will be able to:
Determine AC impedance and admittance of parallel RLC circuits
To analyse a parallel RLC circuit
Understand the phasor relationship between applied voltage and circuit currents in parallel RLC circuits
Draw admittance and phasor diagrams of parallel RLC circuits
Determine power and power factor of RLC circuits.

## Slide 3
Admittance and Impedance of Parallel RLC Circuits :
When dealing with parallel RLC circuits, it is more convenient to represent the resistor, inductor and capacitance by their admittances.
-jBL
G
IR
IL
I
VS
jBC
IC
17-2 Analysis of Parallel RLC Circuits

## Slide 4
G : conductance
Admittance of a parallel circuit
Revision

## Slide 5
where
Admittance and Impedance of Parallel RLC Circuit

## Slide 6
For case of BC > BL
G
jBC
-jBL
Y

j(BC-BL)
Admittance Diagram
OR
G

j(BC-BL)
Y

## Slide 7
G
jBc
-jBL

Y
-j(BC-BL)
For case of BL > BC (Not in Textbook)
Admittance Diagram
OR
G

-j(BC-BL)
Y

## Slide 8
Total circuit current:
 is the phase between and
Voltage and Currents in Parallel Circuit

## Slide 9
Kirchhoff’s Current Law
The voltage, currents and admittances are related by Ohm’s Law:
Applying Circuit Laws to parallel RLC Circuit

## Slide 10
For case of BC > BL ( IC > IL)
IR
IC
I

Vs
IL
I
IR

VS
IC -
IL
OR
I leads VS by 
IC - IL
Phasor Diagram

## Slide 11
1. Admittance diagram and phasor diagram are similar and are related by VS since the admittance diagram when multiplied with the circuit voltage becomes the phasor diagram.
2. The phase of the circuit admittance and the phase of the circuit current is the same:
Relationship Between Admittance Diagram and Phasor Diagram

## Slide 12
4. Draw phasor & admittance diagrams if necessary
1. Calculate circuit admittance:
2. Calculate the circuit current:
3. Calculate
Analysis Procedure

## Slide 13
Example 17-2
Determine all the currents in the circuit. Draw the phasor diagram of the circuit. Assume 0o phase angle for the source voltage
j10
2.2
IR
IL
I
5 V
-j5
IC

## Slide 14
Phasor Diagram
IR
IC
I

VS
IL
IC -IL

## Slide 15
Apparent power (S) , is the total power that appears to be transferred from the source to the RLC circuit. It is the phasor sum of 2 components; the true power and reactive power.
Unit is volt-ampere (VA)
Reactive power (Q) is the cyclical power in the inductor and capacitor that shuttles between the source and the RLC circuit. It does no useful work. Unit is volt-ampere-reactive (VAR)
True power (P) is the power dissipated in the resistance in the form of heat. This is that power that does the actual useful work in the RLC circuit. Unit is Watt (W)
The 3 categories of power in RLC circuit are :
17-3 Power in RLC Circuit

## Slide 16
Power analysis of inductive RLC circuits is similar to that of RL circuits.
Most of the domestic and industrial loads are inductive in nature and hence has lagging power factor.
Power analysis of capacitive RLC circuits is similar to that of RC circuits.
An RLC circuit may be inductive or capactive, depending whether XL or XC is greater.
Power in RLC Circuit

## Slide 17
All 3 categories of power can be calculated using Ohm’s Law as follows :
  True Power (P) = I2 R = (VR)2 / R
  Apparent Power (S) = I2 ZT = (VS)2 / ZT = VS I
Reactive Power (Q) = I2 Xtot (for series RLC circuit)
where Xtot = magnitude of (XL – XC)
Reactive Power (Q) = (VS)2 / Xtot (for parallel RLC circuit)
where Xtot = 1 / Btot
and Btot = magnitude of (BC – BL)

## Slide 18
Impedance 
XL - XC
R

ZT
For the case of XL > XC

VS=I ZT
VR=IR
VL-VC =I(XL-XC)
Phasor  = Impedance  x I
Q=I2 (XL-XC) = VSIsin
P= I2R = VSIcos
S=I 2ZT=VSI
Power  = Phasor  x I

Power Triangle (Series RLC)

## Slide 19
Admittance 
BC - BL
G

Y
For the case of BC > BL

IT=VS Y
IR=VSG
IC-IL =VS (BC-BL)
Phasor  = Admittance  x VS
Q=VS2 (BC-BL) = VSITsin
P= VS2G = VSITVcos
S=VS2Y=VSIT
Power  = Phasor  x VS

Power Triangle (Parallel RLC)

## Slide 20
Power factor measures the conversion efficiency of the apparent power from the source into true power. It is defined as :
0  cos   1
Ideally, Q = 0, P = S so that cos  = 1
If i(t) lags vS (t), power factor is lagging.
If i(t) leads vS (t), power factor is leading.
Power Factor
Power Factor
Power Factor
Series RLC:
Parallel RLC:

## Slide 21
RLC circuit has lagging power factor if XL > XC
RLC circuit has leading power factor if XL < XC
For series RLC circuit :
RLC circuit has lagging power factor if BL > BC ( or XL< XC )
RLC circuit has leading power factor if BL < BC ( or XL > XC)
For parallel RLC circuit :

## Slide 22
Example 17-3
A 75  resistor, an inductor with 25  reactance and a capacitor with 60  reactance are connected in series to a 10 V ac source. Determine the power factor, the true power, the reactive power and the apparent power of the circuit.
Solution

## Slide 23
P = I2R = (121 x 10-3)2 x 75 = 1.1 W
Q = I2(Xtot)=(121x 10-3)2 x 35 = 0.51 VAR
S = I2Z = (121 x 10-3)2 x 82.8 = 1.21 VA
Power factor, cos  = cos 25o = 0.906 leading

## Slide 24
Power factor = cos  = cos 25o = 0.906 leading
Alternative solution
P = VSIcos = 10 x (121 x 10-3) x 0.906 = 1.1 W
Q = VSIsin  = 10 x (121 x 10-3) x sin 25o = 0.52 VAR
S = VSI = 10 x (121 x 10-3) = 1.21 VA
Or

## Slide 25
Summary
In a parallel RLC circuit:
Total current, i(t), leads the source voltage, e(t), by  if BC > BL.
Total current, i(t), lags the source voltage, e(t), by  if BC < BL.
 is directly proportional to the net susceptance of the circuit.
Admittance  and phasor  are similar.
 I =  Y = 
E is the reference phasor

## Slide 26
Summary
Power in RLC Circuit:
Power analysis of inductive RLC circuits is similar to that of RL or RC circuits depending on whether the circuit is inductive or capacitive.
Most of the domestic and industrial loads are inductive in nature and hence has lagging power factor.

## Slide 27
End of Chapter 17